## Slide 1
Module 2A: Woody biomass resources
2.1: Recap: What is woody biomass
2.2: Use and benefits of woody biomass
2.3: Sources of bioenergy biomass
2.4: Wood resources
2.5: Study of wood energy resources in Vermont
2.6: Role of woody biomass in the Northern Forest region
2.7: Harvesting, transporting & storage of woody biomass
2.8: Northern Forest recommendations for biomass use
2.9: Future of woody biomass
MEC 3040: Bioenergy

## Slide 2
2.1: What is woody biomass?

## Slide 3
What is woody biomass?
Wood bioenergy: energy created by direct or indirect conversion of biomass from trees or woody shrubs.
Dahiya (2015)
Plants use woody biomass to create structure.
Created when photosynthesis provides the energy to create woody polymers from water & carbon dioxide.
Composition?
  Water;
  Cellulose;
  Hemicellulose; and
  Lignin.
Methods of use:
Direct combustion;
  In the absence or presence of fossil fuels; or
A variety of thermal, chemical or biochemical conversions.
The path to carbon neutrality is theoretically direct as carbon released by use of woody biomass can be used to grow young trees or shrubs.

## Slide 4
Wood energy content
Dry wood is heated in an oven until the mass stops dropping & all moisture is removed.
Typical dry-sample values for Northeastern woods (GHV-DS) |  |  | 
 | Average (Btu/dry lb) | Low (Btu/dry lb) | High (Btu/dry lb)
hardwoods |  |  | 
white ash |  | 8246 | 8920
white birch |  | 8019 | 8650
elm |  | 8171 | 8810
hickory |  | 8039 | 8670
maple |  | 7995 | 8580
Red oak |  | 8037 | 8690
white oak |  | 8169 | 8810
poplar |  | 8311 | 8920
softwoods |  |  | 
white cedar |  | 7780 | 8400
eastern hemlock | 8885 |  | 
white pine |  | 8306 | 8900
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)

## Slide 5
Less energy dense
Wood, like all biomass, is less energy dense than fossil fuels.
 | Average (Btu/dry lb)
maple | 8,350
spruce | 8,720
corn | 8,120
fuel oil | 19,590
natural gas | 22,080
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)

## Slide 6
Moisture lowers energy content
In practice, wood biomass is not delivered or used in bone-dry condition. We can calculate the energy content of wet wood using a simple equation.
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
GVH-AF = (GVH-DS) (1 – (MC/100))
energy content of wet wood
energy content of bone-dry wood
moisture
content
(%)
For example, calculate the energy content of a wood with 40% moisture and a dry heating value of 8,500 Btu/pound.
GVH-AF = (8,500 Btu/lb) (1 – (40/100)) = (8,500 Btu/lb) (1 – 0.4)
= (8,500 Btu/lb) (0.6) = 5,100 Btu/lb

## Slide 7
Effect of moisture
50% moisture content reduces wood energy values by half.
40% moisture content is common.
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
Moisture content (%) | GHV-AF (Btu/lb)
Oven-dry | 8500
25% | 6375
30% | 5950
35% | 5525
40% | 5100
45% | 4675
50% | 4250
55% | 3825
60% | 3400

## Slide 8
What is a cord?
One cord of split firewood (chunk wood) is a well-stacked pile that is:
4 feet wide;
4 feet high; and
8 feet long.
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)