## Slide 1
Module 2B: Perennial grass biomass resources
2.10: Grass is an herbaceous perennial biomass feedstock
2.11: Grass biomass feedstock considerations & species
2.12: Environmental impact of grass biomass
MEC 3040: Bioenergy

## Slide 2
2.12: Environmental impact of grass biomass

## Slide 3
Environmental impacts (1)
Dahiya (2015); https://www.21stcentech.com/energy-in-the-21st-century-part-7-from-biomass-to-biofuels/
The environmental impacts of using grass biomass can be both positive and negative.
Greenhouse gas emissions (GHG) Grass biomass production has the potential to be carbon-neutral. Neutrality is most likely for:
perennial grasses needing the lowest inputs of energy and nutrients to produce;
used by direct combustion.
As the root system of grass stands develop carbon can be net sequestered.
Energy conversion efficiency as measured by the energy-out : energy-in ratio is high in comparison to other forms of bio-energy.
Direct conversion is the most energy efficient use of grass biomass.
Other conversions require larger energy inputs.
Bioenergy | EO:EI
Grass pellets | 14:1
Biodiesel | 3:1
Corn ethanol | 1.2:1
Grass ethanol | 4:1

## Slide 4
Comparative EROEI values
https://www.21stcentech.com/energy-in-the-21st-century-part-7-from-biomass-to-biofuels/
These values are from 2006 and may have changed a bit, but are useful for relative comparisons.
gufl/technology | EROEI
hydrogen | 0.5:1
corn ethanol | 1.2:1
oil sands | 2:1
corn biodiesel | 3:1
geothermal | 3:1
switchgrass ethanol | 4:1
solar thermal | 4:1
nuclear | 5:1
sugar cane ethanol | 8.3 – 10.2:1
solar PV | 9:1
coal | 10L1
natural gas | 10:1
hydropower | 12:1
windpower | 19:1
conventional oil | 25:1 but dropping

## Slide 5
Environmental impacts (2)
Dahiya (2015)
Protection of soil & water resources Perennial grasses are an excellent soil covering and prevent erosion while allowing infiltration of water.
Growth of perennial grasses absorbs nutrients and prevents nutrient runoff.
Establishment of stands may require minimal use of herbicides but they become unnecessary once grass is established.
Pesticides aren’t generally needed.
Wildlife nesting will occur in most stands of grass as long as harvest is delayed during nesting season.
In the Northeast, a delay until 1 August allows bobolinks to nest and fledge.
Use of marginal land perennial energy grasses can be grown on marginal soils not used for production of human or animal food.
Air emissions of NOx and SOx are higher with perennial energy grasses than with wood biomass so care must be taken in growth and harvesting and in choosing appropriate combustion equipment.
Invasive plants are a legitimate and sometimes serious concern since some energy grass species are invasives.