## Slide 1
Module 3B: Wood pellet heating
3.8: Wood pellets & current use
3.9: Two wood pellet heat case studies
3.10: Bulk delivery
3.11: Pellet stoves
3.12: Pellet boilers
3.13: Air emissions, permitting & ash
3.14: Economics of wood pellet heating
3.15: Recent wood pellet projects
MEC 3040: Bioenergy

## Slide 2
3.11: Pellet stoves vs boilers

## Slide 3
Pellet stoves vs. boilers
Wood pellet heating: a reference on wood pellet fuels & technology for small commercial & institutional systems
Stoves are designed to provide heat for residential buildings.
Generally, pellets are loaded by hand.
Boilers are designed to provide heat for larger buildings.
Fed from pellet silos; &
More automated and controlled.

## Slide 4
Pellet stove considerations
energy.gov/energysaver/wood-and-pellet-heating
Proper sizing is critical to ensure good stove performance.
Oversized stoves will be run at low temperatures, causing air emissions.
Undersized stoves won’t provide sufficient heat.
Rule of thumb?
2,000 SF home can be heated with a stove rated at 60,000 Btu
1,300 SF home can be heated with a stove rated at 42,000 Btu
Some municipalities restrict use of wood burning because of concerns about air emissions, so check before planning on using wood.
Today, EPA certification helps consumers lower air emissions.
Wood pellets are the cleanest burning wood fuel.
Location of pellet stoves influences how efficiently they heat homes.
Place the stove in the room used most often.
Use fans or blowers to move warm air to other areas.

## Slide 5
Pellet stoves are efficient
energy.gov/energysaver/wood-and-pellet-heating
Pellet stoves have very high combustion and heating efficiencies.
EPA certified stoves are in the 70 – 83% range.
Heating capacities are between 8,000 and 90,000 Btu per hour.
The cost of pellet stoves is $1,700 – 3000.
Installation is less expensive when the stove can be vented directly out of the room without a chimney or flue.
Wood pellet appliances are available as:
Freestanding stoves; or
Fireplace inserts.
Most are fed via a pellet hopper that stores 35 – 130 pounds of pellets.
Refilled about once per day.
Most are fed via a timer but several have thermostats that govern feed rate.
Maintenance:
Weekly cleaning;
100 kWh / month to run fans, controls & pellet feeders

## Slide 6
Fireplace inserts
energy.gov/energysaver/wood-and-pellet-heating
High-efficiency fireplace inserts function like stoves, but fit into the masonry or hearth of a fireplace.
For most efficient heating, installation of fireplace inserts is critical.
The insert must be as air-tight as possible; &
Approved insulation must be used to fill any gaps.
The chimney should be cleaned regularly