## Slide 1
Module 3C: Grass biomass heating
3.16: Grass biomass densification and combustion
3.17: Vermont study of energy grass densification &
combustion
3.18: Conversion of grass to liquid biofuels
3.19: Economic considerations for grass biomass
MEC 3040: Bioenergy

## Slide 2
3.16: Grass biomass densification & combustion

## Slide 3
Types of grass biomass conversion
Dahiya (2015)
Direct combustion with or without co-fire
Simplest with lowest cost
Does not require huge supply or high-capital processing
Synthetic fuel production via thermal or biochemical conversion
Requires very large supplies of biomass feedstock
And capital intensive processing plants
Most feasible in the Mid-West and South

## Slide 4
Solid fuel for combustion
Dahiya (2015)
Direct combustion is the most energy efficient use of grass as a fuel.
Grass is generally harvested at 10 – 12% moisture content as long hay or chopped grass.
Harvested dry grass can be burned with or without additional densification:
Whole bales;
Briquettes or cubes; or
Pellets
Densification:
Increase production costs; but
Decreases storage costs of the finished fuel product.
Increasing processing / production costs

## Slide 5
Models for grass energy combustion
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)
There are four models for combusting grasses for energy:
Closed loop, no processing (aka whole bale burning)
  Works for high thermal load;
  Campuses with district heating, hospitals, office complexes, large facilities.
2. Small scale on-farm processing uses a small stationary or mobile pelletizer
or densifier.
  Used on-farm or sold to local users.
3. Regional processing at a central processing plant using biomass grown in the surrounding area.
  Densified fuel would be delivered to local & regional commercial users.
  Users would have to be directed to appropriate furnaces / boilers.
4. Consumer pellet market served by a central pelletizing plant fed by local and regional biomass producers.
  Goal: producing standardized pellets.
  Users would have to be directed to appropriate furnaces / boilers.
 most challenging
 Hard to compete with wood unless demand increases.
 Easiest to implement with haying equipment

## Slide 6
Whole bale burners
Dahiya (2015)
Whole bale burners are fairly common in Europe, particularly Scandinavia.
Plants are large (district or region);
  150 – 1,000 kW = 0.5 – 3.5 MM Btu / hour
Storage costs for bales are higher;
Boilers have moving grates to cope with clinkers; a
Automated ash handling systems;
Large thermal storage, usually water, to allow a constant burn rate.
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)

## Slide 7
Grass densification
Dahiya (2015)
Densification of grass involves a number of processing steps:
Hay bales are fed into a tub grinder that creates small lengths.
This material is fed to a grinder or hammer mill. Briquettes can be formed at this step.
Hammer milling must create particles of 3.5 mm or less.
Particles are passed through a cyclone to remove air.
Particles are pushed through a heated die where pressure and heat soften and crush the particles together into pellets.
Pellets are cooled and screened to remove fines.
densification | production cost ($/ton)
briquette | $130
cubes | $128
pellet | $173
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)