## Slide 1
Module 3C: Grass biomass heating
3.16: Grass biomass densification and combustion
3.17: Vermont study of energy grass densification &
combustion
3.18: Conversion of grass to liquid biofuels
3.19: Economic considerations for grass biomass
MEC 3040: Bioenergy

## Slide 2
3.19: Economic considerations for grass biomass

## Slide 3
Dahiya (2015)
The return on energy grasses isn’t high so keeping the costs of production down is essential.
Fortunately grasses require very few inputs once stands are established.
Costs of establishing stands?
From seed: $400 – 500/acre
From rhizomes: $1500 – 2000/acre
Switchgrass cost of production for five yield scenarios |  |  |  |  |  | 
Establishment cost ($/acre): $350 - 400 |  |  |  |  |  | 
Annual maintenance & harvest cost ($/acre): $170 - 270 |  |  |  |  |  | 
Scenario | 1 |  | 2 | 3 | 4 | 5
Biomass yield (tons/acre) |  |  |  |  |  | 
Establishment year | 0 |  | 0 | 1.5 | 1.5 | 1.5
Year 2 | 2.0 |  | 2.0 | 2.5 | 2.5 | 2.6
Years 3 - 10 | 4.0 |  | 5.0 | 4.0 | 5.0 | 6.0
Total yield (10 years) | 34 |  | 42 | 36 | 44 | 52
Average yield/year | 3.4 |  | 4.2 | 3.6 | 4.4 | 5.2
Annual average cost |  |  |  |  |  | 
$/acre | 261 | 261 |  | 261 | 261 | 286
$/ton | 77 | 62 |  | 73 | 59 | 55
N added & economics improved
Modeling economics of grass biomass

## Slide 4
How much land would be needed to grow enough biomass to heat a residence?
Land use for residential heating?
Economics of using biomass for residential heating, U Ill, Urbana-Champaign

## Slide 5
How much would it cost to heat a home with biomass vs. fossil fuels?
Annual cost for residential heating?
Economics of using biomass for residential heating, U Ill, Urbana-Champaign