## Slide 1
Module 3A: Cordwood and woodchip heating
3.1: EROEI – energy return on energy investment
3.2: Residential heating: a case for cord wood
3.3: Efficient cord wood heating systems
3.4: Buyer’s guide to wood chip energy
3.5: Wood chip heating systems
3.6: Economic analysis of wood chip systems
3.7: Operating and maintaining a wood chip system
MEC 3040: Bioenergy

## Slide 2
3.2: Residential heating: a case for cord wood

## Slide 3
Vermont residential heating (2012)
Vermont sustainable heating initiative (2012)
Statistics from the US Energy Information Agency (EIA) don’t include wood as a residential heating fuel.
VT residential heating fuel | 2012 (%) | 2019 (%)
fuel oil | 59 | 60
propane | 14 | 
natural gas | 12 | 20
electricity | 5 | 
other | 10 | 
wood |  | 14
Total | 100 | 94
have wood stove? | 16 | 
However, 16% of Vermont households have wood stoves
This is the highest per capital use of wood stoves in the US.
In Canada, 20% of households use some wood heat.
In 2008, the average Vermont household used 4.3 cords of wood.
https://www.eia.gov/state/print.php?sid=VT

## Slide 4
Residential heating trends in Canada
Canadian households have a long history of using wood for heating.
14% of all households; or
21% of single-family dwellings use wood for primary or supplemental heat.
6.5% of single-family dwellings use wood as the primary source of heat.
Residential wood heat: a non-commercial service in support of responsible home heating with wood (2016)
In 1982, those who used wood as their primary source of heat used central wood furnaces.
By 1991, only half of that group used central wood furnaces and the other half had shifted to wood stoves, fireplace inserts or space heaters.
And 95% of supplemental wood users used these non-central appliances.
Why?
Houses are more energy efficient and require less heat;
Air quality regulations required replacement of older systems; and
“Glass air wash” systems in stoves allowed users to view the fire.

## Slide 5
Residential heating attitudes in Canada
A 1983 study showed that most Canadian wood-heat users were very or somewhat satisfied with using wood even though this method of heating uses more personal time and effort.
97% of primary wood users
91% of supplemental wood users
Residential wood heat: a non-commercial service in support of responsible home heating with wood (2016)
A 1987 study in Ontario found that people who heated with wood connected to wood use on a personal & family level:
Family-centered activity;
Reflects personal and family values;
Reflects the desire for self-reliance.

## Slide 6
Comparing use & safety of wood fuels
Vermont sustainable heating initiative (2012)
Each form of wood energy has advantages and disadvantages:
Wood fuel | Scale of use
Cord wood | Residential & up
Wood chips | District & commercial
Wood pellets | Residential & up
System cost
> $4,000
> $1.2 million
> $1,400
Safety?
Chimney fires, combustible ash, creosote
Commercial code
Wood fuel
Cord wood
Wood chips
Wood pellets

## Slide 7
Can we increase use of wood heat?
Vermont sustainable heating initiative (2012)
BERC study of wood resources in Vermont concluded that the maximal additional amount of wood we could harvest sustainably would be 900,000 green tons per year.
Vermont’s population is about 620,000.
So additional wood per capita would provide:
  0.725 green tons of hardwood + 0.725 green tons of softwood.
Assuming that the wood’s moisture content is 50%, each Vermonter would get:
  0.36 cords of hardwood + 0.73 cords of softwood.
About a 1 cord increase on the average 4.3 cords/year use in Vermont.
Or 144,000 new users at the average of 4.3 cords/year rate.

## Slide 8
Cordwood conclusions?
Vermont sustainable heating initiative (2012)
If all Vermont homes were converted to cordwood heat, we would deforest Vermont again!
So, what should we do with our additional wood resources?
Convert fast growing softwoods into wood pellets.
Evaluate heating systems for efficiency and EROEI.
Install new systems with the greatest local benefit.
  Export of wood energy from Vermont should be the lowest priority.
  Transportation should be considered when deciding which projects to implement.
Large-scale biomass systems should be required to get a certificate of public good to ensure they are sustainable and worthy of the resource use.
  Any use of > 30,000 green tons per year.
Biomass stewardship is essential to long-term sustainability.

## Slide 9
Economic impacts?
Vermont sustainable heating initiative (2012)
Biomass electricity generation will not lower Vermont electric rates.
And it is an inefficient use of biomass.
Biomass heating could save Vermonters $200 million per year.
And that money would be transferred to local economies.
Pellet production can produce efficient biomass from marginal softwood.