## Slide 1
Module 3A: Cordwood and woodchip heating
3.1: EROEI – energy return on energy investment
3.2: Residential heating: a case for cord wood
3.3: Efficient cord wood heating systems
3.4: Buyer’s guide to wood chip energy
3.5: Wood chip heating systems
3.6: Economic analysis of wood chip systems
3.7: Operating and maintaining a wood chip system
MEC 3040: Bioenergy

## Slide 2
3.3: Efficient cord wood heating systems

## Slide 3
When is cordwood a good option?
Cordwood energy systems for community heating in Alaska: an overview, USDA (2009)
Cordwood systems are generally less expensive than woodchip or pellet systems and are good options when:
Heat, but not electricity, is sought;
The cordwood is produced locally; &
The space to be heated is relatively small, making chip or pellet systems to expensive.
Target heating load for cordwood systems?
100,000 – 900,000 Btu/hour
Replacing systems that require 2,500 – 30,000 gallons of oil per year

## Slide 4
More efficient cordwood systems?
Cordwood energy systems for community heating in Alaska: an overview, USDA (2009)
Cordwood heating systems, particularly small residential systems, are often inefficient and produce high levels of air emissions:
Fireplaces (really inefficient!);
Home heating stoves; &
Outdoor wood furnaces.
However, more efficient cordwood systems are available with these features:
Efficient combustion (> 70%);
Heating loads of 350,000 – 950,000 Btu/hour;
Refractory-lined combustion chambers;
Better use of fans; all leading to lower levels of particulate emissions.
Fed manually;
Also: larger water heat storage units with 1,500 – 4,400 gallon capacities.
Such systems generally need to be stoked (loaded with cordwood) several times a day.
Cost of a good cordwood system? <$100,000 for system that displaces 2,500 – 30,000 gallons of oil per year.

## Slide 5
Example: home cord wood gasifier
www.revisionheat.com/home-cord-wood-boilers/
Tarm offers the Austrian Fröling FHG wood boiler that uses wood gasification combustion technology for residential heating.
91% overall efficiency when combined with a 500 – 1000-gallon water storage tank
  Down-draft gasification is used for hot & fast combustion.
  Water stores the heat provided by intermittent but hot combustion at maximum efficiency.
  Thermal storage allows most homes to heat with one firing per day.
Clean double-burn with very little smoke and creosote
  Primary combustion produces wood gases; &
  Secondary burn adds oxygen & combusts the gases at 1800 - 2000°F.
Operating features:
  Smokeless addition of wood;
  Periodic ash removal

## Slide 6
Cord wood gasification case study
Old stone home uses modern heating technology, Radiant Living (2012)
NY stone home built in 1948.
3 levels
3,000 square feet
Original oil-fired hot air furnace was inefficient ($1,400/month for 55°F)
Renovations weatherized the building & added radiant floor heating.
Fröling FHG-L wood gasification boiler was chosen for primary heating.
  2 combustion chambers w/ final combustion temps of 1800 - 2000°F
  Microprocessor control via oxygen & temperature sensors
  Three pressurized 220-gallon thermal storage tanks set at 100°F
  A domestic hot water tank stores at 140°F
  Six zone radiant floor system
Backup heating system is an efficient propane-fired boiler.
Performance?
‘We only have to put in wood maybe twice a day on very cold days…then you put two pieces of paper in, and light it. It’s the easiest thing. We clean it out maybe once every two weeks.’

## Slide 7
Cord wood gasification case study
Old stone home uses modern heating technology, Radiant Living (2012)

## Slide 8
Cord wood gasification study
Old stone home uses modern heating technology, Radiant Living (2012)

## Slide 9
Examples from Alaska
Cordwood energy systems for community heating in Alaska: an overview, USDA (2009)
Examples of high-efficiency cordwood heating systems:
Tarm USA: boiler of 100,000 – 198,000 Btu/hour @ 80% efficient.
Tarm gasification boiler for home heating in Palmer, AK
GARN boiler heats seven homes & a laundromat in Dot Lake, AK
  900,000 Btu/hour
  Uses 4,400 gallons of water.
  Replaces 7,000 gallons of fuel oil per year.
  Very low emissions when compared to other wood systems by EPA.