## Slide 1
Module 3C: Grass biomass heating
3.16: Grass biomass densification and combustion
3.17: Vermont study of energy grass densification &
combustion
3.18: Conversion of grass to liquid biofuels
3.19: Economic considerations for grass biomass
MEC 3040: Bioenergy

## Slide 2
3.16: Grass biomass densification & combustion

## Slide 3
Types of grass biomass conversion
Dahiya (2015)
Direct combustion with or without co-fire
Simplest with lowest cost
Does not require huge supply or high-capital processing
Synthetic fuel production via thermal or biochemical conversion
Requires very large supplies of biomass feedstock
And capital intensive processing plants
Most feasible in the Mid-West and South

## Slide 4
Solid fuel for combustion
Dahiya (2015)
Direct combustion is the most energy efficient use of grass as a fuel.
Grass is generally harvested at 10 – 12% moisture content as long hay or chopped grass.
Harvested dry grass can be burned with or without additional densification:
Whole bales;
Briquettes or cubes; or
Pellets
Densification:
Increase production costs; but
Decreases storage costs of the finished fuel product.
Increasing processing / production costs

## Slide 5
Models for grass energy combustion
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)
There are four models for combusting grasses for energy:
Closed loop, no processing (aka whole bale burning)
  Works for high thermal load;
  Campuses with district heating, hospitals, office complexes, large facilities.
2. Small scale on-farm processing uses a small stationary or mobile pelletizer
or densifier.
  Used on-farm or sold to local users.
3. Regional processing at a central processing plant using biomass grown in the surrounding area.
  Densified fuel would be delivered to local & regional commercial users.
  Users would have to be directed to appropriate furnaces / boilers.
4. Consumer pellet market served by a central pelletizing plant fed by local and regional biomass producers.
  Goal: producing standardized pellets.
  Users would have to be directed to appropriate furnaces / boilers.
 most challenging
 Hard to compete with wood unless demand increases.
 Easiest to implement with haying equipment

## Slide 6
Whole bale burners
Dahiya (2015)
Whole bale burners are fairly common in Europe, particularly Scandinavia.
Plants are large (district or region);
  150 – 1,000 kW = 0.5 – 3.5 MM Btu / hour
Storage costs for bales are higher;
Boilers have moving grates to cope with clinkers; a
Automated ash handling systems;
Large thermal storage, usually water, to allow a constant burn rate.
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)

## Slide 7
Grass densification
Dahiya (2015)
Densification of grass involves a number of processing steps:
Hay bales are fed into a tub grinder that creates small lengths.
This material is fed to a grinder or hammer mill. Briquettes can be formed at this step.
Hammer milling must create particles of 3.5 mm or less.
Particles are passed through a cyclone to remove air.
Particles are pushed through a heated die where pressure and heat soften and crush the particles together into pellets.
Pellets are cooled and screened to remove fines.
densification | production cost ($/ton)
briquette | $130
cubes | $128
pellet | $173
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)

## Slide 8
3.17: Vermont study of energy grass densification & combustion

## Slide 9
Collaborative study of grass biofuel
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
The Vermont Grass Energy Partnership conducted a study to learn more about:
  Growing & harvesting perennial grasses;
  Pre-processing & densifying the grasses;
  Combustion of densified grass, and grass-wood blends; &
  Air emissions from the combustion.
Three perennial hay grasses were studied:
Switchgrass (Panicum vigratum) A promising biomass grass not typically grown in Vermont
Reed Canarygrass (Phalaris arundinacea) Common in Vermont & adapted to many conditions including wet, marginal soil
Mulch hay Hay that is too poor in quality to serve as livestock feed

## Slide 10
Harvesting
On-farm production of biomass grass pellets, Penn State Extension, (2014)
Some harvest energy grass in the fall and some in the spring.
In the spring, the crop is dry, and the new growth can be fertilized as it begins to come up through the fresh stubble.
Leaving the grass in the field over the winter probably allows nutrients to be reabsorbed by the roots and may lower ash content.
If mowed in the fall, the grass can be left on the ground over the winter to allow the minerals to leach back into the soil.
After baling, moisture content is about 6-8%. But optimal pelletizing requires 12 – 15% moisture. Leaving bales outdoors allows moisture to seep back in.
Store bales on pallets and cover with a tarp to prevent too much moisture.

## Slide 11
Processing & densification
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
The pelletizing process:
40-lb bales were chopped by study personnel.
The chopped hay was reground, blended, dried & pelletized by the Vermont Wood Pellet Company in North Clarendon, VT
Chemical and mineral testing was performed by Twin Ports Testing, Inc.
pellets | 100% | 25%* | 12%* | 6%*
switchgrass | ✔ | ✔ | ✔ | ✔
Reed canarygrass | ✔ | ✔ | ✔ | ✔
mulch hay | ✔ | ✔ | ✔ | ✔
* % grass in wood blend
The 100% grass pellets had less structural integrity than wood pellets or wood/grass blends. This is probably due to the lower lignin content of grass.

## Slide 12
Processing & densification
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)

## Slide 13
Processing & densification
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)

## Slide 14
Processing & densification
On-farm production of biomass grass pellets, Penn State Extension, (2014)
bale at 12-14% moisture
bale buster = coarse chopping
¼” screen hammer mill
pellet mill
10” warm-up
pellet production starts
coarse chopped
1/4” chopped
> 80°C, lignin melts & gets tacky
cooling
bagging
While wood has 22 – 24% lignin, switchgrass has less, 12 – 15%.
But grass still forms pellets without added binders.
Ending the pellet run with low-lignin feedstock like soymeal will purge the die & prevent build up of hard lignins.

## Slide 15
Ash content
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
The grass pellets had dramatically higher ash content (4.3 – 6.7%) than premium grade wood pellets.
100% grass pellets would be classified as utility- or industrial-grade wood pellets.
100% reed canarygrass pellets had ash contents to high for classification.
Switchgrass had the lowest ash content (4.3%) of all the grasses.
The grass-wood blend pellets had lower ash content than 100% grass pellets.

## Slide 16
Energy content, clinkers & emissions
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
The energy content of grass pellets was quite comparable to that of wood pellets.
Energy content | 
wood | 100%
switchgrass | 102%
Reed canarygrass | 90%
mulch hay | 92%
However, fused minerals (aka clinkers) formed during test combustion of the grass pellets.
Grasses had higher concentrations of N, S and Cl than wood, creating more potential emissions:
NOx
SOx
Corrosive chlorine-containing gases.
Stack emission tests confirmed higher Nox & ash (particulate) emissions.

## Slide 17
‘Real world’ combustion tests
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
The longer ‘real world’ combustion tests lasted three hours and boiler performance was monitored.
All grass pellets could be combusted.
Mulch hay combustion was a challenge.
Even switchgrass pellets produced clinkers that blocked new fuel feed and air flow in the combustion chamber.
The best combustion was achieved for grass/wood blends with the most wood.

## Slide 18
Conclusions?
Technical assessment of grass pellets as boiler fuel in Vermont, BERC (2011)
Hay and energy grasses can be grown productively in Vermont.
Hay and energy grasses can be densified into pellets, pucks or briquettes.
  Blending with wood increases the integrity of the densified forms.
Grass pellets should not be used in residential pellet stoves designed for wood.
The VGEP believes that larger boilers designed for alternative fuels will be able to handle grass biofuels… and the search is on!
Next steps:
Blend wood and grass to allow use in current stoves & boilers.
2. Find appliances capable of burning 100% grass and build a market for this
biofuel.

## Slide 19
Cost & markets
On-farm production of biomass grass pellets, Penn State Extension, (2014)
A 2014 study of growing, harvesting and pelletizing switchgrass at Wood Crest Farm in PA found that the barebones cost of producing and pelletizing switchgrass was $89 per ton without including the cost of labor, equipment purchase or land rental.
While the intended market for switchgrass is energy a grower should be aware of alternate markets. In PA, a switchgrass grower has found these markets:
Ground switchgrass is used as a landscaping mulch and sold to landscapers or hardware and gardening stores;
Animal bedding for cows and chickens; &
Absorbent and erosion control.

## Slide 20
Grass pellet burning appliances
Grass Energy in Vermont and the Northeast, Wilson Engineering for VSJF (2014)
Grass pellets burn best in appliances with:
Adjustable fuel feed rate & air-to-fuel ratios;
Automatic &/or mechanical method of ash removal; &
Ample ash storage bins, easily emptied.
Cornell has identified the best stoves for grass pellets:
Quadrafire S
Europa 75
Harman P43 S
Skanden (Reka), B
LEI BB100, B
Cornell has identified the best boilers for grass pellets:
LEI multifuel boilers
New Horizon’s modified Futura MultiBio Boiler

## Slide 21
Case study: VT Farmers Food Center
Vermontbioenergy.com/tag/grass-biofuel
Vermont Farmers Food Center occupies a renovated mill building in Rutland, VT. This vibrant new 4,200 SF agricultural hub uses a heating system that can be fueled by agriculture as well.
With the help of Chris Callahan, an agricultural engineer at UVM Extension, the center installed a multi-fuel boiler that can be fueled with:
Wood pellets;
Grass pellets or pucks; and
Other densified biomass.
While this multi-purpose boiler was more expensive than similar boilers with more limited fuel capacity, payback is expected to be 2-8 years, depending on the price of alternative fuels like propane.
video

## Slide 22
Case study: Meach Cove Farms
Evoworldusa.com/helping-an-organic-farm-test-biomass-heating/
Meach Cove Farms is a 1,000-acre organic farm in Shelburne, VT that grows soybeans, rye, wheat, corn hay and wine-grapes and has a sizeable wood lot.
Have used wood pellet boilers.
Installed the EvoWorld 350c dual wood chip & pellet boiler manufactured in Troy, NY.
The company is eager to help adapt the system to grass pellets & pucks.
video
Hosts grass energy trials funded by a Conservation Innovation Grant from the USDA’s Natural Resource Conservation Service (2011).

## Slide 23
3.18: Conversion of grass to liquid biofuels

## Slide 24
Liquid fuels
Dahiya (2015)
Grass can be converted into liquid fuels like ethanol, methanol and alkanes.
However, conversion is much more difficult for grasses than for high sugar or starch feedstock materials like sugarcane or grains because of the sugars in grass are bound and cross-linked into complex polymers that are difficult to break down: cellulose, hemicellulose and lignins.
Enzymes from yeast, fungi or bacteria are used to digest the highly fibrous material and break out the sugars for fermentation.

## Slide 25
Liquid conversion steps
Dahiya (2015); DOE (2010)
Feedstock is pre-treated with heat and acid or base to break down fibrous cell walls.
Enzymes or catalysts are used to hydrolyze (or break down) cellulose and hemicellulose into simple sugars like glucose and xylose.
Microbes are added in anaerobic conditions to convert the sugars to alcohols (like ethanol). - Alternatively, chemical catalysts rather than microbes can be used to create other products.
Products are recovered by separation from water, solvents, residual & feedstock materials.
Distribution of product that may, or may not, be blended with other liquid fuels.
The lignin that remains after conversion is burned to create heat & power for the conversion process.

## Slide 26
Scale of conversion plants?
Dahiya (2015); DOE (2010)
The scale of conversion plants varies with the complexity of the process.
There are mobile densifiers that can produce grass briquettes or pellets.
Tractor PTO driven;
Or driven by on-trailer engines
However, cellulosic ethanol plants are complex plants that are built on a large scale to take advantage of economies of scale.
All biomass plants have to cope with the variation inherent in grass biomass feedstock.
Smaller and simpler processors are more likely to adapt…
… than large and complex plants that will have strict standards for feedstock material.

## Slide 27
3.19: Economic considerations for grass biomass

## Slide 28
Dahiya (2015)
The return on energy grasses isn’t high so keeping the costs of production down is essential.
Fortunately grasses require very few inputs once stands are established.
Costs of establishing stands?
From seed: $400 – 500/acre
From rhizomes: $1500 – 2000/acre
Switchgrass cost of production for five yield scenarios |  |  |  |  |  | 
Establishment cost ($/acre): $350 - 400 |  |  |  |  |  | 
Annual maintenance & harvest cost ($/acre): $170 - 270 |  |  |  |  |  | 
Scenario | 1 |  | 2 | 3 | 4 | 5
Biomass yield (tons/acre) |  |  |  |  |  | 
Establishment year | 0 |  | 0 | 1.5 | 1.5 | 1.5
Year 2 | 2.0 |  | 2.0 | 2.5 | 2.5 | 2.6
Years 3 - 10 | 4.0 |  | 5.0 | 4.0 | 5.0 | 6.0
Total yield (10 years) | 34 |  | 42 | 36 | 44 | 52
Average yield/year | 3.4 |  | 4.2 | 3.6 | 4.4 | 5.2
Annual average cost |  |  |  |  |  | 
$/acre | 261 | 261 |  | 261 | 261 | 286
$/ton | 77 | 62 |  | 73 | 59 | 55
N added & economics improved
Modeling economics of grass biomass

## Slide 29
How much land would be needed to grow enough biomass to heat a residence?
Land use for residential heating?
Economics of using biomass for residential heating, U Ill, Urbana-Champaign

## Slide 30
How much would it cost to heat a home with biomass vs. fossil fuels?
Annual cost for residential heating?
Economics of using biomass for residential heating, U Ill, Urbana-Champaign