## Slide 1
Module 6: Biodiesel basics to sustainability
6.1: Brief overview of biodiesel
6.2: What’s oil anyway?
6.3: The viscosity problem
6.4: Biodiesel statistics
6.5: Transesterification basics
6.6: ‘Renewable diesel’ and ‘bio-jet’
6.7: Biodiesel sustainability?
MEC 3040: Bioenergy

## Slide 2
6.5: Transesterification basics

## Slide 3
TAG to fatty acid methyl ester
Pahl (2005)
Wikipedia images
Vegetable oils are triacylglycerols: three fatty acids attached to a 3-carbon glycerol backbone by acyl bonds.
FAME (fatty acid methyl ester): fatty acids ‘cut’ from TAGs and capped with a methyl ester group
TAG
FAME x3
transesterification

## Slide 4
Overview: biodiesel process
Pahl (2005)
triacylglycerol
glycerol + 3 fatty acids
reaction of fatty acids with alcohols
‘cracking’ via a
hydroxide catalyst
fatty acid alkyl esters
Phase separation:
oil & water separate
biodiesel layer on top (2/3 volume) over
glycerol-rich bottom phase (1/3 volume)
transesterification
Acids are sometimes added to prevent the formation of soap.

## Slide 5
Translation?
Pahl (2005)
Cracking: A base (a hydroxide) is used to cut the fatty acid chains from the glycerol backbone of triacylglycerols.
Sodium hydroxide (lye or caustic soda) is less expensive than potassium hydroxide.
In petroleum refining, cracking refers to cutting huge oil molecules into smaller and shorter, and thus less viscous, pieces.
Alkyl esters: Molecules created by capping free fatty acid chains with an ester group coming from an alcohol.
Ester (or acyl) linkages connect the FA and the ester.
Methyl ester have a one-carbon ester group.
Ethyl esters have a two-carbon ester group.
O
||
-- O – C --
Free fatty acids:
Fatty acid chains broken from the triacylglycerol by repeated & prolonged heating. FFA are carboxylic acids and lower the pH of oil used or stored oils.