## Slide 1
Module 8: Biodiesel uses and future
8.1: Comparing biodiesel to petro-diesel
8.2: Running diesel engines on biodiesel
8.3: Heating with biodiesel
8.4: Life-cycle analysis: biodiesel EROI
8.5: Future: Europe’s lead, promise and problems
MEC 3040: Bioenergy

## Slide 2
8.1: Comparing biodiesel to petro-diesel

## Slide 3
Energy content?
Dahiya (2015)
Biodiesel energy content is 10-12% lower than that of petro-diesel.
Fuel | Btu per gallon
Petro-diesel | 135,000
Biodiesel | 121,000
Why? Biodiesel contains oxygen which is nearly absent in petro-diesel.
Oxygen increases combustion efficiency.
Oxygen reduces energy content (does not combust).
Result? Biodiesel has a 5% lower torque value.

## Slide 4
Comparing fuel specifications
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Property | ASTM method | biodiesel limits | petro- limits | units
Flashpoint | D93 | 100.0 min | 52.0 | °C
Water & sediment | D1796 | 0.050 max |  | Vol (%)
Carbon residue | D524 | 0.050 max | 0.35 max | Wt (%)
Sulfated ash | D874 | 0.020 max | 0.010 max | Wt (%)
Kinematic viscosity @ 40°C | D445 | 1.9 – 6.5 | 1.9 – 4.1 | centistokes
sulfur | D2622 | 0.050 max | 0.050 max | Wt (%)
cetane | D613 | 40 min | 40 min | 
Cloud point | D2500 | by customer | By customer | °C
Copper strip corrosion | D130 | No. 3b max |  | 
Acid number | D664 | 0.80 max |  | mg KOH/g
Free glycerin | GC | 0.020 max |  | Wt (%)
Total glycerin | GC | 0.240 max |  | Wt (%)
ASTM testing methods and limits

## Slide 5
Flash points
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Flashpoint (°C) | Flashpoint (°F)
Petro-diesel | 52 | 126
Biodiesels |  | 
Soy methyl ester | 167 | 333
Canola methyl ester | 163 | 326
Lard methyl ester | 128 | 263
Edible tallow methy ester | 173 | 344
Inedible tallow methyl ester | 136 | 276
Yellow grease methyl ester | 147 - 160 | 297 - 320
ASTM D 93

## Slide 6
Heat of combustion
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Btu/lb
Petro-diesel | 18,600
Biodiesels | 
Soy methyl ester | 17,153
Canola methyl ester | 17,241
Lard methyl ester | 17,165
Edible tallow methy ester | 17,144
Inedible tallow methyl ester | 17,061
Yellow grease methyl ester | 17,154- 17,215
ASTM D240: determined using a bomb calorimeter.

## Slide 7
Kinematic viscosity
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Viscosity (centistokes)
2D Petro-diesel | 2.45
Biodiesels | 
Soy methyl ester | 4.546
Canola methyl ester | 4.63
Lard methyl ester | 4.85
Edible tallow methy ester | 4.908
Inedible tallow methyl ester | 4.93
Yellow grease methyl ester | 4.66 – 5.62
ASTM D 445

## Slide 8
Ash formation
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Ash (%)
2D Petro-diesel | 0.01%
Biodiesels | 
Soy methyl ester | 0
Canola methyl ester | 0.003
Lard methyl ester | 0
Edible tallow methy ester | 0.001
Inedible tallow methyl ester | 0
Yellow grease methyl ester | 0.01 – 0.04
ASTM D 482

## Slide 9
Ramsbottom carbon residue
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Carbon residue (%)
2D Petro-diesel | 0.35%
Biodiesels | 
Soy methyl ester | 0.01
Canola methyl ester | 0.04
Lard methyl ester | 0.04
Edible tallow methy ester | N/A
Inedible tallow methyl ester | 0.08
Yellow grease methyl ester | 0.04- 0.05
ASTM D 524: propensity to form coke, or carbon deposits

## Slide 10
Cetane number
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Cetane number
2D Petro-diesel | 47
Biodiesels | 
Soy methyl ester | 59
Canola methyl ester | 53.9
Lard methyl ester | N/A
Edible tallow methy ester | 64.8
Inedible tallow methyl ester | 54.3
Yellow grease methyl ester | 52.2 – 53.2
ASTM D 613: a measure of the fuel’s ignition delay; higher is better

## Slide 11
Cloud point
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | Cloud point (°C) | Cloud point (°F)
2D Petro-diesel | -18 | 0
Biodiesels |  | 
Soy methyl ester | 2 | 36
Canola methyl ester | -3 | 27
Lard methyl ester | 14 | 57
Edible tallow methy ester | 20 | 68
Inedible tallow methyl ester | 23 | 73
Yellow grease methyl ester | 8 - 42 | 46 - 108
ASTM D 2500: temperature at which wax crystals begin to form

## Slide 12
Low-temperature flow test
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | CFPP (°C) | CFPP(°F)
2D Petro-diesel | -18 | -4
Biodiesels |  | 
Soy methyl ester | -2 | 28
Canola methyl ester | -4 | 24
Lard methyl ester | 11 | 52
Edible tallow methy ester | 14 | 58
Inedible tallow methyl ester | 10 | 50
Yellow grease methyl ester | 1 - 11 | 34 - 52
ASTM D 4539: temperature at which wax crystals will plug a fuel filter

## Slide 13
Lubricity
Kinast, Production of biodiesels from multiple feedstocks and properties of biodiesels and blends (NREL)
Fuel | g
2D Petro-diesel | 3600
Biodiesels | 
Soy methyl ester | 6050
Canola methyl ester | >7000
Lard methyl ester | >7000
Edible tallow methy ester | >7000
Inedible tallow methyl ester | >7000
Yellow grease methyl ester | >7000
ASTM D 6078: indicates the lubricating property; weight that floats on film

## Slide 14
Emissions
Dahiya (2015)
Biodiesel has no lead, and very low sulfur and aromatics content.
As a result, emissions are less hazardous. Fewer:
  Unburned hydrocarbons;
  Carbon monoxide; and
  Particulates.
However, NOX emissions are higher because there is nitrogen in plant-derived oils.
Carbon cycling results in an overall loss of 78% in carbon dioxide emissions.

## Slide 15
Biodegradability & toxicity
Dahiya (2015)
Biodiesel (B100) is biodegradable:
As biodegradable as sugar.
A spill of biodiesel would be biodegraded in 3-4 weeks.
Biodiesel (B100) is non-toxic:
Ten times less toxic than table salt.
Petro-diesel and even its fumes are toxic to human health.

## Slide 16
Safety: transportation & storage
Dahiya (2015)
The flashpoint (temperature at which fumes ignite) for biodiesel is higher (260°F) than that of petro-diesel (125°F).
As the percent of biodiesel in blends increases, so does the flashpoint of the blend.
Biodiesel can be shipped by UPS or FedEx.
Biodiesel can be stored using the same infrastructure used to store petro-diesel.
In warm conditions, small amounts of biocides should be added to prevent growth of microbes in biodiesel stored for prolonged periods of time.
Generally, biodiesel should not be stored for more than 6 months.