## Slide 1
Module 8: Biodiesel uses and future
8.1: Comparing biodiesel to petro-diesel
8.2: Running diesel engines on biodiesel
8.3: Heating with biodiesel
8.4: Life-cycle analysis: biodiesel EROI
8.5: Future: Europe’s lead, promise and problems
MEC 3040: Bioenergy

## Slide 2
8.2: The diesel engine running on biodiesel

## Slide 3
Diesel engines:
4, 6, or 8 cylinders with pistons connected to a crankshaft.
Up-down motion of the pistons turns the crankshaft.
The crankshaft turns the driveshaft.
The driveshaft turns the vehicles wheels.
Diesel engines
Pahl (2005)
Compression ignition:
While gasoline engines use spark-ignition systems…
... Diesel engines use extremely high temperature and pressure (1,000°F) at the top of the cylinder to ignite the fuel in the cylinder spontaneously.
  No spark is required.
The engine has to be more ruggedly built to create the high rates of compression needed to ignite the fuel. Diesel engines cost more.
  Diesel engines can run 200-300,000 miles before overhaul.
Diesel engines use a glow plug:
… to preheat the combustion chamber and help the fuel ignite.
fuel tank
direct injection (TDI)
[quieter & cleaner]
diesel engine

## Slide 4
Diesel engines are notorious for being hard to start in cold weather. Why?
Petro-diesel ‘clouds’ at 20°F: crystals of paraffin wax begin to form.
The crystals clog fuel filters and stall the engine.
At colder temperatures petro-diesel fuels reach a pour-point at which it does not pour and won’t travel through fuel lines.
Finally, at 15°F petro-diesel gels to the consistency of petroleum jelly.
Cold-weather issues?
Pahl (2005)
Biodiesel also clouds and gels, but at higher temperatures, making it even more difficult to use as an engine fuel.
The performance of biodiesel depends on the fuel source.
Winterizing agents are added to petro-diesel during the winter in colder regions.
These agents can also be used with biodiesel.
Blends? Lower blends (B5 or B20) are better for use in the winter while higher blends (B50 – B100) can be used in warmer weather.

## Slide 5
Biodiesel is more polar than petro-diesel so acts as a very effective solvent.
Solvents, seals, sludge & slime
Pahl (2005)
Rubber seals, hoses and gaskets in engines built before 1994 can be degraded (solubilized) by high biodiesel blends, particularly B100.
Rubber should be replaced by a less polar material like Viton.
The sludge that typically coats old fuel tanks and lines is dissolved and cleaned off by biodiesel.
That sounds good…
... But the moving sludge can clog fuel filters and cause other malfunctions.
Sludge problems are temporary.
Greenish black slime can form if bacteria grow in biodiesel in engines and lines during warm weather.
Biocides can eliminate this problem.

## Slide 6
Now that biodiesel is more common, most US diesel engine warranties are not voided if blends of B20 or lower are used as fuel.
Engine warranties
Pahl (2005)
Note that for fuel-related problems the engine maker is not liable, rather the fuel producer is responsible.
So, fuel should meet ASTM standards.
The National Biodiesel Board has formed the National Biodiesel Accreditation Commission (NBAC) to support biodiesel fuel quality standards.
Look for the “Certified Biodiesel Marketer” seal of approval.

## Slide 7
A variety of types of additives are available to prevent problems or enhance performance in winter conditions.
Additives
Pahl (2005); Dahiya (2015)
Cold-flow improvers lower the temperature at which fuel can be used.
Pour point reducers (aka antigels) lower the temperature at which fuel gels or becomes semi-solid.
Cold-filter plug point reducers lower the temperature at which wax crystals form and plug fuel filters.
What if it biodiesel gels?
Sometimes addition of kerosene (~ 5 gallons to an oil tank) will break up the wax crystals and liquefy the fuel in place.
Heat tape is not recommended.
Dispersants / detergents keep ‘stuff’ in solution so that it does not settle to the bottom of the tank and clog filters or lines. When first used, detergents may clean sludge out of lines and filters will clog until the system is clean.
Antioxidants / metal deactivators slow or prevent fuel degradation.
Biocides prevent growth of microbes in the biodiesel.
They must be oil-soluble and caution is needed as they are toxins.

## Slide 8
In the US, 70% of petroleum fuels are consumed in transportation.
Use of diesel engines?
Pahl (2005)
Passenger cars:
  1% diesel in the US
  36% diesel in Europe
Fleet vehicles: much more use of diesel in this sector
Biodiesel is used in more than 500 fleets in the US, including:
  Postal Service;
  Military (all four branches);
  School districts and municipal fleets.
Mass transit: 90% of vehicles are diesel
  Many city bus fleets are using biodiesel.
  School buses are also increasingly switching to biodiesel.
Trucks and heavy equipment
  Farm equipment (an early adopter)
  Boats
  Trains

## Slide 9
By 2030:
24 European cities will ban diesel vehicles
13 “ will ban all internal combustion vehicles
Coming diesel bans
https://e360.yale.edu/digest/diesel-vehicles-face-a-grim-future-in-europes-cities
Why?
  Air pollution
  Climate change
  The Volkswagen scandal of faked emissions testing