## Slide 1
Module 8: Biodiesel uses and future
8.1: Comparing biodiesel to petro-diesel
8.2: Running diesel engines on biodiesel
8.3: Heating with biodiesel
8.4: Life-cycle analysis: biodiesel EROI
8.5: Future: Europe’s lead, promise and problems
MEC 3040: Bioenergy

## Slide 2
8.3: A second, easier use: heating with biodiesel

## Slide 3
Number 2 heating oil is virtually the same as petro-diesel and can therefore be blended with, or replaced by, biodiesel.
  ‘bioheat’ = B2 to B5
  ‘biofuel’
Petro 2D to biodiesel?
Pahl (2005); Dahiya (2015)
Conversion from 2D to biodiesel doesn’t require any retrofitting.
Just add biodiesel to the fuel tank.
Keep extra fuel filters on hand and change the filters frequently until all the sludge in the fuel tank and lines has been dissolve and displaced.
Watch the seals on the fuel pump, or have the seals replaced if you are planning to use B100.
There are no winterization problems if the fuel is stored in the house.
Use of B100 in furnaces will require some retrofitting.
The oil heat industry plans to convert to B100 by 2040.
Use of heating oil in Vermont peaked at 80% of homes in 1970 & declined to 58% by 2000.

## Slide 4
Roughly 75% of homes heated with fuel oil are located in the Northeast.
Changing oil use in the Northeast
Pahl (2005); Dahiya (2015)
Switching all homes from number 2 petro-diesel to B5 would save 50 million gallons of fossil fuel heating oil per year.
US heating uses 6 billion gallons of number 2 each year.
Switching to B20 would require 1.2 billion gallons of biodiesel.
We could do this now, but would use most of our 2 b gallon capacity.
B20 is working in the real world today:
Schools in Warwick, RI converted to B20 without incident; less O&M.
Newburg, NY fuel dealer has switched to B20 without any issues.
Fuel dealers in Maine, Vermont and Massachusetts are now following along.
Bourne Energy’s bioheat program:
Used a VSJF grant to build a 10,000 gallon tank for B100 (from WMBD, NH) & blending facility in Morristown VT.
Blend and sell B5 to B99