## Slide 1
Module 8: Biodiesel uses and future
8.1: Comparing biodiesel to petro-diesel
8.2: Running diesel engines on biodiesel
8.3: Heating with biodiesel
8.4: Life-cycle analysis: biodiesel EROI
8.5: Future: Europe’s lead, promise and problems
MEC 3040: Bioenergy

## Slide 2
8.4: Life-cycle assessment: biodiesel EROI

## Slide 3
Factors affecting biodiesel EROI
Dahiya (2015)
EROI is a measure of the energy produced by a fuel relative to the energy needed to produce it.
1:1 is a breakeven ratio.
The higher the ratio, the better the return on investment.
EROI values for biodiesel vary greatly. Why?
Three factors account for most differences:
1. No standard system boundaries used in deciding which cost to include.
2. No standard methods applied to estimate energy costs.
3. No standard methods used to account for co-products.
Also: feedstock can be virgin (low EROI) or used (higher EROI)

## Slide 4
Biodiesel EROI values
Dahiya (2015)
Reclaimed vegetable oil | EROI
Elsayed et al. (2003) | 4.85 – 5.88
Soybean oil | EROI
Pimental & Patzek (2005) | 0.78
Carraretto et al. (2004) | 2.090
Ahmet et al. (1994) | 2.5
Sheehan et al. (1998) | 3.215
Hill et al. (2006) | 3.67
Pradhan et al. (2009) | 4.56
Sunflower oil | EROI
Pimental & Patzek (2005) | 0.76
Edwards et al. (2006) | 0.85 – 1.08
Bona et al. (1999) | 1.3 – 8.7
ADEME & DIREM (2002) | 3.16
Kallivroussis et al. (2002) | 4.5
Rapeseed oil | EROI
Edwards et al. (2006) | 1.05 – 1.38
IEA (1999) | 1.09 – 2.48
Elsayed et al. (2003) | 2.17 – 2.42
ADEME & DIREM (2002) | 2.99
Richards (2000) | 3.71

## Slide 5
EROI can be studied at 3 levels
Dahiya (2015)
First-order EROI is calculated as:
EROI = EO
ED
EO is the energy contained in one unit of fuel
ED is the energy required to convert that unit of fuel
Second-order EROI is calculated as:
EROI = EO
ED + EI
EI is the indirect cost to deliver a unit of fuel (aka embodied energy costs)
First-order EROI is straightforward with a high level of certainty.
Second-order EROI has a much broader scope that first-order EROI.
  Indirect costs are difficult and tedious to estimate.
  There are no agreed upon methods of analysis.
  Less certain than first-order analysis.

## Slide 6
Input costs
Dahiya (2015)
seed
planting
cultivation
harvest
drying / cleaning
storage
pressing
processing
biodiesel
farm equipment
fertilizers
pesticides
oil-seed press
bodiesel processor
reagents
meal
glycerol
20%
82%
80%
18%

## Slide 7
Biodiesel regulations in the US
Pahl (2005)
1999 – 2001: ASTM standards for biodiesel were published for B100 and blends ranging from B5 to B20.
The standard gave vehicle manufacturers guidance & certainty.
1992: the Energy Policy Act of 1992 required fleets to buy vehicles that used non-petroleum fuels.
1998 amendment allowed use of biodiesel.
By 1999 major fleets were switching to B20 in order to comply.
1998: the EPA found that biodiesel had lower emissions (except for NOx) than petro-diesel.
2000: EPA found that biodiesel was a lower threat to human heath.
2001: the EPA ruled that sulfur levels in petro-diesel had to be reduced from 500 to 15 ppm by 2010. Biodiesel can do this.
National Biodiesel Accreditation Commission runs a voluntary quality assurance program, BQ-9000.

## Slide 8
US biodiesel subsidies
Pahl (2005)
2000: USDA’s Commodity Credit Corporation (CCC) launched the US Bioenergy Program to spur construction of alternative fuel plants.
The program offered subsidies for growth of soybean oil
2002: The Farm Bill broadened the subsidy to support recycled FOG, though at much lower levels.
Both subsidies lowered biodiesel prices to consumers by about $1.00 and helped to create a market for biodiesel.
The soy bias was a result of lobbying and limited the supply of biodiesel feedstock.