## Slide 1
SSC 2030: Energy Systems & Sustainability
3. Primary energy forms and uses
3.1: Primary energy consumption (conservation!)
3.2: Units of energy and energy data
3.3: Energy density (aka heat content)
3.4: Global and regional sources of energy
3.5: UK energy use today
3.6: Primary energy: UK vs. Denmark vs. US
3.7: Primary energy: France vs. India vs. China
3.8: Trends in US energy use
3.9: Vermont energy statistics

## Slide 2
3. Primary energy forms and uses
  3.1: Energy ‘consumption’
Remember that energy is conserved.
Humans transfer & transform energy.
Transformation from primary energy to used energy is inefficient
Human energy use has increased through time

## Slide 3
Energy ‘consumption’
The 1st law of thermodynamics:
Energy is neither created nor destroyed, but transformed or transferred.
So, the US transforms or converts more energy…
We say that, “The US consumes more energy per capita than any other nation on earth.”
But, that’s incorrect.
Energy Systems & Sustainability, 2/e, Chapter 2
Combustion: fuel  heat energy electricity
chemical energy
Hydroelectric: potential energy  kinetic energy  electricity
Wind power: kinetic energy  electricity
How? For example:

## Slide 4
Let’s start with the fuels
The 1st law of thermodynamics:
Energy is neither created nor destroyed, but transformed or transferred.
So, the US transforms or converts more energy…
We say that, “The US consumes more energy per capita than any other nation on earth.”
But, that’s incorrect.
Energy Systems & Sustainability, 2/e, Chapter 2
Combustion: fuel  heat energy electricity
chemical energy
Hydroelectric: potential energy  kinetic energy  electricity
Wind power: kinetic energy  electricity
How? For example:
Primary energy

## Slide 5
Primary energy
Primary energy:
Total energy content of the energy source.
Naturally occurring energy stores or energy carriers.
“Energy in the form that it is first accounted for in a statistical energy balance, before any transformation to secondary or tertiary forms of energy.
For example, coal can be converted to synthetic gas, which can be converted to electricity; in this example, coal is primary energy, synthetic gas is secondary energy, and electricity is tertiary energy.”
Energy Systems & Sustainability, 2/e, Chapter 2 / EIA
Primary energy is the fuel that we convert to make the electricity, heat or work that we use.

## Slide 6
Conversion of primary to useful energy
Transformation of energy, from one form to another, and transfer of energy from generator to user, both result in losses.
Overall, this process is inefficient, particularly for electricity.
Energy Systems & Sustainability, 2/e, Chapter 3
primary
secondary
tertiary
delivered
used
wasted
10% used
90% wasted
2.5% used
in mining
60-70%
waste heat
7% loss
transmission
1 GJ
32 MJ CFL light
948 MJ waste heat

## Slide 7
Energy flow maps sources to uses
EIA, 2011
https://flowcharts.llnl.gov/content/energy/energy_archive/energy_flow_2013/2013USEnergy.png
waste heat

## Slide 8
Energy use has increased over time
Why?
New technologies: fire  steam  electricity  etc.
New uses: ‘services’ include our computers & nifty new devices
Rapidly growing human population
Energy Systems & Sustainability, 2/e, Chapter 3

## Slide 9
3. Primary energy forms and uses
  3.2: Units of energy and energy data
  Energy is an amount while power is a rate
  Units… many different units
  Heat content: a measure of fuel’s energy

## Slide 10
Let’s compare everyday fuels
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Comparing everyday amounts of gasoline, oil and coal:
 | Joule | Btu | Calorie (kcal) | kWh
Full gas tank | 1,570,893,171 | 1,488,857 | 375,192,000 | 436
Gallon of gas | 130,907,764 | 124,071 | 31,266,000 | 36
*Barrel of gas | 5,498,126,100 | 5,211,000 | 1,313,172,000 | 1,527
*Barrel of crude oil | 6,119,580,000 | 5,800,000 | 1,461,000,000 | 1,700
Coal, 2000 lb | 21,896,490,300 | 20,753,000 | 5,299,756,000 | 6,082
So, it’s clear that we’re going to have to have a basic understanding of units & simple conversion math (‘energy arithmetic’) even in this course.
* 1 barrel = 432 US gallons or 159 L

## Slide 11
Units of energy vs. power
Energy:
Power:
Energy Systems & Sustainability, 2/e, Chapter 2
J Joule
Btu British thermal unit
kW-hr kilowatt-hour
cal calorie
Cal (or kcal) kilocalorie
ft-lb foot-pound
TOE ton oil equivalent
TCE ton coal equivalent
Quad = quadrillion Btu = 1 E15 Btu = 1.056 EJ
Therm = 100,000 Btu
W watt
HP horsepower
See: APS physics link for more information

## Slide 12
Scientific notation & metric prefixes
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
number | scientific notation
2 | 2 E0
300 | 3 E2
3,421.768 | 3.421768 E3
-53,000 | -5.3 E4
6,720,000,000 | 6.72 E9
0.2 | 2 E-1
0.00000000751 | 7.51 E-9

## Slide 13
Often confused…
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Units can be confusing. Here are two frequent issues:
When is a ton a tonne?
What’s the difference between m & M?
1 tonne | 1000 kg | 2200 lb
1 ton | 1016 kg | 2240 lb
1 short ton | 907 kg | 2000 lb
m | milli- | 1 E-3
M | mega- | 1 E6
MM | Mega- | 1 E6
And writers are often sloppy:
Furnace output in Btu probably means Btu/hour;
Energy use in kW probably means kWh; and
MMBtu should be interpreted as million Btu.
imperial
standard US
metric or SI

## Slide 14
Watts (W) vs. kilowatt-hour (kWh)
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Watt: the rate at which energy is being transformed or converted from
one form to another
    unit of power
    one joule per second
600 W heater?
Transforms energy to heat at a rates of 600 joules each second
Global consumption of 15.9 TW of energy?
We convert 15.9 million million joules of primary energy each second to electricity, heat, etc.,.
Kilowatt-hour: the amount of energy being converted in one hour, at a rate of one kilowatt (1 E3 W)
    unit of energy
    1 kWh = 3.6 MJ
3 kW clothes dryer used for 40 minutes?
Converts 2 kWh of electricity into heat energy
  [ =(2/3 hr)(3 kW) = 2 kWhr]

## Slide 15
3. Primary energy forms and uses
  3.3: Energy density (aka heat content)

## Slide 16
Relative energy densities
Energy Systems & Sustainability, 2/e, Chapter 4; http://xkcd.com/1162

## Slide 17
Chemical energy density
Storing energy is ‘expensive’ in terms of quantities of chemical or potential energy needed.
Energy Systems & Sustainability, 2/e, Chapter 4
fuel (=chemical energy) | MJ/kg
hydrogen gas | 130
natural gas | 55
gasoline | 45
oil | 42
coal | 28
ethanol | 27
wood | 15
pounds to store 10 gas gallon equivalents
22
52
68
105
191
6,578
11,440
762,667
lead-acid batteries
water at 80c
pumped storage (h = 370 m)

## Slide 18
HHV vs. LHV heat values?
There are two ‘flavors’ of heat values (or energy densities) for combusted fuels.
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Fuel | HHV (MJ/kg) | LHV (MJ/kg)
hydrogen | 141.80 | 119.96
methane | 55.50 | 50.00
propane | 50.35 | 46.35
diesel | 44.80 | 43.40
wood | 21.20 | 17.0
HHV (high heat values) used when the steam is condensed after use; condensing steam to water releases additional energy.
Aka HCV or GCV
LHV (low heat values) used when the steam is not condensed after use.
Aka LCV or NCV

## Slide 19
Comparing heat contents (energy density)
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
 | Btu/gallon (gross) | Btu/gallon (net)
Auto gasoline | 125,000 | 115,400
hydrogen | 134,200 | 113,400
Diesel fuel | 138,700 | 128,700
biodiesel | 126,206 | 117,093
methanol | 64,600 | 56,560
ethanol | 84,600 | 75,670
gasohol | 120,900 | 112,417
Aviation gas | 120,200 | 112,000
propane | 91,300 | 83,500
butane | 103,000 | 93,000
Jet fuel (naptha) | 127,500 | 118,700
Jet fuel (kerosene) | 135,000 | 128,100
Crude petroleum | 138,100 | 131,800
Residual fuel oil | 149,700 | 138,400
Distillate fuel oil | 138,700 | 131,800
Gaseous & solid fuels | Btu/_____
Natural gas, wet | 1,109 Btu/ft3
Natural gas, dry | 1,027 Btu/ft3
Natural gas, compressed | 20,551 Btu/lb
Liquid natural gas | 90,800 Btu/gallon
Anthracite coal | 21.7 E6 Btu/short ton
Lignite/bit coal | 21.0 E6 Btu/short ton
Net = water’s heat of vaporization is subtracted from gross energy content

## Slide 20
3. Primary energy forms and uses
  3.4: Global and regional sources of energy
  Current global use and projections
  Energy inequity
  Use of renewable energy?

## Slide 21
Predicted growth
Energy Systems & Sustainability, 2/e, Chapter 2 / repsol.com
1 quad
= 1 E15 Btu
= 1.06 E18 J
= 25.2 Mtep

## Slide 22
The 14%
Energy Systems & Sustainability, 2/e, Chapter 2 / Table 2.3
A small part of the world’s population uses most of its energy resources.
 | Population (global %) | Energy produced (%) | Energy consumed (%) | Primary energy consumption per capita** | GDP per capita**
Wealthiest* | 14% | 31% | 41% | 3.1 | 3.4
Others | 86% | 69% | 59% | 0.7 | 0.5
* USA, Canada, Western Europe, Australia, New Zealand, Japan
** As a multiple of the global average

## Slide 23
Global use of renewable energy resources
Energy Systems & Sustainability, 2/e, Chapter 2 / wikiwand.com
Breaking out renewable energy.

## Slide 24
  3.5: UK energy use today
3. Primary energy forms and uses

## Slide 25
UK energy use today
UK total primary energy consumption in 2009: 9000 PJ (9000 E15 J)
UK population was 62 million in 2009
So, per capita energy use: 145 GJ per person
Energy Systems & Sustainability, 2/e, Chapter 3
We’re about to dive into some data that demonstrates:
8840 PJ of energy is provided
6021 PJ of energy is delivered
There’s a discrepancy of 2819 PJ
  5% (141 PJ) is used for shipping
  95% is lost in conversion & delivery
  Electricity generation is only 35% efficient

## Slide 26
UK primary energy use & consumption
Energy Systems & Sustainability, 2/e, Chapter 3

## Slide 27
UK delivered energy consumption
Energy Systems & Sustainability, 2/e, Chapter 3
Here we can look at the types and amounts of fuels used by each sector in the UK.
What stands out to you?

## Slide 28
UK primary vs. delivered energy
Energy Systems & Sustainability, 2/e, Chapter 3
~30% loss
~30% loss

## Slide 29
UK industrial vs. domestic use
Energy Systems & Sustainability, 2/e, Chapter 3
UK industrial use
UK domestic use

## Slide 30
UK generation & distribution of electricity
Energy Systems & Sustainability, 2/e, Chapter 3
~10% used

## Slide 31
UK trends in energy use by sector
Energy use per capita has only increased by about 50% over the last 100 years.
  Industry has become more efficient.
  Transportation has doubled energy use; more autos.
Energy Systems & Sustainability, 2/e, Chapter 3

## Slide 32
3. Primary energy forms and uses
  3.6: Primary energy: UK vs. Denmark vs. US
  What’s self-sufficiency?
  UK
  Denmark
  US

## Slide 33
The ideal primary energy profile?
Energy Systems & Sustainability, 2/e, Chapter 2 / wikiwand.com
What should a country’s (or a region’s or planet’s) primary energy profile look like?
1. Self-sufficient: a good match between primary energy production & consumption. Self-sufficiency (%) = primary energy production (100)
primary energy consumption
2. Low-carbon & low polluting
3. Sustainable & local

## Slide 34
Primary energy in the UK
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
Compared to other industrialized countries: less biomass; little hydro.
When North Sea oil & gas was at its peak (1970-80s) UK was a net oil & NG exporter. Now past peak and importing.
Still consuming residual coal reserves.

## Slide 35
Changes in UK primary energy use
Energy Systems & Sustainability, 2/e, Chapter 2
This graph of UK primary energy production & use shows how UK production & consumption have determined whether the country is a net importer or exporter.
Coal exports
WWII
North Sea oil & NG
depleted

## Slide 36
Influence of energy insecurity
Energy Systems & Sustainability, 2/e, Chapter 3
waste heat
The UK has been fuel secure; first coal, then North Sea oil & gas.
However, prior to 1970, Denmark imported nearly all its fuel, 95% oil
When oil prices soared in the 1970s & 1980s Demark was forced to act and make changes:
  Extreme energy conservation;
  Power stations switched from oil to coal;
  Expansion of use of CHP (combined use of heat & power);
  Favored district heat over individual heating systems;
  Requirements for insulation and building standards; &
  More renewable energy, particularly wind & biomass.
Results? (2007)
Energy use in Denmark has been stable since 1980.
District heat was used in 60% of homes & made up 12% of delivered energy.
CHP kept waste down to 22% vs. 32% in the UK.
Renewable energy rose to 14%.
Still dependent on oil, particularly for transportation.

## Slide 37
Primary energy in Denmark
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
Like UK, ff dominate use and production.
Per capita energy use is very similar the UK & Denmark.
Unlike the UK, Denmark was self-sufficient in 2009.
Denmark had very little native ff energy resources.
  Denmark has halved oil consumption since 1970.

## Slide 38
Changes in Denmark’s primary energy use
Energy Systems & Sustainability, 2/e, Chapter 2
Denmark had little coal, and when they got North Sea oil & NG they made it last.
To Denmark, it’s obvious that the future is RE and conservation.
Demark relied on imported
ff energy until ….
North Sea oil & NG
RE = 14% of production
= 20% of consumption
Notice that consumption has remained flat even while production has risen.

## Slide 39
RE in Denmark
Energy Systems & Sustainability, 2/e, Chapter 2
By 2008, Denmark had made much greater use of renewable energy than the UK.
Use of heat pumps for space heating has contributed to conservation of fossil fuels and electricity.

## Slide 40
Primary energy in the US
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
Note that the US prefers oil to NG and coal.
The US is a net exporter of coal, mainly to Europe, though coal mining & exporting are falling.
The US is also a net exporter of NG (gas by pipeline, liquid by tanker) to Canada, Mexico, Argentina, Barbados, Brazil, Chile, China, India, Japan, Portugal, Taiwan & the UAE.
Self sufficiency was 61% in 2013.

## Slide 41
Changes in US primary energy use
Energy Systems & Sustainability, 2/e, Chapter 2
Our consumption has continued to rise.
Recently (not shown here) fracking has increased exports.
US has been a net energy importer since 1950.

## Slide 42
RE in the US
Energy Systems & Sustainability, 2/e, Chapter 2
By 2009, the US produce about 8% of energy with renewable resources.
Ethanol use is a result of government subsidies and the farm lobby.
2019: RE up to 11% in the US

## Slide 43
US predicted net energy exporter: 2017
https://www.eia.gov/todayinenergy/detail.php?id=29433
US has been a net energy importer since 1950.
EIA predicts that the US could be energy self-sufficient by 2035.
Dec 2018: net oil exporter
2019: $12 b in LNG exports

## Slide 44
Recent energy use in the US
Energy Systems & Sustainability, 2/e, Chapter 1
https://www.eia.gov/energyexplained/?page=us_energy_home

## Slide 45
Comparing the UK, Denmark & US
Energy Systems & Sustainability, 2/e, Chapter 2
Fossil fuel use is similar across the board.
Consumption much higher in the US.
Only Denmark is self-sufficient.
Denmark produces and uses more renewable energy.
 | Fossil fuels (% primary consumption) | Per capita use (GJ/year) | Self-sufficiency (%) | RE (% produc.) | RE (% consump.)
UK | 89.2 | 143 | 79.5 | 3.7 | 3.5
Denmark | 80.4 | 145 | 125.0 | 13.7 | 19.5
US | 86.1 | 306 | 76.9 | 7.9 | 6.2

## Slide 46
3. Primary energy forms and uses
  3.7: Primary energy: France vs. India vs. China
  France
  India
  China
  Global future forecast?

## Slide 47
US & France (1970 – 2008)
Energy Systems & Sustainability, 2/e, Chapter 3
waste heat
US: Per capita energy use is high.
Energy use rose across all energy sectors, averaging 40% increase.
Service sector saw the largest increase.
50% 30% of electricity is generated with coal.
  Coal-fired plants increased three-fold.
  Electricity losses (27 EJ) are larger than total production in the UK.
France: Per capita energy use is also high.
Energy use rose across all energy sectors:
  By 75% to 2005, then decreased slightly.
75% of electricity is generated with nuclear power.
Uses less NG than UK or US.

## Slide 48
Primary energy in France
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
With few fossil fuel resources, France has become the world leader in producing nuclear energy.
  In fact, a 2014 report suggested that France would deplete its fossil fuel resources within one year.
Since nuclear energy can’t be used for transportation and heating, causing France to import large amounts of oil and NG.

## Slide 49
India
Energy Systems & Sustainability, 2/e, Chapter 3
waste heat
India: Overall, per capital energy use is very low, but rising.
Population is massive.
25% live in cities where energy use is higher and growing quickly.
50% of population (mainly rural) still lack electricity.
Coal is used for electricity
  Efficiency is a low 28%
  25% of all electric production is lost.
Agriculture uses 25% of all electricity; mainly for irrigation; diesel pumps are also used.
About 25% of primary energy is biofuel / biomass.
National programs push electrification and use of LNG vs. biomass.

## Slide 50
Primary energy in India
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
2nd largest population; 4th largest consumer of energy.
Dependent on native biomass & coal.
India has large reserves of coal, but quality is so low that they import better coal.

## Slide 51
China
Energy Systems & Sustainability, 2/e, Chapter 3
waste heat
China: Energy use low but rising.
Population is massive: rose to 1.3 billion by 2006, 80% live in cities.
In 2005, biomass still made up 20% of primary energy, and 50% of domestic fuel.
From 1980 – 2006, primary energy use increased three-fold, and GDP increased 10-fold.
From 1952 – 1978, energy / GDP ratio tripled, then fell with efficiency.
Industrial energy use is massive & rose 4-fold from 1980 – 2006. 80% of all new energy use is industrial. Industry consumes 70% of all electricity, most generated from coal. (100 years of coal are left.)
  In 2006, China produced many global goods: 50% of cement & glass; 35% of steel; 28% of aluminum.
Agriculture uses 3.5% of all electricity, mainly pumping deep wells.
Transportation is up from 0.8 to 5 EJ, nearly all petroleum.

## Slide 52
Primary energy in China
Energy Systems & Sustainability, 2/e, Chapter 2
Production
Consumption
China’s rapid industrialization and development during the 20th century
is driving increased coal production.
Coal is our largest remaining fossil fuel reserve.
And reserves are found in Asia.
Recently, China has massively deployed RE.

## Slide 53
How is this changing?
http://www.eco-business.com/news/seven-charts-show-new-renewables-outpacing-rising-demand-for-first-time/
Investment in electric generation and networks for 2015 (IEA data).

## Slide 54
  3.8: Trends in US energy use
  Some increases in use and in efficiency
  Gains in efficiency lost to increased use for electronics
  Heating may be returning to electricity
  Manufacturing has become more efficient
  Transportation is a huge FF user
3. Primary energy forms and uses

## Slide 55
Growth of consumption by sector
https://www.eia.gov/totalenergy/data/annual/pdf/sec2.pdf
waste heat
Not surprisingly, energy use most sectors has increased since WWII.
Why does industrial use seem to be leveling off more than other uses?
What was going on with industrial use in the late 1970s, early 1980s?

## Slide 56
But efficiency evolves as well
Energy use / $GDP is a measure of a nation’s energy efficiency or of the nature of the nation’s economy.
EIA
By the 1990s, the US was manufacturing less than China, but increasing energy costs and scarcity were causing the Chinese economy to become more efficient.

## Slide 57
Evolution of lighting technologies
http://www.led-evolution.com/Technology/benefits-of-LED.html
Lighting technology continues to become more energy efficient.

## Slide 58
Domestic energy use
https://www.eia.gov/todayinenergy/detail.php?id=10271
Energy use in homes hasn’t changed dramatically, but use has shifted.
Efficiency has increased, lowering energy use for heating and cooling.
But energy use for ‘electronics’ has increased.

## Slide 59
Heating fuels have also changed
Efficiency Vermont
Heating fuels have changed… and changed back!
wood  coal  oil  electricity  natural gas  (RE) electricity
antiquity
1700 - 1900
1900 -
1970s
1920 -
2000s

## Slide 60
Manufacturing energy use down
https://www.eia.gov/consumption/manufacturing/

## Slide 61
Manufacturing output, not so clearly
EIA: https://www.eia.gov/consumption/manufacturing/reports/2014/pre_estimates/

## Slide 62
Transportation in the US
http://news.thomasnet.com/imt/2012/03/12/the-damage-done-gas-addiction-edition-how-detrimental-is-petrol
In the US, transportation is dominated by the private auto.

## Slide 63
Commercial services
Energy Systems & Sustainability, 2/e, Chapter 3; EIA
Note that heating & lighting account for 2/3 of all energy use.

## Slide 64
  3.9: Vermont energy statistics
  RE accounts for ~25% of primary energy
  Most electricity supply is RE
  Transportation and heating are FF dependent
  Energy production and consumption are low.
  Energy costs are high
  Vermont‘s Comprehensive Energy Plan is agressive
3. Primary energy forms and uses

## Slide 65
Vermont primary energy use (2015)
24.8% RE
71.4%
fossil fuels
EIA State Energy Profiles & Estimates

## Slide 66
Vermont primary energy use (2015)
193,000 MWh
EIA State Energy Profiles & Estimates

## Slide 67
Vermont energy use by sector (2015)
EIA State Energy Profiles & Estimates

## Slide 68
Vermont energy stats (2015)
EIA State Energy Profiles & Estimates
One in 6 Vermont households uses wood products as their primary heating source.
Vermont produces less than 35% of its electricity & depends on power from the New England grid and Canada.
In 2016, nearly all of Vermont's in-state net electricity generation was produced by renewable energy, including hydroelectric, biomass, wind, and solar resources.
In the years 2011 through 2016, Vermont installed 59.2 megawatts of commercial-scale solar photovoltaic capacity, 26.8 megawatts in 2016 alone.
Vermont has enacted the nation's first integrated renewable energy standard (RES), which makes utilities responsible both for supplying renewable electricity and for supporting reductions in customers' fossil fuel use.

## Slide 69
Vermont energy stats (2015)
EIA State Energy Profiles & Estimates
 | value | US ranking
Population | 600,000 | 
Labor force | 300,000 | 
GDP | $31.1 billion | 51
Average temperature | 44.7 F | 43
Average rainfall | 39.1 inches | 24
Per capita income | $50,321 | 20
Total energy consumption |  | 50
Energy consumption per capita | 211 million Btu/year | 44
Energy cost per capita | $4,273 | 9
Energy production |  | 47
Electricity production |  | 50
RE production | 204,000 MWh | 
RE consumption | 24.9% of all energy consumption | 8
Electricity costs |  | 8
Energy intensity | 8,1000 Btu/$ GDP | 
Total carbon emissions | 6 millionn metric tonnes CO2 | 50

## Slide 70
Vermont Comprehensive Energy Planning
http://www.vtenergydashboard.org/90-by-2050/detail/2016-comprehensive-energy-plan