## Slide 1
SSC 2030: Energy Systems & Sustainability
Introduction to energy systems & sustainability
  1.1: What is energy?
  1.2: What is ‘conventional’ energy?
  1.3: What is ‘sustainable’ energy?
  1.4: What is a system?
  1.5: Why is systems thinking important?

## Slide 2
1. Introduction
  1.1: What is energy?

## Slide 3
What is energy?
Energy: the capacity to do work
    To move an object against a resisting force
    Measured in joules (J)
Energy Systems & Sustainability, 2/e, Chapter 1
Energy is conserved:
Energy can be neither created nor destroyed.
Instead it is transferred (moved) or transformed (from one form to another.)
The word energy was first used in this modern context by Thomas Young, celebrated British physicist in 1807.
This course is concerned with the study of how humans transform energy from energy resources to useful energy, and how we transfer it from one entity or location to another until that energy reaches the consumer or end user.
And that’s not the end. Once ‘used’ most energy is transformed into low density, low temperature heat & dissipated or wasted.

## Slide 4
Energy as heat or electricity (power)
However, when studying energy systems, these terms are used differently.
Energy Systems & Sustainability, 2/e, Chapter 1
Power: electricity, or a source of means of supplying electricity
Expressed in units of:
  watts (W), kilowatts (kW), megawatts (MW), etc.
  kilowatt hours (kWh: the amount of electricity used in 1 hour)
Heat: (1) the flow of energy from a hot object to a cooler object
(2) a form of energy resulting from the movement of atoms, molecules or ions in a substance
(3) the lowest, most diffuse or most disordered form of energy
Expressed in units of J, calories, British thermal units, etc.

## Slide 5
1. Introduction
  1.2: What is ‘conventional’ energy?

## Slide 6
Conventional energy
Conventional energy: sources and forms of energy that are in widespread use today.
https://www.epa.gov/greenpower/what-green-power

## Slide 7
1. Introduction
  1.3: What is ‘sustainable’ energy?

## Slide 8
Sustainable?
1: capable of being sustained
2a : of, relating to, or being a method of harvesting or using a resource so that the resource is not depleted or permanently damaged sustainable techniques sustainable agriculture
2b : of or relating to a lifestyle involving the use of sustainable methods sustainable society
- Merriam-Webster.com
“sustainable development is development that meets the needs of the present without compromising the ability of future generations to meet their own needs.”
- Brundtland Commission, U.N., 1987
"We are looking ahead, as is one of the first mandates given us as chiefs, to make sure and to make every decision that we make relate to the welfare and well-being of the seventh generation to come. ... What about the seventh generation? Where are you taking them? What will they have?"
- Oren Lyons, Chief of the Onondaga Nation

## Slide 9
What is sustainable energy?
Energy Systems & Sustainability, 2/e, Chapter 1
Sustainable energy uses sources that meet these requirements:
1. Are not significantly depleted by continued use;
2. Do not emit pollutants or other hazards to humans or ecological and
climate systems on a significant scale; and
3. Do not perpetuate social injustice.
In this course, we’ll look at the argument that many forms of energy can be considered sustainable if they are used in a sustainable manner.

## Slide 10
Three linked ‘pillars’ of sustainability
Energy Systems & Sustainability, 2/e, Chapter 1
Economic sustainability: encompasses requirements for strong & durable economic growth; preserving financial stability & a low & stable inflationary environment
Environmental sustainability: focuses on the stability of biological & physical systems and on preserving access to a healthy natural environment
Social sustainability: emphasizes the importance of well functioning labor markets & high employment, of adaptability to major demographic change & stability in social & cultural systems of equity and democratic participation in decision making
- IEA (2001); OECD (2001)
There are those who advocate for any sustainable change and those who believe climate change and other challenges require a much more rigorous approach to sustainability. [weak vs. strong sustainability]

## Slide 11
Three linked ‘pillars’ of sustainability
https://sustain.wisconsin.edu/sustainability/triple-bottom-line/
Social sustainability
culture
ethics
equity
Environmental sustainability
ecosystems
Economic sustainability
growth
profit
costs
*
aka ‘Triple Bottom Line’

## Slide 12
Theory vs. reality?
W.M. Adams (2006) The Future of Sustainability
Re-thinking Environment and Development in the Twenty-first Century .
http://cmsdata.iucn.org/downloads iucn_future_of_sustanability.pdf
Economy
Society
Environment
Theory
Economy
Society
Environment
Reality
Economy
Society
Environment
Change that needs to happen

## Slide 13
Decarbonized? Low-carbon? Renewable?
https://sustain.wisconsin.edu/sustainability/triple-bottom-line/
*
Low-carbon: processes or technologies that produce power [or heat] with substantially lower amounts of carbon emissions than is emitted from conventional (fossil fuel) power generation
There is no carbon-free fuel.
Renewable: processes or technologies that produce power [or heat] from sources that are not depleted when used
Nuclear: processes or technologies that produce power from the fission or fusion of atoms
  Nuclear is finite rather than renewable, but is low-carbon

## Slide 14
Sustainability of our energy resources?
https://ourworldindata.org/how-long-before-we-run-out-of-fossil-fuels
These are global reserves.

## Slide 15
This changes if we mitigate GCC
https://ourworldindata.org/how-long-before-we-run-out-of-fossil-fuels
These are global budgets.

## Slide 16
Why does sustainable energy matter?
Energy Systems & Sustainability, 2/e, Chapter 1
1. There is a very large unmet demand for energy in developing countries.
There are three major reasons, each creating a point of view or perspective.
2. The supply of fossil fuels is finite and won’t meet these demands.
3. GCC requires us to dramatically reduce emissions of carbon dioxide.
‘Growthist’
‘Peakist’
‘Environmentalist’

## Slide 17
POV and perspective shape action
growthist
environmentalist
peakist
‘As we get richer, I’ve no doubt we’ll find ingenious ways of getting the remaining fossil fuel out of the ground and we have other options like nuclear power too – but how much more carbon dioxide can we dump into the atmosphere?’
‘Consumption is at the heart of the matter. We can’t go on comsuming as we do. The bad news is that we are changing the Earth’s climate. The good news is that we may be running out of cheap oil and gas, possibly coal’
‘We’ve got plenty of options to solve climate change – but I am concerned that we are running out of cheaper energy supplies and this could impact on global economic growth rates.’
‘Economic prosperity is the key to solving the twin problems of maintaining energy supply and combatting climate change.’

## Slide 18
Global climate change
Coming to you next week in Module 2!

## Slide 19
1. Introduction
  1.4: What is a system?

## Slide 20
What is a system? (1)
“So what is a system? A system is a set of things-people, cells, molecules or whatever- interconnected in such a way that they produce a pattern of behavior over time. The system may be buffeted, constricted, triggered, or driven by outside forces. But the system's response to these forces is characteristic of itself, and that response is seldom simple in the real world.”
“The system, to a large extent causes its own behavior!”
- Donella Meadows, Thinking in systems: a primer
1: a regularly interacting or interdependent group of items forming a unified whole a number system: such as
a group of interacting bodies under the influence of related forces a gravitational system
an assemblage of substances that is in or tends to equilibrium a thermodynamic system
      - Merriam-Webster.com

## Slide 21
What is a system? (2)
System: ‘A system is an interconnected set of elements that is coherently organized in a way that achieves something (function or purpose)”
Donella Meadows, ‘Thinking in systems’
Characteristics of systems:
  Integrity (wholeness)
  Adaptive
  Resilient
  Evolutionary
  Goal-seeking
  Self-preserving
  Self-organizing
Component 2
Component 1

## Slide 22
Example?
A football team is a system.
Donella Meadows, ‘Thinking in systems’
What are the components or elements?
What are the interconnections for flows?
What is the purpose?
players
coach
management
field
ball
rules
physics
strategy
pressure?
rules
physics
Purpose: winning, $.... Fun?

## Slide 23
Sub-systems should be in harmony
Example: college or university
Donella Meadows, ‘Thinking in systems’
Purposes of students vs. faculty vs. administrators?

## Slide 24
Diagramming the bathtub example
Bathtub: classic example for about systems diagrams and behavior
Donella Meadows, ‘Thinking in systems’
stock: elements that you can see or measure
- Changes with flows
inflow
outflow
source:
where it comes from
sink:
where it goes to

## Slide 25
Bathtub behavior?
1. What happens when you pull the plug?
Donella Meadows, ‘Thinking in systems’
2. What happens when you don’t?
water level (inches)
time (minutes)
3. If inflow < outflow?
4. If inflow > outflow?
5. How can you reach equilibrium?

## Slide 26
Most people focus on ‘stock’
Change of stock takes time and that time is related to the rate of flows.
Donella Meadows, ‘Thinking in systems’
Changes in stock determine the dynamics of the system.
Most decision are designed to regulate levels of stock.
System thinkers see the world as a collection of stocks along with the mechanisms of regulating their levels by manipulating flows.
Stock: the amount of a critical element of the system
  Note that ‘critical’ is in the eye of the beholder

## Slide 27
Feedback loops
Feedback loops: occur when a stock affects its own flows.
Donella Meadows, ‘Thinking in systems’
Feedback loops can cause stocks to remain constant, grow or shrink.
Positive (reinforcing) feedback loops amplify stock.
Positive: (1) interest rate;
(2) account balance (capital)

## Slide 28
Feedback loops
Donella Meadows, ‘Thinking in systems’
Negative feedback loops regulate (temper) growth of stock.
Stabilizing loops
Balancing loops

## Slide 29
Competing balancing loops
Donella Meadows, ‘Thinking in systems’
Here two competing balancing loops control a system regulated by a thermostat and furnace.

## Slide 30
Non-renewable constraint
Donella Meadows, ‘Thinking in systems’
Here the reinforcing (+) loop for economic capital is constrained (balanced -) by a non-renewable resource, oil.

## Slide 31
Renewable constraint
Donella Meadows, ‘Thinking in systems’
Here the reinforcing (+) loop for economic capital is constrained (balanced -) by a renewable resource, fish stocks.

## Slide 32
1. Introduction
  1.5: Why is system thinking important?

## Slide 33
Why is systems thinking important?
Micheal Goodman, ‘Systems thining: what, why, where, when, and how?’ Systems Thinker
https://thesystemsthinker.com/systems-thinking-what-why-when-where-and-how/
“Systems thinking expands the range of choices available for solving a problem by broadening our thinking and helping us articulate problems in new and different ways. At the same time, the principles of systems thinking make us aware that there are no perfect solutions; the choices we make will have an impact on other parts of the system. By anticipating the impact of each trade-off, we can minimize its severity or even use it to our own advantage. Systems thinking therefore allows us to make informed choices.”

## Slide 34
Lessons from systems thinking
Donella Meadows, ‘Thinking in systems’
1. We don’t pay enough attention from history. We focus on the events, but not the context, causes and results.
2. We aren’t great at understanding relationships. We want relationships to be linear and they often aren’t.
3. We don’t pay enough attention to sources and sinks.
4. Our minds seem to want to find single causes for single effects.
5. We don’t identify limiting factors.
6. We aren’t good at seeing true system boundaries and therefore
miss the true or full range of possible outcomes.

## Slide 35
Earth is a system
Closed system: exchanges only matter with the surroundings
http://wikieducator.org/File:Natural_Cycles-01-1.png
Open system: exchanges matter and energy with the surroundings

## Slide 36
Need for energy systems?
Goldman Sachs
(1) once societies had become complex and dependent on energy;
(2) supplies and prices of that energy had become vulnerable & volatile.
Nations developed energy systems – and energy policy…

## Slide 37
Need for energy systems?
Goldman Sachs

## Slide 38
Energy systems are complex
Energy systems connect the energy resources that nature provides to the energy services that people want.
Sanborn etal. (2008) The hydrogen defense against climate catastrophe.
Canadian Energy Systems Analysis Research, https://www.cesarnet.ca/background-energy-systems

## Slide 39
Analysis of system flows is critical
This Sankey diagram focuses on stocks and flows.
ISEEE/CanESS

## Slide 40
Broader view of energy systems
https://intelligence.weforum.org/topics/a1Gb00000038oN6EAI?tab=publications

## Slide 41
Reinforcing systems diagram: technology
Dangerman and Shellnhuber (2012) Energy systems transformation, PNAS.
Existing technologies are advantaged by their accelerating success.

## Slide 42
Success to the successful
Dangerman and Shellnhuber (2012) Energy systems transformation, PNAS.
“…the conventional system has been in place successfully for a longer period of time, and during that period competition for the adoption of technologies by consumers has occurred, for example, among the steam engine, the (electric car) battery, and the combustion engine. Thus, the technology and products of the conventional energy system obviously have built up hardware infrastructures, know-how, and goodwill. The alter- native energy system lacks this historically accumulated position.”
Marketplace success gives ‘incumbents’ an advantage.

## Slide 43
How to we shift the advantage?
Dangerman and Shellnhuber (2012) Energy systems transformation, PNAS.
“Policymakers aiming to change the status quo of the energy system therefore are faced with taking rather draconian measures, namely, not spreading their subsidies and loans over the different energy technologies— because doing so only reinforces the existing and dominating positive feedback loops—but focusing on those that solve the problems.”
“Problem-causing technologies should be addressed only by prohibitive laws, and problem-relieving technologies should be facilitated by stimulus laws..”

## Slide 44
Energy cycles are business cycles
Adapted from Marchetti and Nakicenovic (1979)