## Slide 1
SSC 2030: Energy Systems & Sustainability
3. Primary energy forms and uses
3.1: Primary energy consumption (conservation!)
3.2: Units of energy and energy data
3.3: Energy density (aka heat content)
3.4: Global and regional sources of energy
3.5: UK energy use today
3.6: Primary energy: UK vs. Denmark vs. US
3.7: Primary energy: France vs. India vs. China
3.8: Trends in US energy use
3.9: Vermont energy statistics

## Slide 2
3. Primary energy forms and uses
  3.2: Units of energy and energy data
  Energy is an amount while power is a rate
  Units… many different units
  Heat content: a measure of fuel’s energy

## Slide 3
Let’s compare everyday fuels
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Comparing everyday amounts of gasoline, oil and coal:
 | Joule | Btu | Calorie (kcal) | kWh
Full gas tank | 1,570,893,171 | 1,488,857 | 375,192,000 | 436
Gallon of gas | 130,907,764 | 124,071 | 31,266,000 | 36
*Barrel of gas | 5,498,126,100 | 5,211,000 | 1,313,172,000 | 1,527
*Barrel of crude oil | 6,119,580,000 | 5,800,000 | 1,461,000,000 | 1,700
Coal, 2000 lb | 21,896,490,300 | 20,753,000 | 5,299,756,000 | 6,082
So, it’s clear that we’re going to have to have a basic understanding of units & simple conversion math (‘energy arithmetic’) even in this course.
* 1 barrel = 432 US gallons or 159 L

## Slide 4
Units of energy vs. power
Energy:
Power:
Energy Systems & Sustainability, 2/e, Chapter 2
J Joule
Btu British thermal unit
kW-hr kilowatt-hour
cal calorie
Cal (or kcal) kilocalorie
ft-lb foot-pound
TOE ton oil equivalent
TCE ton coal equivalent
Quad = quadrillion Btu = 1 E15 Btu = 1.056 EJ
Therm = 100,000 Btu
W watt
HP horsepower
See: APS physics link for more information

## Slide 5
Scientific notation & metric prefixes
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
number | scientific notation
2 | 2 E0
300 | 3 E2
3,421.768 | 3.421768 E3
-53,000 | -5.3 E4
6,720,000,000 | 6.72 E9
0.2 | 2 E-1
0.00000000751 | 7.51 E-9

## Slide 6
Often confused…
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Units can be confusing. Here are two frequent issues:
When is a ton a tonne?
What’s the difference between m & M?
1 tonne | 1000 kg | 2200 lb
1 ton | 1016 kg | 2240 lb
1 short ton | 907 kg | 2000 lb
m | milli- | 1 E-3
M | mega- | 1 E6
MM | Mega- | 1 E6
And writers are often sloppy:
Furnace output in Btu probably means Btu/hour;
Energy use in kW probably means kWh; and
MMBtu should be interpreted as million Btu.
imperial
standard US
metric or SI

## Slide 7
Watts (W) vs. kilowatt-hour (kWh)
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
Watt: the rate at which energy is being transformed or converted from
one form to another
    unit of power
    one joule per second
600 W heater?
Transforms energy to heat at a rates of 600 joules each second
Global consumption of 15.9 TW of energy?
We convert 15.9 million million joules of primary energy each second to electricity, heat, etc.,.
Kilowatt-hour: the amount of energy being converted in one hour, at a rate of one kilowatt (1 E3 W)
    unit of energy
    1 kWh = 3.6 MJ
3 kW clothes dryer used for 40 minutes?
Converts 2 kWh of electricity into heat energy
  [ =(2/3 hr)(3 kW) = 2 kWhr]