## Slide 1
SSC 2030: Energy Systems & Sustainability
3. Primary energy forms and uses
3.1: Primary energy consumption (conservation!)
3.2: Units of energy and energy data
3.3: Energy density (aka heat content)
3.4: Global and regional sources of energy
3.5: UK energy use today
3.6: Primary energy: UK vs. Denmark vs. US
3.7: Primary energy: France vs. India vs. China
3.8: Trends in US energy use
3.9: Vermont energy statistics

## Slide 2
3. Primary energy forms and uses
  3.3: Energy density (aka heat content)

## Slide 3
Relative energy densities
Energy Systems & Sustainability, 2/e, Chapter 4; http://xkcd.com/1162

## Slide 4
Chemical energy density
Storing energy is ‘expensive’ in terms of quantities of chemical or potential energy needed.
Energy Systems & Sustainability, 2/e, Chapter 4
fuel (=chemical energy) | MJ/kg
hydrogen gas | 130
natural gas | 55
gasoline | 45
oil | 42
coal | 28
ethanol | 27
wood | 15
pounds to store 10 gas gallon equivalents
22
52
68
105
191
6,578
11,440
762,667
lead-acid batteries
water at 80c
pumped storage (h = 370 m)

## Slide 5
HHV vs. LHV heat values?
There are two ‘flavors’ of heat values (or energy densities) for combusted fuels.
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Fuel | HHV (MJ/kg) | LHV (MJ/kg)
hydrogen | 141.80 | 119.96
methane | 55.50 | 50.00
propane | 50.35 | 46.35
diesel | 44.80 | 43.40
wood | 21.20 | 17.0
HHV (high heat values) used when the steam is condensed after use; condensing steam to water releases additional energy.
Aka HCV or GCV
LHV (low heat values) used when the steam is not condensed after use.
Aka LCV or NCV

## Slide 6
Comparing heat contents (energy density)
Energy Systems & Sustainability, 2/e, Chapter 2 / wikipedia
 | Btu/gallon (gross) | Btu/gallon (net)
Auto gasoline | 125,000 | 115,400
hydrogen | 134,200 | 113,400
Diesel fuel | 138,700 | 128,700
biodiesel | 126,206 | 117,093
methanol | 64,600 | 56,560
ethanol | 84,600 | 75,670
gasohol | 120,900 | 112,417
Aviation gas | 120,200 | 112,000
propane | 91,300 | 83,500
butane | 103,000 | 93,000
Jet fuel (naptha) | 127,500 | 118,700
Jet fuel (kerosene) | 135,000 | 128,100
Crude petroleum | 138,100 | 131,800
Residual fuel oil | 149,700 | 138,400
Distillate fuel oil | 138,700 | 131,800
Gaseous & solid fuels | Btu/_____
Natural gas, wet | 1,109 Btu/ft3
Natural gas, dry | 1,027 Btu/ft3
Natural gas, compressed | 20,551 Btu/lb
Liquid natural gas | 90,800 Btu/gallon
Anthracite coal | 21.7 E6 Btu/short ton
Lignite/bit coal | 21.0 E6 Btu/short ton
Net = water’s heat of vaporization is subtracted from gross energy content