## Slide 1
SSC 2030: Energy Systems & Sustainability
4. Coal
4.1: Coal: an introduction
4.2: Fuel of the industrial revolution
4.3 : Formation & composition
4.4: Modern extraction & current uses
4.5: Coal deposits, reserves & production
4.6: Global coal resources & reserves
4.7: Coal combustion & emissions
4.8: Alternative uses of coal
4.9: Carbon sequestration & clean coal

## Slide 2
4. Coal
  4.3: Formation & composition

## Slide 3
Chemical composition of coal
Energy Systems & Sustainability, 2/e, Chapter 5; pmfias.com
organics
partially
decompose
peat
heat, pressure & time
coal (older is better)

## Slide 4
Chemical composition of coal
Energy Systems & Sustainability, 2/e, Chapter 5
Proximate analysis: Quality of coal increases with increasing carbon content.
Elements:
C
H
N
S
O
smokeless fuel
coke / steam
coke
steam

## Slide 5
Combustion of coal
Energy Systems & Sustainability, 2/e, Chapter 5
Water is heated & evaporated using a tiny fraction of coal’s energy.
smokeless fuel
coke / steam
coke
steam
increasing temperature
Volatile matter (hydrocarbons) are boiled off into gases: H2, CO, CH4, C2H4, C2H2.
The gases combust, releasing heat.
Fixed carbon (coke) combines with oxygen to produce carbon dioxide flue gases (emissions) and heat.
Ash remains: silicates & oxides of iron & aluminum.

## Slide 6
Why does coal produce more CO2?
https://www.wou.edu/las/physci/GS361/Energy_From_Fossil_Fuels.htm
smokeless fuel
coke / steam
coke
steam
increasing temperature
The higher the C:H ratio of fuels, the more carbon dioxide they produce.
Coal is often referred to as a dirty fuel because of its emissions.
And it’s said to produce more carbon dioxide than other fossil fuels. Why?
fuel | C:H ratio | Energy (MJ/kg) | CO2 (mol/MJ)
coal | 1:1 | 39.3 | 2.0
oil | 2:1 | 43.6 | 1.6
ethanol | 3:1 | 27.3 | 1.6
natural gas | 4:1 | 51.6 | 1.2
hydrogen gas | 100% H | 120.0 | 0