## Slide 1
SSC 2030: Energy Systems & Sustainability
4. Coal
4.1: Coal: an introduction
4.2: Fuel of the industrial revolution
4.3 : Formation & composition
4.4: Modern extraction & current uses
4.5: Coal deposits, reserves & production
4.6: Global coal resources & reserves
4.7: Coal combustion & emissions
4.8: Alternative uses of coal
4.9: Carbon sequestration & clean coal

## Slide 2
4. Coal
  4.7: Combustion of coal & emissions

## Slide 3
Combustion
Energy Systems & Sustainability, 2/e, Chapter 5
Moisture evaporates in the first stages of combustion.
A Watt double-acting steam engine (1859)
Volatile matter is turned to gas like CO, CH4 and other hydrocarbons.
These gases combust to create heat.
Fixed carbon combines with oxygen gas to produce carbon dioxide flue gas.
Ash is any material that remains.
Best quality coal has ~10% ash.
Lower quality may produce 15-30%.

## Slide 4
Combustion: newer technologies
Energy Systems & Sustainability, 2/e, Chapter 5
Pulverized fuel boilers create a fine carbon powder that is blown into the combustion chamber with air.
90% efficient
Problem: fine fly ash in flue gases.
A Watt double-acting steam engine (1859)
Fluidized bed boilers combust small coal particles in a bed of sand. ‘Bubbles’ of coal and air heat the entire bed.
Very efficient
Lower combustion temps, so less NOx

## Slide 5
Combustion flue gases
Energy Systems & Sustainability, 2/e, Chapter 5
Emissions: NOx, CO2, H2O, SOx, fly ash & particulates
A Watt double-acting steam engine (1859)
Coal’s challenges?
Hot, dirty & corrosive
Volume: 3000 tonnes/hour!
Very high levels of:
  Moisture
  SOx; &
  Particulates
Wyoming Public Media

## Slide 6
Making emissions real
Energy Systems & Sustainability, 2/e, Chapter 5
Let’s look at some numbers to bring home the scale of emissions from coal-fired power plants.
A Watt double-acting steam engine (1859)
A power plant burns 250 tonnes of coal per hour to produce 500 MW.
Emission | tonnes | problem?
N2 (from air for combustion) | 2000 | little harm
CO2 | 650 | GHG !
Steam (H2O) | 150 | harmless (energy loss)
NOx | 1 | acid-rain, health
SOx | 1 - 20 | acid-rain, health
Fly ash | 20 | health
Mercury vapor | 30 g | health

## Slide 7
Lowering SOx
Energy Systems & Sustainability, 2/e, Ch 5
SOx can be reduced by using limestone (CaCO3) or seawater to precipitate the 90-95% of sulfur out of the flue gases.
CaCO3 + SO2  CaSO3/4 + CO2

## Slide 8
Lowering NOx
Energy Systems & Sustainability, 2/e, Chapter 5
NOx can be reduced by:
Decreasing combustion temperatures (a la fluidized bed);
Selective catalytic reduction (removal of O from N); or
Gas reburn via added natural gas to remove oxygen.
A Watt double-acting steam engine (1859)
4NH3 + 6NO  5N2 + 6H2O
W (tungsten) or V (vanadium) catalyst

## Slide 9
Lowering particulates and ash
Energy Systems & Sustainability, 2/e, Chapter 5; wikipedia
Particulates and ash can be reduced using:
Cyclone;
Bag filter; or
Electrostatic precipitator:
A Watt double-acting steam engine (1859)
Disposing of the ash?
Ash is toxic because of metal contaminants.
Landfill; or
Use as a ‘filler’ in concrete where toxins are fixed.
Particles are ionized (charged) & then attracted to charged filters / plates.