## Slide 1
SSC 2030: Energy Systems & Sustainability
4. Coal
4.1: Coal: an introduction
4.2: Fuel of the industrial revolution
4.3 : Formation & composition
4.4: Modern extraction & current uses
4.5: Coal deposits, reserves & production
4.6: Global coal resources & reserves
4.7: Coal combustion & emissions
4.8: Alternative uses of coal
4.9: Carbon sequestration & clean coal

## Slide 2
4. Coal
  4.8: Alternative uses of coal

## Slide 3
Gasification to syngas
Energy.gov
Gasification converts hydrocarbons like coal into gases using heat, pressure and steam. Oxygen levels are controlled to prevent combustion.
A Watt double-acting steam engine (1859)
Wyoming Public Media
Syngas:
CO & H2

## Slide 4
Gasification to syngas
Energy.gov
Integrated gasification combined-cycle:
Cleaned syngas is combusted to drive a combustion turbine that drives a generator;
Exhaust heat is used to create steam, to drive a second steam turbine-generator.
Combined turbines generate electricity very efficiently: 40%
A Watt double-acting steam engine (1859)
Wyoming Public Media
Other uses of syngas?
Chemical building blocks for the chemical industries
Fuel for fuel-cell systems
Source of hydrogen
Compatible with carbon capture & storage
If oxygen is used in place of air, carbon dioxide is produced in a concentrated stream that is easier to capture and sequester.

## Slide 5
Gasification products & co-products
A Watt double-acting steam engine (1859)
Wyoming Public Media
Energy Systems & Sustainability, 2/e, Chapter 5

## Slide 6
Underground coal gasification
Energy Systems & Sustainability, 2/e, Chapter 5
Uses conventional gasification technology, put performed underground.
Wyoming Public Media
Air & water are injected into the coal seam;
Ignited under low-oxygen conditions to partially oxidize coal into:
  H2, CO, CO2, CH4, H2S
  Gases piped to the surface for combustion.
The UK will not use this technology because its CO2 emissions are significantly higher than those from NG.