## Slide 1
SSC 2030: Energy Systems & Sustainability
4. Coal
4.1: Coal: an introduction
4.2: Fuel of the industrial revolution
4.3 : Formation & composition
4.4: Modern extraction & current uses
4.5: Coal deposits, reserves & production
4.6: Global coal resources & reserves
4.7: Coal combustion & emissions
4.8: Alternative uses of coal
4.9: Carbon sequestration & clean coal

## Slide 2
4. Coal
  4.1: Introduction to coal

## Slide 3
Comparing coal, oil & NG
How does coal compare to oil and natural gas?
Abundant: huge, globally distributed reserves;
Energy Systems & Sustainability, 2/e, Chapter 5
For these reasons, coal is sometimes called the ‘ignoble’ fuel.
Yet coal production is up 4-fold from 1920 – 2009;
Even as its contribution to energy production is down from 60 – 25%
Extraction has large environmental impacts (stip-mining);
  And is a health hazard;
More difficult to transport (less dense);
Produces twice as much carbon dioxide;
Produces large amounts of ash when burned;
  Ash can leach sulfuric acid & arsenic into ground water;
  Coal ash ponds and floods; &
Produces SOx and NOx in flue gasses.

## Slide 4
History of coal use
Wood was man’s first fuel and has been used for 3000 – 4000 years.
Charcoal is partially combusted (pyrolysis) wood that is more energy dense than wood.
Energy Systems & Sustainability, 2/e, Chapter 5; Daily Mail
Coal has been used for 2000 years in China & the Middle East.
Sea coal on the beaches of Scotland
Hampton Court (1500s)
‘Sea coal’ washes ashore from underwater deposits and was traditionally collected as a highly valued fuel along the coasts.
Mining started in the Roman era.
Brick chimneys allowed wood and coal to be combusted indoors & withstood the corrosive flue gases.
  By 1680 1400 ships were used to transport coal in Britain.

## Slide 5
Air quality problems arose quickly
Air quality suffered as use of coal boomed. In this era British coal was ‘brown’ and high in sulfur. Air emissions resulted in huge amounts what we now call ‘smog’.
Energy Systems & Sustainability, 2/e, Chapter 5; wikipedia
By 1661, London was cloaked in:
"Such a cloud of sea-coal, as if there be a resemblence of hell upon earth, it is in this volcano in a foggy day: this pestilent smoak, which corrodes the very yron [iron], and spoils all the moveables, leaving a soot on all things that it lights: and so fatally seizing on the lungs of the inhabitants, that cough and consumption spare no man."
- John Evelyn petitioning Charles II for zoning to move industry out of the city and improve air quality

## Slide 6
4. Coal
  4.2: Fuel of the Industrial Revolution

## Slide 7
Industrial revolution: coal, iron & steel
The industrial revolution was made possible by coal, and one of its products, steel.
Energy Systems & Sustainability, 2/e, Chapter 5
Iron ore is actually iron oxide.
Iron is purified by the process of smelting, that removes oxygen.
Fe2O3, Fe3O4 + C  Fe + CO2 + CO
iron ore
coke
iron
flue gases
Coke: created by pyrolysis (combustion in limited oxygen) of coal at high temperatures (2000°F).
Nearly pure carbon as most impurities (O, S) are ‘driven off’
Coking works at night

## Slide 8
Industrial revolution: coal, iron & steel
Energy Systems & Sustainability, 2/e, Chapter 5; wikipedia
Steel: an alloy of iron & other elements, mainly carbon
Harder and stronger than iron
Carbon provided by adding coke
James Watt’s steam engine (1769) converted the energy of coal to heat (steam) and then mechanical work.
Heralded the true start of England’s industrial revolution.
Made possible by coal and steel.
A Watt double-acting steam engine (1859)

## Slide 9
By 1800, coal was essential
Energy Systems & Sustainability, 2/e, Chapter 5
https://ragpickinghistory.co.uk/2012/10/04/meta-ornament-railway-tracks/
Over the next 100 years coal’s role expanded to include:
Powering ships;
Driving railways;
Lighting cities; and
Providing feedstock for synthetic fertilizer and chemical production
By the 1800s coal was an essential commodity in England.
Coal powered mills;
Was essential for smelting & ironworks;
Was used in domestic heating.
1845

## Slide 10
Coal production in England
https://blogs-images.forbes.com/williampentland/files/2011/09/UK-Coal-History2.jpg
1900
UK & US: 300 Mtonnes
Germany: 100 Mtonnes
Global: 1 billion tonnes
1/3 exported

## Slide 11
4. Coal
  4.3: Formation & composition

## Slide 12
Chemical composition of coal
Energy Systems & Sustainability, 2/e, Chapter 5; pmfias.com
organics
partially
decompose
peat
heat, pressure & time
coal (older is better)

## Slide 13
Chemical composition of coal
Energy Systems & Sustainability, 2/e, Chapter 5
Proximate analysis: Quality of coal increases with increasing carbon content.
Elements:
C
H
N
S
O
smokeless fuel
coke / steam
coke
steam

## Slide 14
Combustion of coal
Energy Systems & Sustainability, 2/e, Chapter 5
Water is heated & evaporated using a tiny fraction of coal’s energy.
smokeless fuel
coke / steam
coke
steam
increasing temperature
Volatile matter (hydrocarbons) are boiled off into gases: H2, CO, CH4, C2H4, C2H2.
The gases combust, releasing heat.
Fixed carbon (coke) combines with oxygen to produce carbon dioxide flue gases (emissions) and heat.
Ash remains: silicates & oxides of iron & aluminum.

## Slide 15
Why does coal produce more CO2?
https://www.wou.edu/las/physci/GS361/Energy_From_Fossil_Fuels.htm
smokeless fuel
coke / steam
coke
steam
increasing temperature
The higher the C:H ratio of fuels, the more carbon dioxide they produce.
Coal is often referred to as a dirty fuel because of its emissions.
And it’s said to produce more carbon dioxide than other fossil fuels. Why?
fuel | C:H ratio | Energy (MJ/kg) | CO2 (mol/MJ)
coal | 1:1 | 39.3 | 2.0
oil | 2:1 | 43.6 | 1.6
ethanol | 3:1 | 27.3 | 1.6
natural gas | 4:1 | 51.6 | 1.2
hydrogen gas | 100% H | 120.0 | 0

## Slide 16
4. Coal
  4.4: Coal deposits, reserves & production

## Slide 17
US coal deposits
Energy Systems & Sustainability, 2/e, Chapter 5
Higher grade:
Hard coal
Black coal
Anthracite
Bituminous
Lower grade:
Brown coal
Lignite
Sub-bituminous

## Slide 18
Global coal reserves & production
Energy Systems & Sustainability, 2/e, Chapter 5
Reserves
Production

## Slide 19
Global coal R/P ratios (2006)
Energy Systems & Sustainability, 2/e, Chapter 5
China’s R/P 38 y
India importing
Russia: coal displaced by NG
Australia exporting
UK mines down from 3000 to 13

## Slide 20
Some countries are well past peak
https://www.researchgate.net/profile/Kjell_Aleklett/publication/228838239/figure/fig1/AS:300666963677184@1448695998872/Figure-1-The-peaking-of-several-countries-with-a-long-history-of-coal-mining-The-two.png
A Watt double-acting steam engine (1859)
Figure 5.4
In fact, some have nearly null R/P ratios.

## Slide 21
4. Coal
  4.5: Modern coal extraction methods & current uses

## Slide 22
Mining automation: pit mines
Energy Systems & Sustainability, 2/e, Chapter 5
Automation has changed pit mining dramatically over the past 70 years.
Fewer workers.
More production.
Washington DNR
UK, 1953
Today’s pit mine

## Slide 23
Mining automation: open mines
Energy Systems & Sustainability, 2/e, Chapter 5
Bagger 288 bucketwheel excavator is used to remove overburden.
Weighs 13,500 tonnes
Moves 240,000 cubic meters per day
A Watt double-acting steam engine (1859)
Washington DNR

## Slide 24
Deep mining
Energy Systems & Sustainability, 2/e, Chapter 5
Deep (aka underground) mines, use shafts & tunnels up to 1000 m deep.
The longwall method is still used, exposing a long, horizontal surface of a coal seam.
Now very mechanized, using huge cutting loaders and long conveyer belts to carry the coal for transport out of the mine.
A Watt double-acting steam engine (1859)
Advantages & disadvantages?
Able to access deep deposits of coal.
Environmental impacts:
  land subsidence;
  Toxic tailing piles & sludge;
Health impacts:
  Black lung; &
  Accidents (Today in the US 1/50 lifetime risk for miners)
Washington DNR
msha.gov

## Slide 25
Surface (strip) mining
Energy Systems & Sustainability, 2/e, Chapter 5
Surface mines, aka open cast mines, aka strip mining
The surface (aka ‘overburden’) is removed first to get to the coal beneath it. Explosives & mechanical methods are used.
Mountain top removal is an extreme form of strip mining.
A Watt double-acting steam engine (1859)
Advantages & disadvantages?
Relative to deep mining:
  Simpler;
  Less expensive, so more efficient;
  Safer for miners.
However, the environmental effects of surface mining are extreme.
  Laws sometimes require rehabilitation of closed mines, but are not always completely enforced.
In 2008-9, 70% of US coal & 60% of UK coal was strip-mined.
Washington DNR

## Slide 26
Current uses of coal
Energy Systems & Sustainability, 2/e, Chapter 5
As of 2008, two-thirds of global coal was used for producing electricity.
In the UK, 80%.
A Watt double-acting steam engine (1859)
Coke is still used for smelting and steel production.
Global coke use was 800 million tonnes in 2009.
Nearly half of coke was used in China.
To avoid transporting bulky coal from mines to distant population centers, electric generating plants are often located near mines and electricity is transmitted to urban centers: ‘coal by wire’.
2-6% losses.
As of 2017, coal is used to produce <31% of electricity.

## Slide 27
4. Coal
  4.6: Global coal resources & reserves

## Slide 28
Global coal deposits (2009)
Energy Systems & Sustainability, 2/e, Chapter 5
Coal is found on every continent except Antarctica.
A Watt double-acting steam engine (1859)
Hard coal has 1.5 times as much energy as lignite.

## Slide 29
Global reserves & deposits (2010)
Energy Systems & Sustainability, 2/e, Chapter 5
Note that areas of highest production are not the areas with the largest reserves.
A Watt double-acting steam engine (1859)
Coal reserves
Coal production

## Slide 30
Global reserves & R/P ratios (2009)
Energy Systems & Sustainability, 2/e, Chapter 5
A Watt double-acting steam engine (1859)

## Slide 31
Coal in the US
Energy Systems & Sustainability, 2/e, Chapter 5
A Watt double-acting steam engine (1859)
The US has 25% of global coal reserves.
R/P of 245 years
Eastern coal
  Deep pits
  High-quality coking coal
Western coal
  Surface mined
  Sub-bituminous, so low heat content
  Must be transported to areas with high need, increasing cost

## Slide 32
Coal in China
Energy Systems & Sustainability, 2/e, Chapter 5
A Watt double-acting steam engine (1859)
Use of coal in China has been expanding rapidly, but…
R/P of 38 years
Coal is found in the north & west, but need is in the south & east.
  Transported by truck and rail
Nearly all mines are deep pits.
  Poor safety: 5,00o deaths in the 1990s
  10X worse than the UK
  Uncontrolled underground mine fires occur.
Chinese coal has > 5% sulfur.
  Acid rain is a problem in many cities

## Slide 33
Coal elsewhere
Energy Systems & Sustainability, 2/e, Chapter 5
A Watt double-acting steam engine (1859)
Russia
R/P of >500 years
But production has fallen because of abundant NG
  Coal in Siberia can be considered a conditional reserve.
India
4th largest reserves
R/P of 105 years
Poor quality: low heat content & high ash
  Imports high-quality coal from Australia
Australia
Less than 10% of global reserves
R/P of 186 years
Surface mines are located near railways to cities of need.
Australia’s largest export:
  40% to Japan
  Coking coal to Europe
  Middle East, Asia (India, China)

## Slide 34
Reserves & R/P ratios can change…
Energy Systems & Sustainability, 2/e, Chapter 5
A Watt double-acting steam engine (1859)
previously unknown
Resources: deposits likely to exist
Conditional resources: deposits that are not now reserves because their extraction isn’t economically or politically feasible now
Reserves: deposits that can be economically extracted now
McKelvey diagram
…as technology and economic conditions change.

## Slide 35
4. Coal
  4.7: Combustion of coal & emissions

## Slide 36
Combustion
Energy Systems & Sustainability, 2/e, Chapter 5
Moisture evaporates in the first stages of combustion.
A Watt double-acting steam engine (1859)
Volatile matter is turned to gas like CO, CH4 and other hydrocarbons.
These gases combust to create heat.
Fixed carbon combines with oxygen gas to produce carbon dioxide flue gas.
Ash is any material that remains.
Best quality coal has ~10% ash.
Lower quality may produce 15-30%.

## Slide 37
Combustion: newer technologies
Energy Systems & Sustainability, 2/e, Chapter 5
Pulverized fuel boilers create a fine carbon powder that is blown into the combustion chamber with air.
90% efficient
Problem: fine fly ash in flue gases.
A Watt double-acting steam engine (1859)
Fluidized bed boilers combust small coal particles in a bed of sand. ‘Bubbles’ of coal and air heat the entire bed.
Very efficient
Lower combustion temps, so less NOx

## Slide 38
Combustion flue gases
Energy Systems & Sustainability, 2/e, Chapter 5
Emissions: NOx, CO2, H2O, SOx, fly ash & particulates
A Watt double-acting steam engine (1859)
Coal’s challenges?
Hot, dirty & corrosive
Volume: 3000 tonnes/hour!
Very high levels of:
  Moisture
  SOx; &
  Particulates
Wyoming Public Media

## Slide 39
Making emissions real
Energy Systems & Sustainability, 2/e, Chapter 5
Let’s look at some numbers to bring home the scale of emissions from coal-fired power plants.
A Watt double-acting steam engine (1859)
A power plant burns 250 tonnes of coal per hour to produce 500 MW.
Emission | tonnes | problem?
N2 (from air for combustion) | 2000 | little harm
CO2 | 650 | GHG !
Steam (H2O) | 150 | harmless (energy loss)
NOx | 1 | acid-rain, health
SOx | 1 - 20 | acid-rain, health
Fly ash | 20 | health
Mercury vapor | 30 g | health

## Slide 40
Lowering SOx
Energy Systems & Sustainability, 2/e, Ch 5
SOx can be reduced by using limestone (CaCO3) or seawater to precipitate the 90-95% of sulfur out of the flue gases.
CaCO3 + SO2  CaSO3/4 + CO2

## Slide 41
Lowering NOx
Energy Systems & Sustainability, 2/e, Chapter 5
NOx can be reduced by:
Decreasing combustion temperatures (a la fluidized bed);
Selective catalytic reduction (removal of O from N); or
Gas reburn via added natural gas to remove oxygen.
A Watt double-acting steam engine (1859)
4NH3 + 6NO  5N2 + 6H2O
W (tungsten) or V (vanadium) catalyst

## Slide 42
Lowering particulates and ash
Energy Systems & Sustainability, 2/e, Chapter 5; wikipedia
Particulates and ash can be reduced using:
Cyclone;
Bag filter; or
Electrostatic precipitator:
A Watt double-acting steam engine (1859)
Disposing of the ash?
Ash is toxic because of metal contaminants.
Landfill; or
Use as a ‘filler’ in concrete where toxins are fixed.
Particles are ionized (charged) & then attracted to charged filters / plates.

## Slide 43
4. Coal
  4.8: Alternative uses of coal

## Slide 44
Gasification to syngas
Energy.gov
Gasification converts hydrocarbons like coal into gases using heat, pressure and steam. Oxygen levels are controlled to prevent combustion.
A Watt double-acting steam engine (1859)
Wyoming Public Media
Syngas:
CO & H2

## Slide 45
Gasification to syngas
Energy.gov
Integrated gasification combined-cycle:
Cleaned syngas is combusted to drive a combustion turbine that drives a generator;
Exhaust heat is used to create steam, to drive a second steam turbine-generator.
Combined turbines generate electricity very efficiently: 40%
A Watt double-acting steam engine (1859)
Wyoming Public Media
Other uses of syngas?
Chemical building blocks for the chemical industries
Fuel for fuel-cell systems
Source of hydrogen
Compatible with carbon capture & storage
If oxygen is used in place of air, carbon dioxide is produced in a concentrated stream that is easier to capture and sequester.

## Slide 46
Gasification products & co-products
A Watt double-acting steam engine (1859)
Wyoming Public Media
Energy Systems & Sustainability, 2/e, Chapter 5

## Slide 47
Underground coal gasification
Energy Systems & Sustainability, 2/e, Chapter 5
Uses conventional gasification technology, put performed underground.
Wyoming Public Media
Air & water are injected into the coal seam;
Ignited under low-oxygen conditions to partially oxidize coal into:
  H2, CO, CO2, CH4, H2S
  Gases piped to the surface for combustion.
The UK will not use this technology because its CO2 emissions are significantly higher than those from NG.

## Slide 48
4. Coal
  4.9: Carbon sequestration & clean coal

## Slide 49
Carbon sequestration
Energy Systems & Sustainability, 2/e, Chapter 5; US Carbon Sequestration Program, US DOE
Sequestration ties up carbon to keep it out of the atmosphere.
A Watt double-acting steam engine (1859)
Wyoming Public Media
Biological sequestration is natural.
Can we engineer sequestration?

## Slide 50
Dirty coal, clean future (Fallows)
https://www.theatlantic.com/magazine/archive/2010/12/dirty-coal-clean-future/308307/
A Watt double-acting steam engine (1859)
Wyoming Public Media