## Slide 1
SSC 2030: Energy Systems and Sustainability
5. Oil and natural gas
5.1: Origins and geology of petroleum and its industry
5.2: Case study - rise and fall of North Sea oil and gas
5.3: Why are oil and gas so special?
5.4: Finding and producing petroleum
5.5: Petroleum refining and products
5.6: Oil consumption and production today
5.7: Natural gas
5.8: Methane leaks and GCC
5.9: Unconventional oil and gas
5.10: Methyl hydrates (clathrates)
5.11: Petroleum’s future?

## Slide 2
Module 5. Oil and gas
  5.1: Origins and geology of petroleum
  and today’s oil and gas industry

## Slide 3
Introduction to oil and gas
Petroleum: all hydrocarbons deposited in the Earth’s crust
Crude oil (liquid)
Natural gas (gaseous)
Bitumens (coal; solids)
Energy Systems and Sustainability, 2/e, Chapter 7
Formed by decomposition of marine organics followed by time, heat and pressure. (Coal + more time and pressure?)
Abundant where marine strata accumulated.
Traps: geologic formations where hydrocarbons accumulate
Geologic traps: porous, permeable reservoir rock; high pressure
Structural traps: anticline, fault trap, salt dome

## Slide 4
Use of ‘surface’ petroleum is ancient
Early use of petroleum depended on easy access:
Surface seepage; or
Topographical features allowing easy access.
Energy Systems and Sustainability, 2/e, Chapter 7
Oil seep in CA after Northridge
earthquake (USGS)
Petroleum’s many ancient uses
From the Babylonians onward, surface petroleum was used as a lamp fuel, an adhesive, for caulking boats, medicines and … myriad other uses

## Slide 5
Modern use started with lighting
In the 1800s, coal gas was used to light cities, but was not available outside of cities.
Energy Systems and Sustainability, 2/e, Chapter 7
In 1850, Scottish chemist James ‘Paraffin’ Young patented the distillation of coal oil and paraffin wax from coal.
Coal oil became a popular lighting and lubricating oil.
In 1859, Edwin Drake ‘hit’ oil in Titusville PA.
Early uses focused on distillation of lighting oil.
Within 40 years, uses were soon found for all fractions produced by distillation of crude oil.
coal
oil

## Slide 6
... And quickly dominated transportation
The energy density and liquid state of heavy and light fractions of petroleum made it an attractive alternative to coal for transportation.
Energy Systems and Sustainability, 2/e, Chapter 7
1903: The Wright brothers’ first flight was fueled with gasoline.
1908: British navy used oil-fired steam turbines for its lightest and fastest ships.
1890: The Diesel engine developed for peanut oil, but was able to use petroleum.
1930: Half of all global shipping was powered by oil.
After 1950: Diesel engines replace steam turbines in shipping.
1970s: international conflicts increase price and decrease global supply of petroleum.
Nonetheless, the world becomes firmly addicted to petroleum

## Slide 7
The natural gas industry
Natural gas can be found associated with oil or non-associated
The latter may have developed from fresh-water plant material.
Energy Systems and Sustainability, 2/e, Chapter 7
https://www.bp.com/content/dam/bp/business-sites/en/global/corporate/pdfs/energy-economics/statistical-review/bp-stats-review-2019-full-report.pdf
Natural gas is often contaminated with water, condensate or natural gas liquids.
Condensate is a light oil (C5H12).
Natural gas liquids are lighter hydrocarbons like propane (C3H8) & butane (C4H10).
  Liquified using high pressure and sold as liquid petroleum gas (LPG).
Until recently, NG was flared (burned off) as a waste.
1920s: NG used in US as heating and power station fuel.
Post-WWII Europe: transformed energy economies came to rely on NG
Russia supplies Europe by with NG by pipeline.
2020: NG = 23.8% of global primary energy
    40% of UK primary energy

## Slide 8
5. Oil & gas
  5.2: Case study - North Sea oil and gas
Module 5. Oil and gas

## Slide 9
Oil and gas are finite
Energy Systems and Sustainability, 2/e, Chapter 7
North Sea oil and gas have benefitted the UK, Norway, Denmark and the Netherlands.
But the benefit won’t last…
1969
1975
2000

## Slide 10
Timeline of UK production
Energy Systems and Sustainability, 2/e, Chapter 7
Large-scale production began in 1975 and provided a cushion from oil crisis of 1970s.
Plateau 1983 – 2000
Piper Alpha 167 dead
Production is now declining at a rate of 7% per year.
Piper Alpha
167 dead

## Slide 11
Norway’s approach to a finite resource
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Government_Pension_Fund_of_Norway#/media/File:Norway_Oil_Fund.png
The UK aggressively produced North Sea oil and gas. UK governments used the revenue to keep non-oil taxes down, arguing that this would grow the UK economy.
Norway’s approach was different. Oil changed Norway’s economy radically; oil was a relatively larger boon to Norway. But Norway called it ‘Oljeeventyr’, the oil fairy tale, and saw it as a fleeting source of wealth.
In 1974, Norway decided to use oil money to develop a "qualitatively better society”.
Domestic control of oil;
Oil revenue invested in a sovereign wealth fund now worth >$1 billion;
Only 4% of surplus from this investment is spent for the public good.

## Slide 12
Module 5. Oil and gas
  5.3: Why are oil and gas so special?

## Slide 13
High energy density and a ‘clean’ burn
Why have oil and gas become such dominant forms of primary energy?
High energy density
Cleaner burning than coal (less CO2/energy unit)
Ease of transport and use (universal infrastructure)
Abundant and cheap
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 14
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Energy_returned_on_energy_invested
Energy return on energy investment (EROEI): a measure of how much energy a fuel will produce vs the amount of energy it took to create that fuel, from harvest through processing (and sometimes distribution)
EROEI = __________energy delivered________
energy required to deliver the energy
EROEI
fossil fuel | EROEI | EROEI 2020*
coal | 80 | 6 - 8
oil | 12 - 35 | 
NG | 10 | 
shale oil | 5 | 
tar sands | 3 | 

## Slide 15
Energy Systems and Sustainability, 2/e, Chapter 7; http://euanmearns.com/eroei-for-beginners/; Prieto and Hall
In essence, EROEI balances the cost of producing energy with its benefits.
Factors affecting EROEI

## Slide 16
Energy Systems and Sustainability, 2/e, Chapter 7; http://euanmearns.com/eroei-for-beginners/
Will we fall off the energy cliff?

## Slide 17
Energy Systems and Sustainability, 2/e, Chapter 7; http://euanmearns.com/eroei-for-beginners/
Net energy cliff hypothesis contends that when EROEI falls too low, energy costs too much relative to the benefits it provides society.
EROEI energy cliff?

## Slide 18
LCOE: US projections
https://www.eia.gov/outlooks/aeo/pdf/electricity_generation.pdf

## Slide 19
Module 5. Oil and gas
  5.4: Finding and producing petroleum

## Slide 20
Oil prospecting
Modern survey methods make drilling the last step.
Energy Systems and Sustainability, 2/e, Chapter 7
Gravimetric survey:
oil-bearing rock is less dense than most rock
Geomagnetic survey:
looks for variation in magnetic field.
Sedimentary rock is iron-poor and not magnetic.
Seismic survey:
reflection and refraction of waves may reveal pockets of oil

## Slide 21
Oil wells
Wells as deep as 4500 m are possible depending on geology.
If the initial well finds oil, more
appraisal wells are drilled to assess the size and shape of the deposit or oil field.
Finally, production wells are drilled used to extract maximum amounts of oil.
Deviation wells can be drilled from a single platform to extract oil from a larger area.
Used in the North Sea
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 22
Offshore oil well technology
Energy Systems and Sustainability, 2/e, Chapter 7
After depleting easily harvested oil, we’ve developed technology that allows us to drill for oil in more challenging conditions.
“Necessity is the mother of invention.”

## Slide 23
The three ‘Ps’ of the oil and gas industry
Energy Systems and Sustainability, 2/e, Chapter 7
Oil and gas exploration is a form of informed gambling.
How lucky to you feel?
1P = 90%
2P = 50%
3P = 10%

## Slide 24
Oil production
Energy Systems and Sustainability, 2/e, Chapter 7
Primary recovery: pumping oil from freshly drilled and capped wells
Initial high well pressure makes this simple.
Secondary recovery: becomes necessary after well pressure falls
Pressure is increased by pumping in NG or water.
Secondary recovery may be very slow.
Saudi Arabia pumps seawater across the desert.
30 – 50%
recovery
Tertiary recovery (aka enhanced oil recovery): more extreme
Injecting steam
Injecting CO2 or N2
Energy intensive & slow
5 – 15%
recovery

## Slide 25
Module 5. Oil and gas
  5.5: Oil refining and products

## Slide 26
What is crude oil?
Energy Systems and Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Petroleum
Crude oil: a mixture of hydrocarbon molecules, of varying carbon number (chain length) and structure
element | % by mass
C | 83 - 85
H | 10 - 14
N | 0.1 - 2
O | 0.05 – 1.5
S | 0.05 - 6
metals | <0.1
hydrocarbon | average % | range %
alkanes | 30 | 15 - 60
naphthenes | 49 | 30 - 60
aromatics | 15 | 3 - 30
asphaltics | 6 | remainder
Properties like color, density, viscosity, heat value vary greatly depending on composition.
S content may be regulated by governments because it leads to pollution.

## Slide 27
Products of crude oil
Energy Systems & Sustainability, 2/e, Chapter 7
Useful products can be created from crude oil by separating and transforming oil molecules by the process of fractional distillation, based on boiling points.
distilled fraction | boiling range (°C)
liquid petroleum gas | - 40
butane | - 12 - -1
Gasoline (octane) | -1 - 110
jet fuel | 150 - 205
kerosene | 205 - 260
fuel oil | 205 - 290
diesel fuel | 260 - 315
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Petroleum
alkane | formula | boiling point (°C) | heat value (MJ/kg)
methane | CH4 | -162 | 55.5
ethane | C2H6 | -89 | 51.9
propane | C3H8 | -42 | 50.4
butane | C4H10 | -0.5 | 49.5
octane | C8H18 | 125 | 47.1
Light: crude with large amounts of light molecules (gases)
Sweet: low levels of sulfur

## Slide 28
Oil refining: fractional distillation
Energy Systems and Sustainability, 2/e, Chapter 7
Fractionation (aka cracking): a process that breaks long hydrocarbon chains down into smaller chains that are then separated by fractional distillation.
The process uses:
Heat;
steam; and/or
catalysts.
Lighter molecules separate at lower temperatures.
Light: gas; jet fuel; kerosene
Middle: diesel; heating oil
Heavy: semi-solid; heavy diesel

## Slide 29
The many uses of oil
Energy Systems and Sustainability, 2/e, Chapter 7
natural gas and energy gases
aviation fuel
vehicle fuel
petrochemical feedstock
industrial solvent
paint thinner
dry cleaner
lamps
heating stoves
ship’s fuel
power station fuel
lubricating oil
waxes
bitumen
petroleum coke for graphite
transportation
electricity

## Slide 30
Module 5. Oil and gas
  5.6: Oil consumption and production today

## Slide 31
Quick review of units of oil production
Energy Systems and Sustainability, 2/e, Chapter 7
1 metric tonne = 7.3 barrels = 42 GJ
1 million barrels per day (bpd) = 0.365 billion barrels / year
= 50 million tonne / year
= 2.1 EJ / year
= 2 quads / year
Global oil use in 2019: 100 million barrels per day

## Slide 32
Geographical distribution of petroleum resources

## Slide 33
Geographical distribution of petroleum resources

## Slide 34
Geographical distribution of petroleum reserves

## Slide 35
R/P ratios for oil
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html
Even with up-to-date data, R/P ratios for oil are low in North America, Europe and Asia.
years

## Slide 36
Global oil demand (consumption)
https://www.iea.org/reports/oil-information-overview

## Slide 37
Global oil consumption (GJ/capita)
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html

## Slide 38
Global oil production
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html
million barrels/day
Note the apparent leveling off of production even before COVID.
Sanctions
OPEC slowdowns to prevent price declines

## Slide 39
Global oil trading
million barrels/day
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html

## Slide 40
Refinery output growth
https://www.iea.org/reports/oil-information-overview

## Slide 41
Impacts of COVID? Demand in 2020 relative to 2019
https://www.iea.org/data-and-statistics/charts/change-in-monthly-oil-demand-in-selected-countries-2020-relative-to-2019

## Slide 42
Oil prices: recently volatile
https://www.iea.org/data-and-statistics/charts/change-in-monthly-oil-demand-in-selected-countries-2020-relative-to-2019

## Slide 43
US oil production: driven by technology
Energy Systems and Sustainability, 2/e, Chapter 7
Development of automobiles and planes spurred early growth.

## Slide 44
Peak oil will occur but is delayed
Energy Systems and Sustainability, 2/e, Chapter 7
Note that US production figures support Hubbert’s hypothesis.
Why is peak delayed?
Technology
Policy
Growth
Inertia

## Slide 45
US production appears to be defying peak?
Energy Systems and Sustainability, 2/e, Chapter 7
Many have noted that US oil production appears to be defying peak predictions.
While we can probably shift the timing of the peak extraction and conversion won’t make a finite resource endless.

## Slide 46
Example? Fracking boosted US oil production

## Slide 47
Revised fossil fuel reserves
Energy Systems and Sustainability, 2/e, Chapter 7
While reserves figures are revised upwards, only a tiny fraction is new discoveries.
Because fossil fuel reserves and revenues are critical to the stability of many governments, fossil fuels ‘data’ may be subject to political influence or revision.
Reserves = political stability

## Slide 48
Planning to move away from oil
http://money.cnn.com/2017/07/26/autos/countries-that-are-banning-gas-cars-for-electric/index.html
By 2017, several European countries have pledged to either:
Stop producing and selling petro fueled cars…
  India
  France
  Britain
  Norway
…or are planning to increase to percentage of electric cars in their fleet.
  Austria
  China
  Denmark
  Germany
  Ireland
  Japan
  the Netherlands
  Portugal
  Korea
  Spain

## Slide 49
Has peak use already passed?

## Slide 50
Module 5. Oil and gas
  5.7: Natural gas

## Slide 51
NG units
Energy Systems and Sustainability, 2/e, Chapter 7
UK units:
1 therm = 100,000 BTU = 29.3 kWh = 105.5 MJ = 2.7 m3 NG
US units:
1 MMBTU = 1,000,000 BTU = 293 kWh = 1.055 GJ = 27 m3 = 1E3 ft3 NG
International:
1000 m3 NG = 39 GJ = 10.8 MWh = 0.93 tonnes of oil
‘Roundly’:
1000 m3 NG = 40 GJ = 10 MWh = 1 tonnes of oil

## Slide 52
Processing NG: ‘scrubbing’ by-products
Energy Systems and Sustainability, 2/e, Chapter 7
Natural gas (CH4) is contaminated with other gases:
Ethane (C2H6)
He
H2S
CO2
plastics manufacturing
medical uses; superconducting magnets
S used in fertilizers
re-injected to flush more NG out of wells
NG with low levels of contaminants is called ‘sweet’.
These gases are ‘scrubbed’ out of NG using amine chemistry.

## Slide 53
Natural gas: ‘cleaner’ than oil and coal
Energy Systems and Sustainability, 2/e, Chapter 7
Natural gas is mostly methane (CH4) but contains small amounts of other hydrocarbon gases when extracted: ethane (2 carbons); propane (3 carbons); and butane (4 carbons).
CH4 + 2O2  CO2 + 2H2O
mass 16 64 44 36
CO2 = 44 = 2.75
fuel 16
Propane is (C3H8) and is separated from natural gas during processing.
C3H8 + 5O2  3CO2 + 4H2O
mass 44 160 132 72
CO2 = 132 = 3.0
fuel 44
It is often said that NG is a ‘cleaner’ fuel than oil or coal and produces less CO2.
Why & how?
Hydrogen ‘burns’ without producing CO2. The more hydrogen a fuel has, the less CO2 it produces.
So, to identify ‘clean’ fuels look for a high H:C ratio.

## Slide 54
NG: lower CO2 emissions
Natural gas has lower carbon dioxide emissions because of its high H:C ratio
Energy Systems and Sustainability, 2/e, Chapter 7; https://www.eia.gov/tools/faqs/faq.php?id=73&t=11
fossil fuel | H:C ratio | pounds CO2 / MBtu
coal (anthracite) | 0 – 0.3:1 | 228.6
coal (bituminous) | 0.8:1 | 205.7
coal (lignite) | 1:1 | 215.4
diesel fuel / heating fuel | 2.27:1 | 161.3
gasoline (no ethanol) | 2.25:1 | 157.2
propane | 2.67: 1 | 139.0
natural gas | 4:1 | 117.0

## Slide 55
Domestic condensing gas boilers
Energy Systems and Sustainability, 2/e, Chapter 7
Because NG burn cleanly, water vapor produced by combustion can be condensed allowing recovery of the latent heat of vaporization.
40°C return water cools flue gases below 50°C, increasing recovery of heat from the flue gases by 11%, the difference between HHV and LHV.
Increases boiler efficiency to >90%.

## Slide 56
Natural gas: a ‘recent’ fossil fuel
While the US started using NG in the 1920s, European countries did not.
In 1959, a huge non-associated NG field was discovered in the Netherlands; later, off-shore NG fields in the North Sea.
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/North_Sea#/media/File:Nseamap.gif
In the UK, conversion from coal gas to NG took a decade and cost £564 m.
Pricing lower than coal gas incentivized customers to switch.

## Slide 57
Lessons learned while switching fuels
Energy Systems and Sustainability, 2/e, Chapter 7; http://www2.nationalgrid.com/uploadedImages/Resources/Image_library/Maps/UK%20Transmission%20maps.jpg
In the UK, conversion from coal gas to NG took a decade and cost £564 m.
NG has 2X the energy content of coal gas; retrofitting was needed.
  13 m customers
  40 m appliances
2007: 92% of homes have central heat
  75% are heated with NG
Pricing NG lower than coal gas incentivized the switch.
2000: 40% of electricity from NG
  Generated with CCGTs
To meet peak winter demands, 3% of annual NG demand is stored by injection into depleted offshore wells
  Some large users have interruptible contracts and have secondary energy

## Slide 58
Global geographical distribution of NG
https://www.worldenergy.org/assets/images/imported/2016/10/World-Energy-Resources-Full-report-2016.10.03.pdf

## Slide 59
NG reserves: a point of friction for Qatar and Iran
https://www.aljazeera.com/indepth/interactive/2017/06/qatar-north-dome-iran-south-pars-glance-lng-gas-field-170614131849685.html
https://www.haaretz.com/middle-east-news/the-qatar-iran-gas-field-behind-the-diplomatic-war-in-the-middle-east-1.5480343
”The Qatar-Iran Gas Field Behind the Diplomatic War in the Middle East.”
Qatargas, the world's largest exporter of liquefied natural gas, reassures Japan, the world's largest importer, that Gulf state rift will not effect supply…”

## Slide 60
Global NG consumption
https://www.iea.org/fuels-and-technologies/gas

## Slide 61
Global NG consumption (GJ/capita)
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html

## Slide 62
Global NG production
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html
billion m3
Production is up.
US
Asia
  Australia
  China
  Middle East

## Slide 63
2018 was a record year for NG – forecast?
https://www.iea.org/fuels-and-technologies/gas
Sustainable planning
forecast
NG use increased 4.6% in 2018
½ of new energy demand
US: fracking
China: economic growth
Middle East: diversification

## Slide 64
While valuable, much NG is flared and wasted
Flaring and waste drop here in sustainable development scenarios
https://www.iea.org/fuels-and-technologies/gas
Why flare it?
Difficult (ie expensive) to:
  capture
  Store
  Transport
Technology fix needed
No penalty
But GCC requires a fix

## Slide 65
COVID dramatically decreased NG use
https://www.iea.org/fuels-and-technologies/gas

## Slide 66
US NG prices have fallen: recession and supply
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html
$/MMBtu

## Slide 67
R/P ratios for NG
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html

## Slide 68
Transporting NG? Pipelines
Energy Systems and Sustaiability, 2/e, Chapter 7
High-pressure pipeline transports natural gas from NG storage depots to communities and industries.
Pipelines can transport the equivalent of gigawatts of power.

## Slide 69
Transporting NG? LNG
Energy Systems and Sustainability, 2/e, Chapter 7
LNG, liquified natural gas, is produced by compressing natural gas. Increased energy density allows economical long-distance transportation.

## Slide 70
Europe is now dependent on NG
Energy Systems and Sustainability, 2/e, Chapter 7
Russia exports NG to Europe from Siberia through long pipelines.
Note that NG from Russia must cross Ukraine & Belarus.
Pipeline pressure is boosted by in-pipe gas turbines powered by adding O2.
Europe’s energy security is not boosted.

## Slide 71
And NG trade is global
https://www.bp.com/en/global/corporate/energy-economics/statistical-review-of-world-energy/natural-gas.html

## Slide 72
Module 5. Oil and gas
  5.8: Methane leaks and GCC

## Slide 73
Methane’s global warming potential
A number of atmospheric gases have global warming potentials (GWP): can hold heat in the earth’s atmosphere. GWP values are measured relative carbon dioxide (CO2), given an arbitrary GWP of one.
  CO2 has an atmospheric lifetime of thousands of years.
https://www.epa.gov/ghgemissions/understanding-global-warming-potentials#Learn%20why
Methane (CH4; natural gas) has a much higher GWP than CO2.
CH4 has a shorter atmospheric lifespan, about 10 years.
But CH4 absorbs much more energy than CO2.
And methane is converted into ozone, also a GHG.
Over a 100-year period, methane’s GWP is 28 - 36 20-year 84 - 87

## Slide 74
Perspective: methane as a GWP
Methane is a significant contributor to annual global carbon emissions.

## Slide 75
Methane emissions rising even as CO2 may peak
“Global emissions of methane, a potent greenhouse gas, soared to a record high in 2017”, our most recent data
https://www.nytimes.com/2020/07/14/climate/methane-emissions-record.html?auth=login-email&login=email
Methane emissions are driven by fossil fuel leaks and agriculture.
“There’s a hint that we might be able to reach peak carbon dioxide emissions very soon. But we don’t appear to be even close to peak methane,” said Rob Jackson, an earth scientist at Stanford University who heads the Global Carbon Project, which conducted the research. “It isn’t going down in agriculture it isn’t going down with fossil fuel use.”
Global methane emissions are up 9 percent from the early 2000s
  Human activity is responsible for >50% those emissions.

## Slide 76
Satellite detection of methane emissions
Harvesting fossil fuels releases methane into the atmosphere as leaks.
https://www.nasa.gov/feature/jpl/nasa-led-study-solves-a-methane-puzzle
https://www.nasa.gov/press/2014/october/satellite-data-shows-us-methane-hot-spot-bigger-than-expected
Satellite imaging is essential for finding and resolving leaks.
The four-corners CH4 hotspot is due to poor recovery of coal-seam methane.
2,500 mi2
½ CT
released 0.59 tonne/year

## Slide 77
Methane storage leaks
Methane leak from underground NG storage facility in southern CA.
https://earthobservatory.nasa.gov/images/88245/imaging-a-methane-leak-from-space

## Slide 78
Methane storage leaks
https://www.nytimes.com/interactive/2019/12/12/climate/texas-methane-super-emitters.html?action=click&module=RelatedLinks&pgtype=Article

## Slide 79
Methane fracking leaks
Road monitoring of methane levels finds leaks from the ground.
https://news.psu.edu/photo/338850/2014/12/17/methanemapbarkley
NG compressor station
NG wells

## Slide 80
Ocean methane hydrates melting?
Methane hydrates lie frozen deep in the oceans.
http://arctic-news.blogspot.com/2012/05/striking-increase-of-methane-in-arctic.html
But as the ocean’s warm hydrates seem to be melting and releasing methane; correlation with warming temperatures!

## Slide 81
Permafrost methane … also leaking
The permafrost is a thick subsurface layer of soil that remains frozen throughout the year, occurring chiefly in polar regions.
https://www.nytimes.com/2011/12/17/science/earth/warming-arctic-permafrost-fuels-climate-change-worries.html
It’s estimated that the permafrost contains twice the carbon now in the atmosphere.
Warming temperatures could cause permafrost to release 15-33% of current carbon emissions.

## Slide 82
Undersea methane leaks
A July 2020 study has found cracks in huge craters under the Barents sea ‘gushing’ methane into sea water. This is an old fault system.
Study raises many questions:
Destabilized by drilling?
Will large amounts of methane be released to the atmosphere?
Effects on GCC?
https://www.nature.com/articles/s41598-020-65018-9

## Slide 83
5. Oil & gas
  5.9: Unconventional oil and gas
Module 5. Oil and gas

## Slide 84
Heavy and extra-heavy oil
Energy Systems and Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Orinoco_Belt#/media/File:Orinoco_USGS.jpg
Oil that is so thick and viscous that it will not flow to the surface without injection of steam into the well to heat the oil and add enough pressure to force it to the surface.
Venezuela’s Orinoco basin has 500 billion barrels of reserve of heavy oil, more oil than Saudi Arabia.
High levels of S.
Difficult to harvest and refine.

## Slide 85
Shale oil
Energy Systems and Sustainability, 2/e, Chapter 7; https://slowair.wordpress.com/category/experiments-research/
Shale oil: an ‘immature’ hydrocarbon trapped or embedded in rock as a waxy substance called kerogen.
Energy content of raw shale oil = 5 – 15 GJ/tonne (like poor lignite).
Shale oil was produced commercially in Scotland (1880 – 1940), Estonia (1920s – present), China and Brazil.
Shale oil ‘bings’ (Scotland)
Concerns?
Environmental: the extraction process expands the volume of the rock, creating huge ‘bings’.
EROI is poor: 2.5 - > 10

## Slide 86
Oil sands or tar sands
Energy Systems & Sustainability, 2/e, Chapter 7;
https://infograph.venngage.com/p/232326/oil-sands
Oil sands (aka tar sands): mature bitumens binding together loose rock
Easier recovery than shale oil.
Huge reserves of 27 billion tonnes in the Athabasca (northern Alberta)
  16 billion tonnes can be surface mined.
  2007 production was 75 million tonnes.

## Slide 87
Tar sands extraction
Up to 90% recovery of bitumen
Energy Systems & Sustainability, 2/e, Chapter 7;
https://infograph.venngage.com/p/232326/oil-sands

## Slide 88
Tar sands challenges and costs
Energy Systems & Sustainability, 2/e, Chapter 7;
https://en.wikipedia.org/wiki/Oil_sands
https://insideclimatenews.org/news/22022017/exxon-mobil-tar-sands-alberta-canada-climate-change-oil-prices
Tar sands extraction has significant challenges and costs.
Huge requirement for clean water use:
~ 500 – 1000 gallons / tonne of bitumen
High energy inputs of heat and steam the remove bitumen from the rock:
Energy input: 1 – 1.25 GJ / barrel of bitumen
Energy return: 6.12 GJ / barrel of bitumen
Mainly from NG
EROI ~ 5-6
Low cost of oil (2017)
Exxon ‘delisted’ 3.5 billion barrels of tar sands oil in Canada in 2017.
Environmental destruction

## Slide 89
Tar sands: environmental changes
Energy Systems & Sustainability, 2/e, Chapter 7;
http://e360.yale.edu/features/on_ravaged_tar_sands_lands_big_challenges_for_reclamation
Following tar sands extraction, reclamation must create ecosystems on stripped lands. As of 2014, reclamation focused on ecosystems that could cope with the salts, metals and acids released by tar sands operations.
Shrub land marshes
Upland forests
Much of the Athabasca land mined for tar sands was a complex, boreal forest or peatland fens ecosystem (50% of land area) that sequestered a great deal of CO2.
At 54,000 square miles mining could release 11.4 – 47.3 million tonnes of CO2.
These reclaimed ecosystems are less complex and sequester less.
- 7.2 million tonnes CO2 / year
Biodiversity has been reduced.
Massive use of Athbasca River water and contamination with tar sands chemicals.

## Slide 90
Hydraulic fracturing – now conventional
Energy Systems and Sustainability, 2/e, Chapter 7
Fracking allows production of tight gas trapped in sandstone and shale gas trapped in shale formations.

## Slide 91
Costs of fracking?
Energy Systems & Sustainability, 2/e, Chapter 7
https://news.yale.edu/2016/01/06/toxins-found-fracking-fluids-and-wastewater-study-shows
http://www.pbs.org/newshour/rundown/earthquakes-triggered-by-fracking/
In order to pressurize fracking wells and force out gas, fracking fluids are pumped into the wells at high pressure.
Scientists at Yale analyzed over 1000 chemicals found in fracking fluid.
  Good data on 240 showed that 157 are associated with developmental or reproductive toxicity.
    67 were already chemicals of concern.
    Included: arsenic, benzene, cadmium, lead, formaldehyde, chlorine, and mercury
Fracking chemicals often enter groundwater when fractures extend from gas wells into water-bearing rock.
This contaminates drinking water supplies.
Earthquakes are caused by:
The fracking process itself; and
Injection of fracking fluid waste into deep wells.

## Slide 92
Some have banned fracking
Energy Systems and Sustainability, 2/e, Chapter 7
A number of countries and states have banned fracking:
Scotland
Ireland
France
The Netherlands
Germany
Tunisia
Vermont
New York
Maryland
Quebec

## Slide 93
Fracking (et al.) will extend oil production
Energy Systems and Sustainability, 2/e, Chapter 7
Fracking technology is allowing us to extract oil not previously seen as reserves.
Redefining resources vs. reserves.

## Slide 94
The impact of fracking is huge
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 95
US NG reserves and production are up
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 96
US NG export is booming
Energy Systems and Sustainability, 2/e, Chapter 7
…to Canada & Mexico

## Slide 97
Are unconventional sources the answer?
Energy Systems and Sustainability, 2/e, Chapter 7
Let’s look at some numbers:
Canadian oil sands: 4.6 million barrels per day
Venezuelan extra heavy oil: 2.3 million barrels per day
World shale oil: 0.5 million barrels per day
11% current world oil production
Unconventional sources of petro-fuels appear to be extending – or postponing – peak oil, but these sources are also finite.

## Slide 98
Reserves of unconventional fossil fuels
Energy Systems and Sustainability, 2/e, Chapter 7
Increasingly, our reserves of petro-fuels will trend ‘unconventional’.

## Slide 99
Summary: oil and gas
Upsides:
Relatively inexpensive and readily available;
Convenient and easy use – existing infrastructure supports oil and gas;
‘Cleaner’ than coal;
Easy to distribute, store and transport;
High density:
  40 MJ/L;
  125,000 Btu/gallon
Downsides:
Extraction also has environmental impacts;
Carbon dioxide emissions and GCC;
Petroleum is a finite resources.
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 100
Are unconventional sources the answer?
Energy Systems and Sustainability, 2/e, Chapter 7
Let’s look at some numbers:
Canadian oil sands: 4.6 million barrels per day
Venezuelan extra heavy oil: 2.3 million barrels per day
World shale oil: 0.5 million barrels per day
11% current world oil production
Unconventional sources of petro-fuels appear to be extending – or postponing – peak oil, but these sources are also finite.

## Slide 101
Reserves of unconventional fossil fuels
Energy Systems and Sustainability, 2/e, Chapter 7
Increasingly, our reserves of petro-fuels will trend ‘unconventional’.

## Slide 102
Summary: oil and gas
Upsides:
Relatively inexpensive and readily available;
Convenient and easy use – existing infrastructure supports oil and gas;
‘Cleaner’ than coal;
Easy to distribute, store and transport;
High density:
  40 MJ/L;
  125,000 Btu/gallon
Downsides:
Extraction also has environmental impacts;
Carbon dioxide emissions and GCC;
Petroleum is a finite resources.
Energy Systems and Sustainability, 2/e, Chapter 7

## Slide 103
5. Oil & gas
  5.10: Methyl hydrates (or clathrates) The last fossil fuel frontier?
Module 5. Oil and gas

## Slide 104
Methane hydrates: what are they?
Methane hydrates form at the high pressures (hundreds of atm) and cold temperatures (1-2°C) below the sea floor at 300 – 500 m depth.
4 CH4 + 23 H2O  4CH423H2O (methyl hydrate)
Ice-like crystalline compound of methane trapped in a cage of ice
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Methane_clathrate

## Slide 105
Methane hydrates: Where are they?
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/Methane_clathrate
Methyl hydrates are found in coastal waters off of most continents.
And in (melting) permafrost.
Brings FF resources to nations that don’t have any other FF.
Most are withing national control.
Attractive resources for energy security.

## Slide 106
Methane hydrates: How big a resource?
The earth’s estimated methane hydrates (aka gas hydrates) dwarf the amount of fossil fuels and allows us to continue using fossil fuels and avoid some fundamental changes to our energy system.
However, combusting this additional source of fossil fuels will accelerate GCC.
http://priceofoil.org/2013/03/13/the-madness-of-exploiting-methane-hydrates/

## Slide 107
Methane hydrates: What’s the potential?
“Depending on economics and technology, they could potentially supply the world with more than 1 million exajoules of energy, equivalent to thousands of years of current global energy demand.”
“And they are nearing commercial production, with some ventures looking to be only half a decade away. That’s why it is time now to think about how to govern their use.”
https://foreignpolicy.com/2020/01/09/fracking-oceanic-methane-hydrates-global-energy-landscape-bonanza/
Biggest concerns:
Who owns them or the rights to them? offshore/international waters
Huge disruption of existing global FF economics
Potential for big leaks during extraction/production
Impact on ocean shelf fisheries
A new source of huge GHG emissions when used
South China Sea
Artic region
“If methane hydrates are to be extracted responsibly, the world needs to create strong regulations to protect the marine environment and the atmosphere.”

## Slide 108
Creating a carbon storage loop while harvesting?
https://www.nature.com/articles/s41598-019-52745-x
In a 2019 lab study, scientists were able to use hot CO2—rich flue gases to displace (release and harvest) the methane in methyl hydrates in frozen permafrost.
The CO2-rich gases replace the CH4, are frozen and stored as CO2-hydrates.
Question?
How do you get hot flue gases to the methyl hydrate sites?

## Slide 109
China reports successful harvest of methyl hydrates
https://global.chinadaily.com.cn/a/202003/27/WS5e7d4499a310128217282599.html
https://www.chinausfocus.com/peace-security/methane-hydrates-chinas-real-south-china-sea-goal
In February of 2020 China said it extracted a record amount of flammable ice during its second trial exploration in the South China Sea, with about 28,700 cubic meters collected per day for a total of 861,400 m3.
1,225 m depth
Horizontal drilling method
Environmental surveillance system developed; no leaks detected
“…one cubic meter of methane hydrate releases about 164 cubic meters of gas at standard conditions－making it a potential energy resource,"

## Slide 110
Module 5. Oil and gas
  5.11: Petroleum’s future?

## Slide 111
Finite, but not quite down for the count
While all fossil fuels, coal, oil, NG, etc., are finite resources human ingenuity will probably allow us to keep finding and exploiting ‘new’ reserves of fossil fuels for decades if not hundreds of years.
https://www.nature.com/articles/s41598-020-65018-9
So, whether to keep using fossil fuels or switch to alternatives is choice people, governments and corporations will make.
What will we choose to do and why?

## Slide 112
Much petroleum ‘is unburnable’ for a 2C GCC limit
A Watt double-acting steam engine (1859)
Wyoming Public Media
https://www.carbonbrief.org/media/366129/percentage-usable2.png

## Slide 113
There are signs of change
February 2020
“The British oil giant BP set the most ambitious climate change goal of any major oil company on Wednesday, saying that it aimed to eliminate or offset by 2050 all of the planet-warming emissions from its operations — as well as the emissions caused by the burning of the oil and gas it pumps out of the ground.”
https://www.nytimes.com/2020/02/12/climate/bp-greenhouse-gas-emissions.html?searchResultPosition=6
Other members of Europe’s “Big Oil” fraternity have made similar pledges.
BP offered few details about how it fulfill this pledge.
“We are aiming to earn back the trust of society,” said Bernard Looney, BP’s chief executive, at a news conference in London. “We have got to change, and change profoundly.”
  BP’s direct emissions: 55 m tons GHG/year
  BP’ emissions from fossil fuels it sells: 360 m tons GHG/year
  BP sells fossil fuels from others: 77 m tons GHG/year (cut those in ½ by 2050)
  CA (for context): 424 m tons GHG in 2017
BP still expects to be producing and selling petroleum in 2050.

## Slide 114
BP’s current ”strategy”
https://www.bp.com/en/global/corporate/what-we-do/our-strategy.html

## Slide 115
First hints of BP’s plan
August 2020
https://www.greentechmedia.com/articles/read/bp-to-invest-5b-a-year-on-low-carbon-and-cut-fossil-fuel-output-by-40-percent-by-2030
Cut oil and gas output by 40% by 2030.
No new petro exploration in countries it isn’t yet operating in.
Increase low-carbon investment from $500 m/year in 2019 to $5 b/year in 2030.
To $3 – 4 b/year by 2025
Note that BP’s capital expenditures were $12 b in 2020
Create / invest in 50 GW of RE by 2030.
From 2.5 GW in 2020 to 20 GW by 2025.
 Similar to French EDF’s RE goal.
BP has cut its shareholder dividend in half.
Stock price rose by 8% when this news was released.

## Slide 116
What about government subsidies to big petro?
https://www.euractiv.com/section/climate-environment/news/eu-countries-have-no-concrete-plans-to-phase-out-fossil-fuel-subsidies-report/
2019: The G7 gave the fossil fuel industry $100 b/year in subsidies.
G7 nations:
US
Canada
UK
France
Germany
Italy
Japan
2009: The G20 pledged to end fossil fuel subsidies within 10 years.
2016: The G7 pledged to end fossil fuel subsidies by 2025.
2014 - 2016: EU gave the fossil fuel industry €55.5 b/year in subsidies.
2017: EU + Norway earned €400 b/year from the fossil fuel revenues.
2018: France adds a modest fuel tax and the response is months of very serious ‘yellow vest’ protest
The EU has repeatedly promised to end fossil fuel subsidies. But what actions?
2019: Draft plans show that 8 / 27 countries plan to end coal subsidies by 2030.
2019: 5 / 27 countries plan modest increases in FF subsides as ‘low-carbon transition support.

## Slide 117
COVID, lower demand and revenue may be a push
https://www.bloomberg.com/news/articles/2020-04-29/oil-slump-spurs-talk-of-ending-eu-subsidies-for-polluting-fuels
EU Energy Commissioner Kadri Simson wants to make a Green Deal part of the pandemic recovery plan. “Getting rid of fossil fuel subsidies while lowering taxes on electricity can nudge us in the right direction, without putting too much pressure on the consumers.”
"At the same time, the crisis has given us a snapshot of the future: in many countries, the penetration of renewables has significantly increased and this will become more and more common," Simson said. "Many investors are turning their interest away from fossil fuels and into renewable energies, where they see higher long-term returns. That's why I believe the recovery plan is an opportunity to accelerate support for renewable energy."
While the EU has yet to lower its €200 b/year subsidies to fossil fuels, the EU Parliament is said to be taking another look.

## Slide 118
Plastics?
https://www.vox.com/energy-and-environment/21419505/oil-gas-price-plastics-peak-climate-change

## Slide 119
Plastics are a petroleum product
https://www.vox.com/energy-and-environment/21419505/oil-gas-price-plastics-peak-climate-change
95% of growth
And a great deal of energy must be used to convert oil to plastic.

## Slide 120
But plastics may not be the answer for big oil
https://www.vox.com/energy-and-environment/21419505/oil-gas-price-plastics-peak-climate-change
https://www.npr.org/2019/07/09/735848489/plastic-has-a-big-carbon-footprint-but-that-isnt-the-whole-story
1. Plastics cause carbon emissions at a time when the issue has become critical.
  5 tons CO2 / ton of plastic
  That’s doubles the carbon yield of oil.
  And if the plastic is burned for disposal (much is) the emissions from no to 2050 would equal 56 Gtons, >50X annual emissions of all US coal-fired power plants.
2. Plastics’ external costs are nearly equal to its market value.
  Mainly emissions, sorting, pollution, microplastics; estimated ~ $1,000 / ton
3. Plastics is a wasteful industry.
  36% single-use
  40% mismanaged – ends up as pollution
  20% sent for recycling but only 5% is actually recycled
  Without design and production guidelines, little can be recycled.
4. The public is becoming aware of the downsides of plastic and voting it off the island.
  Polls show that 70-80% want to reduce plastics, particularly single-use.