## Slide 1
SSC 2030: Energy Systems & Sustainability
5. Oil and natural gas
5.1: Origins & geology of petroleum
5.2: Origins of oil & gas industries
5.3: Finding & producing petroleum
5.4: Petroleum refining & products
5.5: Oil today
5.6: Natural gas
5.7: Rise & fall of North Sea oil & gas
5.8: Why are oil & gas so special?
5.9: Conversion technologies
5.10: Unconventional oil & gas
5.11: Methane leaks and GCC

## Slide 2
5. Oil & gas
  5.6: Natural gas

## Slide 3
Natural gas: a ‘recent’ fossil fuel
While the US started using NG in the 1920s, European countries did not.
In 1959, a huge non-associated NG field was discovered in the Netherlands; later, off-shore NG fields in the North Sea.
Energy Systems & Sustainability, 2/e, Chapter 7; https://en.wikipedia.org/wiki/North_Sea#/media/File:Nseamap.gif
In the UK, conversion from coal gas to NG took a decade & cost £564 m.
Pricing lower than coal gas incentivized the switch.

## Slide 4
Lessons learned while switching fuels
Energy Systems & Sustainability, 2/e, Chapter 7; http://www2.nationalgrid.com/uploadedImages/Resources/Image_library/Maps/UK%20Transmission%20maps.jpg
In the UK, conversion from coal gas to NG took a decade & cost £564 m.
NG has 2X the energy content of coal gas; retrofitting was needed.
  13 m customers
  40 m appliances
2007: 92% of homes have central heat
  75% are heated with NG
Pricing lower than coal gas incentivized the switch.
2000: 40% of electricity from NG
  Generated with CCGTs
To meet peak winter demands, 3% of annual NG demand is stored by injection into depleted offshore wells
  Some large users have interruptible contracts & have secondary energy

## Slide 5
Processing NG: ‘scrubbing’ by-products
Energy Systems & Sustainability, 2/e, Chapter 7
Natural gas (CH4) is contaminated with other gases:
Ethane (C2H6)
He
H2S
CO2
plastics manufacturing
medical uses; superconducting magnets
S used in fertilizers
re-injected to flush more NG out of wells
NG with low levels of contaminants is called ‘sweet’.
These gases are ‘scrubbed’ out of NG using amine chemistry.

## Slide 6
Natural gas: ‘cleaner’ than oil & coal
Energy Systems & Sustainability, 2/e, Chapter 7
Natural gas is mostly methane (CH4) but contains small amounts of other hydrocarbon gases when extracted: ethane (2 carbons); propane (3 carbons); and butane (4 carbons).
CH4 + 2O2  CO2 + 2H2O
mass 16 64 44 36
CO2 = 44 = 2.75
fuel 16
Propane is (C3H8) and is separated from natural gas during processing.
C3H8 + 5O2  3CO2 + 4H2O
mass 44 160 132 72
CO2 = 132 = 3.0
fuel 44
It is often said that NG is a ‘cleaner’ fuel than oil or coal & produces less CO2. Why & how?
Hydrogen ‘burns’ without producing CO2. The more hydrogen a fuel has, the less CO2 it produces.
So, to identify ‘clean’ fuels look for a high H:C ratio.

## Slide 7
NG: lower CO2 emissions
Natural gas has lower carbon dioxide emissions because of its high H:C ratio
Energy Systems & Sustainability, 2/e, Chapter 7; https://www.eia.gov/tools/faqs/faq.php?id=73&t=11
fossil fuel | H:C ratio | pounds CO2 / MBtu
Coal (anthracite) | 0 – 0.3:1 | 228.6
Coal (bituminous) | 0.8:1 | 205.7
Coal (lignite) | 1:1 | 215.4
Diesel fuel / heating fuel | 2.27:1 | 161.3
Gasoline (no ethanol) | 2.25:1 | 157.2
Propane | 2.67: 1 | 139.0
Natural gas | 4:1 | 117.0

## Slide 8
Domestic condensing gas boilers
Energy Systems & Sustainability, 2/e, Chapter 7
Because NG burn cleanly, water vapor produced by combustion can be condensed allowing recovery of the latent heat of vaporization.
40°C return water cools flue gases below 50°C, increasing recovery of heat from the flue gases by 11%, the difference between HHV & LHV.
Increase boiler efficiency to >90%.

## Slide 9
Global gas reserves & production
Energy Systems & Sustainability, 2/e, Chapter 7
Once again, distribution doesn’t predict production.
40% of global NG reserves are in the Middle East, most in the Gulf between Qatar & Iran.
Qatar is a huge exporter of LNG.
reserves
production

## Slide 10
NG units
Energy Systems & Sustainability, 2/e, Chapter 7
UK units:
1 therm = 100,000 BTU = 29.3 kWh = 105.5 MJ = 2.7 m3 NG
US units:
1 MMBTU = 1,000,000 BTU = 293 kWh = 1.055 GJ = 27 m3 = 1E3 ft3 NG
International:
1000 m3 NG = 39 GJ = 10.8 MWh = 0.93 tonnes of oil
‘Roundly’:
1000 m3 NG = 40 GJ = 10 MWh = 1 tonnes of oil

## Slide 11
R/P ratios for NG
Energy Systems & Sustainability, 2/e, Chapter 7

## Slide 12
Transporting NG? Pipeline
Energy Systems & Sustainability, 2/e, Chapter 7
High-pressure pipeline transports natural gas from NG storage depots to communities and industries.
Pipeline can transport the equivalent of gigawatts of power.

## Slide 13
Transporting NG? LNG
Energy Systems & Sustainability, 2/e, Chapter 7
LNG, liquified natural gas, is produced by compressing natural gas. Increased energy density allows economical long-distance transportation.

## Slide 14
Europe is now dependent on NG
Energy Systems & Sustainability, 2/e, Chapter 7
Russia exports NG to Europe from Siberia through long pipelines.
Note that NG from Russia must cross Ukraine & Belarus.
Pipeline pressure is boosted by in-pipe gas turbines powered by adding O2.
Europe’s energy security is not boosted.