## Slide 1
SSC 2030: Energy Systems & Sustainability
5. Oil and natural gas
5.1: Origins & geology of petroleum
5.2: Origins of oil & gas industries
5.3: Finding & producing petroleum
5.4: Petroleum refining & products
5.5: Oil today
5.6: Natural gas
5.7: Rise & fall of North Sea oil & gas
5.8: Why are oil & gas so special?
5.9: Conversion technologies
5.10: Unconventional oil & gas
5.11: Methane leaks and GCC

## Slide 2
5. Oil & gas
  5.9: Conversion technologies

## Slide 3
Should we convert coal to syngas?
Energy Systems & Sustainability, 2/e, Chapter 7
CTL (coal to liquid) technology has a long history: 1930s to the present.
Used when coal is abundant but oil & gas are not.

## Slide 4
Conversion chemistry
Energy Systems & Sustainability, 2/e, Chapter 7
Chemistry needed to convert coal (C) to methane (CH4).
2C + O2  2CO
C + H2O  CO + H2
CO + H2O  CO2 + H2
CO + 3H2  CH4 + H2O
2C + 2H2O  CH4 + CO2
pyrolysis: combustion of coal with limiting O2 (-ΔH)
water gas reaction (+ΔH)
water gas shift reaction (-ΔH)
methanization (+ΔH) requires Ni catalyst
overall syngas reaction
24 36 16 44 tonnes
32.8 55.5 MJ / kg
7.87 E5 8.88 E5 MJ
Not 100% efficient; process heat
Large amounts of water required.

## Slide 5
Syngas from coal in ND
Energy Systems & Sustainability, 2/e, Chapter 7
The Great Plains Synfuels, ND: a pilot plant in operation since 1984
lignite  CH4 (syngas = NG)
By-products:
(NH4)2(SO4) fertilizer, Kr gas, Xe gas, CO2 for enhanced oil production in CA

## Slide 6
Energy Systems & Sustainability, 2/e, Chapter 7
To convert coal to a liquid fuel, hydrogen must be added to increase the H:C ratio.
Coal to liquids
Steps:
Remove C from coal
Add H
  Direct coal liquefaction (Germany, 1913) [EROI of 60-73%]
    Mix finely ground coal with coal tar oil.
    Add heat & pressure.
    Add H2 gas with an iron catalyst.
    Refine the synthetic crude oil.
  Sasol process (Germany, 1930s) [EROI of 55%, but ‘sweet’]
    Convert coal to NG.
    Polymerize carbons via Fischer-Tropsch process.
      Pass CO, H2 mixture over iron catalyst at 20-30 atm, 200-350°C.
        Lower temperatures produce paraffin & waxes; higher temperatures produce lighter products.

## Slide 7
Energy Systems & Sustainability, 2/e, Chapter 7
South Africa has large coal reserves, but lacks liquid hydrocarbons.
Operates 3 Sasol plants that produce 6,000 – 30,000 barrels of oil products per day.
While the process isn’t very efficient, sulfur and nitrogen are removed, producing ‘clean’ fuels.
Commercial CTL in South Africa

## Slide 8
Energy Systems & Sustainability, 2/e, Chapter 7
Because liquids are more easily transported, methane is sometimes converted into liquid hydrocarbons by reversing the chemistry we’ve just looked at:
CH4 + H2O  CO + 3H2O
Gas to liquid conversion
Methanol (CH3OH) can be used as a liquid fuel or converted to ‘petrol’.
New Zealand used a methanol-to-gasoline plant to supply 10% of national need until NG reserves started running low.
Sasol process can also be used to build longer hydrocarbon fuels from methane.
Malaysia uses this technology in a middle distillate synthesis plant to produce 140,000 barrels of liquid fuel per day.
Massive amounts of water are required.

## Slide 9
Energy Systems & Sustainability, 2/e, Chapter 7
Economics?
2010 studies of CTL show that a break even price for the technology would be between $24 – 75/barrel of oil.
Is CTL the answer to peak oil?
CO2 emissions?
CTL produces twice the CO2 emissions than conventional oil.
GTL produces 1.5 times “ “
Carbon sequestration could mitigate these increases in CO2.
Supplies of water and coal?
Two barrels of oil would require 1 tonnes of coal.
Water use might be the larger problem.