## Slide 1
SSC 2030: Energy Systems & Sustainability
6. Nuclear power
6.1: Nuclear power: an introduction
6.2: Nuclei: a brief summary
6.3: Radioactivity
6.4: Nuclear fission
6.5: Thermal fission reactors
6.6: Types of thermal fission reactors
6.7: Nuclear fuel cycles
6.8: Fast neutron reactors
6.9: Newer nuclear reactor designs
6.10: Nuclear power in Vermont
6.11: Power from fusion

## Slide 2
6. Nuclear power
  6.5: Thermal fission reactors

## Slide 3
Thermal fission reactors?
Nuclear reactors don’t burn fuel, rather their uranium undergoes fission giving off heat in the process. That’s one type of thermal.
Energy Systems & Sustainability, 2/e, Chapter 10
There are two basic types of nuclear reactors:
Thermal reactors use moderators like graphite to slow neutrons & allow controlled chain reactions
  The slowed neutrons carry lost energy as heat.
Fast neutron reactors don’t need moderators so the neutrons aren’t ‘thermalized’.

## Slide 4
Thermal fission reactors: 4 essentials
Thermal fission reactors have four essential components:
Fuel = uranium;
Moderator, usually graphite;
Coolant to pick up and transfer heat; &
Control system.
Energy Systems & Sustainability, 2/e, Chapter 10

## Slide 5
Fuel rods
Early nuclear plants used natural uranium, but recent plants use enriched uranium with 2-5% U-235.
Plutonium produced in breeder plants can be reprocessed & used as fuel.
Thorium can also be used as fuel.
Energy Systems & Sustainability, 2/e, Chapter 10;
https://i.pinimg.com/originals/ae/a7/02/aea702d2b7bfdf48ae724853261c2456.jpg
Uranium oxide (UO2) is a hard ceramic that can be formed into pellets.
Pellets are held in metal tubes.
The metal must not absorb neutrons.
Fuel rods are replaced every 12-18 months.
100 tonnes of fuel per reactor:
2-3 GW of heat
600 – 1000 MW of electricity

## Slide 6
Moderator
Three types of moderator are common:
Light water (H2O)
Heavy water (D2O)
Graphite (a form of carbon)
Energy Systems & Sustainability, 2/e, Chapter 10;
http://consumedland.com/images/Control%20Rods_en.jpg
Remember that moderators are needed for fission to happen.

## Slide 7
Coolants & control systems
Coolants absorb heat released by decaying fuel pellets & carry the heat to the steam generator.
Liquid moderators like light & heavy water can also act as the coolant.
Gas coolants like carbon dioxide can also be used.
Energy Systems & Sustainability, 2/e, Chapter 10
Control rods are made of material that absorbs freed neutrons & slow or stop fission from continuing.
Good neutron absorbers:
Cadmium
Boron
When control rods are inserted between fuel rods fission is dampened or stopped.

## Slide 8
Nuclear plant safety
Design of a nuclear plant must store & use fuel at the correct densities & must have a robust coolant system that will continue to function under the most adverse circumstances.
Lack of cooling can cause the fuel in the reactor core to meltdown.
Energy Systems & Sustainability, 2/e, Chapter 10
Shielding is needed to protect operators from radiation in the core.
1E12 times the safe limit.
Safe distance without shielding would be 8 km.
Concrete & steel both absorb gamma radiation.
Containment is needed deal with high pressure & radioactive gases produced in the plant.

## Slide 9
Accidents
Most accidents result from loss of control of the nuclear chain reaction resulting in too much heat.
Energy Systems & Sustainability, 2/e, Chapter 10
Water used as moderator or coolant can be turned to steam, react with the zirconium alloy fuel rods & produce explosive hydrogen gas.
Loss of cooling is a problem even if the fusion chain reaction is stopped because the fuel will continue to decay & produce heat. This can melt the fuel which can then escape containment.
Three Mile Island (1979, PA)
Fukushima (2011, Japan)
Loss of control would allow a runaway fission chain reaction.
Chernobyl (1986, Ukraine)
Passive response cause plants to safely shutdown if power or coolant systems failed.
Shutdown would be triggered without operator action.