## Slide 1
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin
Notes: Module 7 examines the extent to which integration of farm and anaerobic digester operations are possible and / or necessary. The major issues considered here are operational. Fiscal issues will be covered in the AD economics module.

## Slide 2
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 3
On-farm AD vs. partnership
with off-farm AD

## Slide 4
AD pros & cons from a farmer’s POV?
Much has been written on the pros and cons of anaerobic digestion, but the point of view is often societal, environmental or economic.
What about the farmer’s POV? Here’s a summary from a 2015 Pennsylvania meeting about farm anaerobic digestion.
Opportunities:
Opportunities for the addition of food waste (co-digestion) into methane digesters are increasing.
Separated solids used for bedding have been shown to be a very positive benefit as a bedding material for the dairy herd. The landscape industry may also have interest in the fibrous material for mulching and as a soil amendment allowing for additional local business opportunities.
Stacking multiple benefits of an anaerobic digester system can result in a very positive return on investment. [aka bio-refinery approach]
www.hoards.com/IB_Anaerobic-Digester-Meeting-Tour
Notes: While much as been written about the pros and cons of anaerobic digestion, this assessment rarely comes from a farmer’s point of view. Instead writers usually address society’s point of view an economic point of view or how anaerobic digestion will affect the environment. [] So, what about the farmer’s point of view? In 2015, Pennsylvania farmers met to discuss the opportunities presented by an anaerobic digestion. Hoard’s Dairyman reported the opportunities and the challenges seen by these farmers. [] Among the opportunities were: the ability to add food waste, or co-digest; [] separated solids are a great benefit to dairy farmers; and, [] if the multiple benefits of anaerobic digestion are considered, AD technology can provide a very positive return on investment. We will discuss this “stacked” or bio-refinery concept in the last module of this course.

## Slide 5
Caveats and advice
It is critical to the success of any anaerobic digester system that one person have a significant passion to see the system function efficiently and profitability.
www.hoards.com/IB_Anaerobic-Digester-Meeting-Tour
Now is the time for potential owners to do research and discovery.
Producers should develop a game plan now so they are ready if the opportunity and circumstances (funding and permitting) present themselves.
Research companies and vendors to determine which ones have a proven track record.
Producers establish a trusted team of advisors to assist in the planning and “what if” process of coming to a go or no-go decision regarding the implementation of an AD system.
Notes: While much as been written about the pros and cons of anaerobic digestion, this assessment rarely comes from a farmer’s point of view. Instead writers usually address society’s point of view an economic point of view or how anaerobic digestion will affect the environment. [] So, what about the farmer’s point of view? In 2015, Pennsylvania farmers met to discuss the opportunities presented by an anaerobic digestion. Hoard’s Dairyman reported the opportunities and the challenges seen by these farmers. [] Among the opportunities were: the ability to add food waste, or co-digest; [] separated solids are a great benefit to dairy farmers; and, [] if the multiple benefits of anaerobic digestion are considered, AD technology can provide a very positive return on investment. We will discuss this “stacked” or bio-refinery concept in the last module of this course.

## Slide 6
Stand-alone on-farm AD?
Construction and operation of digesters requires capital (funding) and increased personnel time.
These costs may be too steep for a farm of less than 1000 head of dairy cattle.
In 2004, AgSTAR provided cost estimates:
Capital costs at $150 - $500 / cow; and
Annual operating costs of $11,000 - >$50,000 for labor and / or an AD operator.
Co-digestion will increase revenue (essentially increase herd size) but will also increase capital costs, project complexity and operational requirements.
Notes: Construction and operation of anaerobic digesters requires capital and increased personal time. [] These costs may be too steep for a small farm with less than 1000 head of dairy cattle. In 2004, AgSTAR provided cost estimates for building and operating anaerobic digesters. They estimated capital costs at $150 to $500 per cow. And AgSTAR estimated annual operating expenses at $11,000 to greater than $50,000 for labor and or a full-time operator. It’s not clear whether maintenance costs were included in these annual operating costs. Co-digestion will increase revenue by essentially increasing herd size. [] However, co-digestion will also increase the capital costs of constructing a digester, the project’s complexity and operational requirements.

## Slide 7
Participating in an AD cooperative?
Small farms might reap some of the benefits of AD by becoming partners in an cooperative AD project.
Farms would contribute manure, and possibly other on-farm feedstock materials like extra crops or spoiled feed.
The nutrients from those contributions would be returned to farmers.
Fertilizer
Bedding
Nutrient management planning assistance
(Some $ for electricity?)
The partnership could be cooperative, or strictly by contract for goods & services.
Participation in cooperative AD and other partnership models is covered in more detail in the last module of this course.
Notes: Small farms may be able to reap some of the benefits of anaerobic digestion by becoming partners in a cooperative anaerobic digester project. [] Farms would contribute manure and possibly other on-farm feedstock materials like extra crops or spoiled feed. [] The nutrients that each firm contributes would be returned to that farm in the form of fertilizer, bedding, nutrient management planning assistance, and perhaps a share of electric revenue. [] The nature of the partnership could vary from a true cooperative to a contract for goods and services rendered. [] Cooperative anaerobic digestion and other partnership models are covered in more detail in the last module of this course.

## Slide 8
Assessment!
Please answer the questions in section 7.1 of the Module 7 Assessment.
Notes: [] Please open the Module 7 assessment tool and answer the questions relating to section 7.1.

## Slide 9
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 10
Manure only or co-digestion?

## Slide 11
Manure-only is the simpler option.
The digestion of liquid dairy manure is simpler in a number of respects.
AD design can be simpler (unmixed plug-flow);
Caveat: small herd size may not produce sufficient manure to justify AD.
Location of the AD facility next to the barn minimizes transportation and/or pumping of manure; and
AD operation can be very automated if manure is automatically pumped from the barn into the digester.
Notes: The digestion of liquid dairy manure or alone is simpler than co-digestion in a number of respects. [] First, the design of the AD system can be simpler; for example unmixed plug-flow. [] Location of the AD facility next to the barn minimizes transportation and or pumping of manure to the digester tanks. [] The operation of the AD facility can be very automated when manure is pumped directly from the barn to the digester. [] However, farms with a very small herd size – certainly less than 500 cattle – may not produce sufficient manure to justify on-site manure-only AD.

## Slide 12
Co-digestion
Co-digestion of off-farm feedstock materials can allow smaller farms to consider AD. However,
More complex AD systems are required for co-digestion;
Co-digestion requires farmers to secure sources of off-farm feedstock;
AD operation will be complicated by delivery of feedstock,
… more rigorous record keeping and compliance,
... and increased nutrients to plan for.
Regulation may limit the amount of off-farm feedstock that can be used in on-farm digesters.
So, farms must be sure they are able to produce the required amount of on-farm material.’
This may include ‘energy’ crops.
Notes: Co-digestion of off-farm feedstock material may allow smaller farms to consider on-site AD. However, co-digestion is not without its own costs. [] More complex AD systems are required for co-digestion. [] Farms must secure consistent and clean sources of off-farm feedstock. [] Operation will be complicated by delivery of feedstock, [] more rigorous record keeping and compliance, [] and finding a home for the added nutrients delivered in off-farm feedstock. [] Regulation may limit the amount of off-farm feedstock that can be used in on-farm digesters. [] So, farms must be certain they’re able to produce the required amount of on-farm material that allows them to accept off-farm material. [] On-farm feedstock may include so-called energy crops.

## Slide 13
Assessment!
Please answer the questions in section 7.2 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.2.

## Slide 14
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 15
Production of AD feedstock?

## Slide 16
On-farm production of AD feedstock
Non-manure on-farm feedstock materials may include:
sub-par or slightly spoiled feed;
a variety of crops;
plant material typically not fed to dairy cattle, like C4 grasses;
waste fruits; and
food residuals from on-farm food processing.
On-farm feedstock, manure and other materials may, or may not, be purchased from neighboring farms.
Check your state’s regulations.
Notes: Typical non-manure on farm feedstock materials include: [] sub-par or slightly spoiled feed for animals, [] a variety of crops, [] plant material not normally fed to dairy cattle like C4 grasses, [] waste fruit, [] and residuals from on-farm food processing. And it’s critical to note that the food processing must happen on farm to allow that material to be considered an on farm feedstock. Examples would include production of cheese, yogurt, jams, cider, pickles, egg production, or maple syrup production. [] To be sure what is allowed in your state check regulations and talk to your Agency of Agriculture.

## Slide 17
Spoiled or sub-par feed
Remember that high levels of mold can inhibit bacterial growth, and thus anaerobic digestion.
So, spoiled feed should be delivered to a digester as soon as it discovered.
Spoiled feed from bunkered crops should be delivered to the digester daily.
Stockpiling or storing spoiled feed will:
Reduce its energy value;
Promote overgrowth with molds and fungi that can inhibit AD;
Cause the material to decompose and begin to clump; and
Greatly increase odor released when these materials are transported to the digester.
Moving spoiled feed to the digester thus becomes a daily task that increases work of farm personnel.
Notes: While spoiled feed contains high levels of energy and can make great digester feedstock we have to bear in mind that high levels of mold, or fungal growth, can inhibit bacterial growth and anaerobic digestion. [] So, spoiled feed should be delivered to a digester as soon as it is discovered or uncovered. The longer it waits the more problematic it becomes. [] Ideally spoiled feet from bunkered crops should be delivered to the digester daily. Stockpiling or storing feed once it is recognized as spoiled will: [] reduce its energy value; [] promote overgrowth with mold and fungi that can inhibit AD; [] cause decomposition and cause spoiled feed to clump making handling difficult; [] and greatly increased odor released when the spoiled feed is moved and transported to the digester. At Vermont Tech, we’ve noticed that very spoiled feed is one of the more odiferous feedstock materials we get. [] So, to use spoiled feed to your best advantage, it must be moved daily and this will increase work of farm personnel and use of equipment.

## Slide 18
‘Energy’ crops
Almost any farm crop can be fed to anaerobic digesters.
But there are caveats:
Crops higher in cellulose and lignocellulose will require longer HRTs and may not be completely digested.
  Of course, that can produce more solids with bedding value!
Crops must be chopped finely to avoid clogging pipes, pumps and valves.
  Silage choppers can work well.
  Bale choppers may not produce small enough or uniform material.
Feeding of energy crops should be fairly steady and this may require extra storage capacity; new bunkers?
Chopped crops will require use of farm equipment and personnel, likely on a daily basis.
Notes: Almost any farm crop can be fed to an anaerobic digester to produce biogas and energy. [] However, there are some points you should consider. [] Crops higher in cellulose and lignocellulose will require a longer HRT is and may not be completely digested during normal digester operations. [] Of course, that can be an advantage since undigested solids will make great bedding! [] Second, crops must be chopped finally to avoid clogging pipes pumps and valves. [] Silage choppers or forage choppers used in the field can work very well. [] At Vermont Tech we have not had good luck with tub bill choppers: the size of resulting material was too large and not uniform enough for using a digester. [] Third, any feedstock should be used consistently. So ideally energy crops should be stored so that they can be fed year round. This may require a new storage capacity like new bunkers. [] Fourth, planting, harvesting, chopping, and storing energy crops will require an additional use of farm equipment and personnel.

## Slide 19
Crops for marginal land?
Almost any vegetation can be fed to anaerobic digesters, including C4 photosynthesizers that would typically not be fed to animals.
It may be possible, and economically feasible, to grow such perennial grasses on marginal lands that are not suited for dairy crop production.
Low quality grasses could also be harvested from generous riparian buffer strips.
Low quality forage collected from brush hogged property might could also be used for AD feed if chopped finely.
Notes: Almost any vegetation can be fed to anaerobic digesters including C4 photosynthesizers that would not normally be fed to animals. [] It maybe possible, and economically feasible, to grow perennial grasses on marginal lands that are not suited for dairy crop production. Low quality grasses could also be harvested from generous riparian buffer strips. [] Low-quality forage collected from brush-hogged property might also be used for anaerobic digesters if chopped finely.

## Slide 20
Assessment!
Please answer the questions in section 7.3 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.3.

## Slide 21
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 22
Clean collection of AD feedstock

## Slide 23
Changing manure collection?
Manure used for anaerobic digestion must be collected and stored with care.
Manure must be either pumped to the digester as it is collected, or stored, in a temporary reception pit prior to moving to the digester.
While milk-house wash-water can be used to dilute semi-solid manure and make it pumpable, the presence of cleaning chemicals will likely reduce biogas output.
Note that rumensin and other antibiotics used in feed may reduce biogas output. Rumensin clearly inhibits AD.
Manure must be free of:
  Large biodegradables like placentas that clog pipes, valves & pumps;
  Non-biodegradable contaminants like hoof blocks, vet wrap, ag bag plastics, bandages, etc.,.
  Significant amounts of gravel and rock;
  Any materials large enough to clog pipes, valves and pumps; and
  Bacteriocidal compounds like copper sulfate, formaldehyde and similar hoof-treatments used in foot baths.
Notes: Manure used for anaerobic digestion must be collected and stored with care. [] Manure must be free of: [] large biodegradables like placentas that clogged pipes, valves and pumps; [] non-biodegradable contaminants like hoof-blocks, vet wrap, ag-bag plastic, bandages, etc.; [] significant amounts of gravel and rock; [] any materials large enough to clogged pipes valves and pumps; [] and bacteriocidal compounds like copper sulfate, formaldehyde, and similar hoof treatments used in foot baths. [] Note that rumensin and other antibiotics used in feed may reduce biogas output; rumensin clearly inhibits AD. [] While milk-house wash-water can be used to dilute semi-solid manure and make it pumpable, the presence of cleaning chemicals will likely reduce biogas output. [] Manure must either be pumped directly into the digester as it is collected, or stored in a temporary reception pit prior to moving to the digester. Temporary reception pits must be equipped with powerful pumps.

## Slide 24
Manure from heifers and dry cows
The solid or semi-solid manure from heifers and dry cows is a valuable feedstock, but is only available if and when those animals are confined.
So, remember that material will likely not be available during the late spring, summer and early fall.
  During the months that cows are pasteured, freshly cut forage may be able to take the place of dry manure.
Dry manure is easier to feed when it has not sat for long periods of time, so frequent transfer to the digester is better than episodic clean out.
  Stored manure begins to compost & clump.
When smaller amounts are transported, less of the solid manure needs to be stored at the digester.
Equipment and labor time need to be considered.
And avoid adding gravel or stone to manure when storing & moving it.
Notes: The solid or semisolid manure from heifers and dry cows is a valuable feedstock, but this manure is available only if and when those animals are confined. [] So, remember that material will likely not be available during the late spring, summer, and early fall. During the months that cows are pastured, freshly cut forage maybe able to take the place of dry manure. [] Dry manure is easier to feed when it has not sat for long periods of time, so frequent transfer to the digester is better than episodic clean outs. Stored or stacked manure begins to compost clump making it difficult to move and pump. [] When smaller amounts are transported, less solid manure needs to be stored at the digester. [] And remember that equipment and labor time for transfer will need to be considered. [] Avoid adding gravel or stone to mentor when scraping, storing, and moving it.

## Slide 25
Storage of crop feedstock
Most crop material used to feed AD systems is either fed as it is harvested or ensiled.
It’s important that gravel, sand and crushed stone are not mixed into ensiled material during its storage or during collection and transportation to the AD.
And ag bag plastic must be kept out of material fed to the digester.
Notes: Most crop material used to feed to AD systems is either fed as it is harvested or ensiled. [] It is important that gravel, sand, and crushed stone are not mixed into ensiled material during its storage or during collection and transportation. [] And ag-bag plastic must be kept out of material fed to the digester.

## Slide 26
Off-farm feedstock
Off-farm feedstock accepted for anaerobic digestion must also be collected in a clean stream, without non-biodegradable contaminants.
This is more difficult that it sounds!
For example, here are two methods of collecting food waste.
Collected into totes (large trash cans) and covered with a bit of sawdust.
  The generator is responsible for keeping the stream clean.
  Napkins, silverware, plastic must be excluded.
  The hauler inspects totes upon pickup and refuses those that contain contaminants.
  A last chance to remove contaminants occurs when totes are tipped at the digester before being ground and added to the system.
Collected in plastic bags, and
  Either pulped at the generator and transported in tanker trucks, or
  Transported to a central facility and mechanically debagged and pulped.
  Contaminants will to be ground into the pulp.
In each case, only human care keeps contaminants out!
Notes: Off-farm feedstock accepted for anaerobic digestion must also be collected in a clean stream, without non-biodegradable contaminants. [] This is more difficult than it sounds! [] For example here are two methods of collecting food waste. [] First, food waste can be collected in totes, or large trash cans, and covered with a bit of sawdust. [] The generator of waste is responsible for keeping the stream clean. Napkins, silverware, plastic, and other non-biodegradables must be excluded. [] The hauler inspects totes upon pick-up and refuses those that contain contaminants. [] A last chance to remove contaminants occurs when totes are tipped at the digester before being added to the slurry. [] In the second method, food waste is collected in plastic bags and either pulped at the generator and transported in tanker trucks, [] or transported to a central facility and mechanically debagged and pulped. [] Contaminants will be ground into the pulp. [] In each case, only human attention and care keeps contaminants out!

## Slide 27
Assessment!
Please answer the questions in section 7.4 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.4.

## Slide 28
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 29
On-farm use of co-products

## Slide 30
AD co-products for farmers?
AD produces a number of co-products that may be useful for farmers:
  Separated solids from effluent;
  Nutrient-rich liquid effluent;
  Heat recovered from the genset; and
  Carbon dioxide from genset exhaust.
Remember that anaerobic digestion decreases carbon content, but does not significantly effect NPK content of effluent. The implications for NMP and cropping are discussed in more detail in the NMP module.
Thoughtful and extensive use of co-products is vital to making AD economically viable.
Notes: Anaerobic digestion produces a number of co-products that maybe useful for farmers: [] separated solids from effluent; [] nutrient-rich liquid effluent; [] heat recovered from the genset; []and carbon dioxide from genset exhaust. [] Remember that anaerobic digestion decreases carbon content, but does not significantly affect NPK content of effluent. The implications for NMP and cropping are discussed in more detail in the NMP module. [] Thoughtful and extensive use of co-products is vital to making anaerobic digestion economically viable.

## Slide 31
Separated solids
Separated solids are fibrous material not completely degraded by the AD process and left in digester slurry.
Solids are:
Separated from digestate slurry using a solids separator;
  Often a screw press auger;
Generally about 65% moisture, 35% solids; and
Nutrient rich, and often enriched for phosphorous.
Bacterial levels in solids are decreased, but not eliminated by AD.
When solids are stored in piles they begin to compost, generating significant amounts of heat and often becoming moldy.
  Spreading piles into a thin layer allows drying and safer storage.
Solids are generally the most highly valued co-product on dairy farms because they can be used as bedding.
Solids can also be composted to create soil amendment.
Notes: Separated solids are fibrous materials that are not completely degraded by the anaerobic digester process and are left in digester slurry. [] Solids are: [] separated from digestate using a solids separator, often a screw-press auger; [] generally about 65% water and 35% solids; []and nutrient-rich and often enriched in phosphorus. [] Anaerobic digestion reduces levels of bacteria in solids but does not completely eliminate the presence of bacteria. [] When solids are stored in piles they begin to composted generating significant amounts of heat and often becoming moldy. [] Spreading piles into thin layers allows drying and safer storage. [] Solids are generally the most highly valued co-product on dairy farms because they can be used as bedding, replacing expensive sawdust, straw, or sand that cannot be used in anaerobic digesters. [] And solids can be composted to create soil amendments.

## Slide 32
Separated solids: mastitis?
Cornell University has compared the use of a wide variety of dairy bedding materials including separated raw manure, separated composted manure, separated solids from AD with and without composting, and sand.
Bedding strategies and economics were studied.
Mastitis, somatic cell count, foot and leg health were assessed.
Conclusions:
Using manure solids can provide an economic benefit without adversely affecting herd health.
Cornell Waste Management Institute (2010): ‘Use of dried manure solids as bedding for dairy cows…’
Bacterial levels in the bedding alone are not what cause high SCC or mastitis.
  Management of the bedding in the stalls is much more important than analyzing it for pathogens.
  Keeping stalls free of manure and urine, regardless of bedding type, will go a long way toward keeping SCC and mastitis under control.
Use a dried manure solids system that fits into your farm’s routine and one with which you are most comfortable.
Notes: Cornell University has compared the use of a wide variety of dairy bedding materials including separated raw manure, separated composted manure, separated solids from anaerobic digestion with and without composting, and sand. [] Bedding strategies and economics were studied. [] Mastitis, somatic cell count, and foot and leg health were assessed. [] The study concluded that using manure solids for bedding can provide an economic benefit without adversely affecting heard health. [] Bacterial levels in the bedding are not a cause of high somatic cell count or mastitis. [] Management of the bedding is much more important then analyzing bedding for pathogens. [] Keeping stalls or bedding areas free of manure and urine, regardless of bedding type, will go a long way towards minimizing somatic cell count and mastitis. [] Farms should use the dried manure solids system that best suits their operations.

## Slide 33
Separated solids: sales?
If a farm AD project produces more separated solids than it needs it may be able to sell them to other farms as bedding.
However, in Vermont regulators are hesitant to allow solids to be transferred for use as bedding if any beef has been included in AD feedstock.
Reluctance stems from fears about biosecurity due to bovine spongiform encephalopathy (BSE), aka mad cow disease.
  The BSE prion pathogen cannot be inactivated by pasteurization.
Notes: If a farm anaerobic digester produces more separated solid than it needs it may be able to sell them to other farms for dairy bedding. [] However, in Vermont regulators are hesitant to allow solids to be transferred for use as bedding if any beef has been included in feedstock. [] Their reluctance stems from fears about bio-security, specifically bovine spongiform encephalopathy, also known as mad cow disease. [] The BSE prion cannot be inactivated by pasteurization.

## Slide 34
Heat?
Heat is one of the most frequently ignored co-products of anaerobic digestion. Heat is difficult to transfer, so can only be used on-site.
The most frequent use for recovered heat is heating of greenhouses used to grow a valuable crop like winter tomatoes.
Heat can be used to dry solids and prevent storage issues.
Unless the solids are pelletized first, they tend to be very powdery.
Since the heating of homes and other buildings accounts for a very large part of Vermont’s carbon footprint, it would be very beneficial to use waste heat for space heating.
Industrial, institutional or residential spaces all need heat.
Co-location of AD is a challenge, particularly for on-farm AD.
Some on-farm AD has used waste heat to heat farm homes, or other farm businesses.
Notes: Heat is one of the most frequently ignored co-products of anaerobic digestion. Heat is difficult to transfer and can only be used on-site. [] The most frequent use for recovered heat is the heating of greenhouses used to grow a valuable crop like winter tomatoes. [] Heat can be used to dry separated solids and prevent storage issues like composting. [] Unless the solids are pelletized first, they tend to be very powdery. [] Since the heating of homes and other buildings accounts for a very large fraction of Vermont’s carbon footprint, It would be very beneficial to use waste heat for space heating. [] Industrial, institutional and residential spaces all need heat. [] Co-location of anaerobic digestion is a challenge, particularly for on-farm anaerobic systems. Some on-farm anaerobic digesters have used waste heat for heating farm homes or other farm businesses.

## Slide 35
Carbon dioxide
Plants use carbon dioxide as a building block and transform it into carbon-rich structural molecules like cellulose.
CO2 from a generating engine’s exhaust can be used to fuel plant growth if it the exhaust gas is scrubbed to remove harmful gases like carbon monoxide.
Recovered CO2 can then be added to the atmosphere of a greenhouse as long as levels are not dangerous to human workers.
Notes: Plants use carbon dioxide as a building block for biomass and transform it into carbon-rich structural molecules like cellulose. [] Carbon dioxide from a generating engine’s exhaust can be used to fuel plant growth if the exhaust gas is scrubbed to remove harmful gases like carbon monoxide. [] Recovered and scrubbed carbon dioxide can then be added to the atmosphere of a green house as long as levels are not dangerous to human workers. Some have experimented with using carbon dioxide to increase the biomass of algae grown in greenhouse conditions. Algae can be used as a feed supplement or a source of oils for biodiesel production.

## Slide 36
Assessment!
Please answer the questions in section 7.5 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.5.

## Slide 37
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 38
Effect of AD on nutrient management

## Slide 39
Liquid effluent
The liquid remaining after solids separation is nutrient-rich and can be used as a fertilizer.
AD reduces carbon content, but not nitrogen, phosphorous & potassium levels.
AD changes the chemical form of nutrients, mineralizing them.
Mineralized nutrients are very bioavailable and are quickly taken up by plants.
However, if applied incorrectly or not used by plants, these bioavailable nutrients could enter bodies of water and encourage growth of algae and depletion of dissolved oxygen.
Ammonia is the dominant form of nitrogen in liquid effluent.
Broadcast spreading will allow the ammonia to evaporate into the atmosphere and it won’t reach crops.
Instead, effluent should be injected into the soil or spread at the soil’s surface.
Notes: The liquid remaining after solid separation is nutrient-rich and can be used as a fertilizer. Anaerobic digestion reduces carbon content without changing nitrogen, phosphorus, and potassium levels. [] Anaerobic digestion does change the form of nutrients, mineralizing them. [] Mineralized nutrients are very bioavailable and are quickly taken up by plants. [] However, if applied incorrectly or not used by plants, these bioavailable nutrients can enter bodies of water and encourage growth of algae and depletion of dissolved oxygen. [] Ammonia is the dominant form of nitrogen in liquid effluent. [] Broadcast spreading will allow the ammonia to evaporate into the atmosphere and much will not reach crops. [] Instead, effluent should be injected into the soil or spread at the soil’s surface.

## Slide 40
More bioavailable NPK vs. more land?
The mineralized nutrients produced by AD may be more effective fertilizer than undigested manure.
So, less AD effluent than manure may be needed to crop the same acreage.
Cover crops may be useful sinks for nutrient management.
Alternately, farmers must find a use for increased fertilizing power.
If manure is brought in from other farms, or if off-farm feedstock is brought in for co-digestion, then AD will produce a significant excess of nutrients.
This may eliminate the need for synthetic fertilizer purchase.
Or, it may provide nutrients that will need homes.
‘Orphaned’ nutrients could be shared with, or sold to, other local farmers.
Trucking should be kept to a minimum.
Notes: The mineralized nutrients produced by anaerobic digestion may be more effective fertilizer and undigested manure. [] So, less anaerobic digester effluent than manure may be needed to crop the same acreage. [] Cover crops maybe useful sinks for nutrient management. [] Alternately, farmers must find a use for increased fertilizing power. [] If manure is brought in from other farms, or if off-farm feedstock is brought in for co-digestion, then anaerobic digestion will produce a significant excess of nutrients. [] This may eliminate the need for synthetic fertilizer purchase. [] Or, it may provide nutrients that will need homes. [] These orphaned nutrients could be shared with, or sold to, other local farmers. [] Trucking should be kept to a minimum.

## Slide 41
Assessment!
Please answer the questions in section 7.6 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.6.

## Slide 42
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 43
Transportation & storage issues

## Slide 44
Storage: without off-farm feedstock
Will an on-farm digester increase the need for storage?
It depends!
For an on-farm, manure-only digester, effluent volume should fit into the farm’s existing manure pit.
Separated solids may be used for bedding as quickly as they are produced by the digester.
Excess solids may need new storage. Beware of the heat produced by piled fresh solids.
Again, if solid manure is fed as quickly as it’s generated, it won’t have to be stored and moved twice.
If the farm’s existing manure pit is used to collect manure prior to pumping to the digester, a new pit or pond will be needed for AD effluent.
Notes: Will an on-farm digester increase the need for storage? [] It depends! [] For an on farm, manure only digester affluence volume should fit into the farm’s existing manure pits. [] Separated solids may be used for betting as quickly as they are produced by the digester. [] Excess solids may need new storage. Beware of the heat produced by piles of fresh solids. [] Again, if solid manure is fed as quickly as it is generated, It won’t have to be stored and moved twice. [] If the farm’s existing manure pit is used to collect manure prior to pumping to the digester, a new pit or pond will be needed to store AD effluent.

## Slide 45
Storage of off-farm feedstock
Digesters accepting off-farm feedstock will almost certainly need on-site storage for those materials.
Low-strength off-farm feedstock can be fed directly to the digester if the volumes don’t exceed reasonable portions of the daily feed volume.
But, high-strength off-farm feedstock will have to be stored on-site if the volumes delivered exceed the amount appropriate for daily feeding.
Storage tanks may be used for liquid materials.
Covered and enclosed bunkers or bays can be used to store solid feedstock.
Tanks: Pulped materials (those with some solids content) tend to settle during storage.
Robust mixing and pumping systems will be need to mix settled feedstock and deliver it to preparation pits or tanks.
Tanks may need to be heated to prevent freezing or gelling.
Ventilation, with charcoal filters or other strategy, of tanks and solids bays is essential for odor control and for personnel safety!
Notes: Digesters accepting off-farm feedstock will almost certainly need on-site storage for that feedstock. [] Low-strength off farm feedstock can be fed directly to the digester if the volumes don’t exceed a reasonable portion of the daily feed volume. [] But, high-strength off -farm feedstock will have to be stored on site the volumes delivered exceed the amount appropriate for daily feeding. [] Liquid feedstock can be stored in tanks. [] Bunkers, or covered bays can be used to store a solid feedstock. [] Tanks used to store pulped feedstock will need robust mixing, pumping, and plumbing systems in order to reliably deliver pulped material into feedstock mixing pits or the digester. [] And liquid storage tanks may need to be heated to prevent freezing or gelling of feedstock during winter weather. [] Ventilation using charcoal filters or other motor control strategies will be needed for solid storage bays, and should be used in feedstock mixing areas both for odor control and for the safety of personnel. Mixing feedstock in preparation pits can release ammonia, and sometimes hydrosulfuric acid.

## Slide 46
Co-digestion: storage of co-products
Digesters accepting off-farm feedstock will almost certainly need to increase storage of effluents.
Estimate the increase in liquid effluent volume as the volume of added, non-manure feedstock.
New storage ponds may needed for effluent.
If the new storage is sufficiently far from the digester to require trucking, then
  …a small effluent storage tank at the digester is needed to hold effluent for transportation.
A large, covered storage area will be needed if the digester produces more solids than the farm can use, and the solids are sold as a revenue producer.
Because of their high phosphorous content, solids should not be field stacked or exposed to water that can leach phosphorous and carry it to surface or groundwater.
Notes: Digesters accepting off farm feedstock will almost certainly need to increase storage of effluent. [] Estimate the increase in liquid effluent volume as the volume of added, non-manure feedstock. [] New storage ponds may be needed for effluent. [] If the new storage is sufficiently far from the digester to require trucking, then a small effluent storage tank is needed at the digester to hold effluent for transportation. [] A large, covered storage area will be needed if the digester produces more solids than the farm can use and if the solids are sold as a revenue producer. [] Because of their high phosphorus content, solids should not be field stacked or exposed to water that can leach phosphorus and carry it to surface or groundwater.

## Slide 47
Transportation: manure-only
Will operation of an on-site digester increase the use of (or need for) farm equipment for transportation?
For manure-only digesters that pump manure directly from the barn, additional transportation will only be necessary if:
Solid manure needs to be moved to the digester and mixed into liquid dairy manure. This requires powerful mixing by chopper pumps and or impellers.
  Manure spreaders or small wagons/trailers can be used to move solid manure.
The storage pond for liquid effluent is far from the digester facility.
  Manure tanker / spreaders can move liquid effluent.
Notes: Will operation of on-site digesters increase the use of, or need for, farm equipment for transportation? [] For manure-only digesters that pump manure directly from the barn to the digester, additional transportation will only be necessary under two circumstances. [] First, solid manure needs to be moved to the digester and mixed into liquid dairy manure. This requires powerful mixing by chopper pumps and/or impellers. [] Manure spreaders or small wagons and trailers can be used to move solid manure. [][] Second, if the storage pond for liquid effluent is far from the digester facility, manure tankers or spreaders must be used to move liquid effluent to the pond.

## Slide 48
Transportation with co-digestion (1)
On-farm co-digestion is very likely to increase the use of farm equipment and the need for regular transportation of feedstock and co-products.
Feedstock:
Liquid feedstock will be delivered by generators or haulers and can be stored in on-site tanks, so no on-site transportation will be needed.
Solid feedstock materials – like manure, spoiled feed, or energy crops – may be delivered by generators, or may need to be picked up by digester operators.
  Loaders, skid steers, tractors, manure-spreaders, wagons or trailers may be needed.
  After transportation and storage on-site, solids will needed to be moved again, from the storage site into the digester.
Notes: On-farm co-digestion is very likely to increase the use of farm equipment and the need for regular transportation of feedstock and co-products. [] Liquid feedstock will be delivered by generators or haulers and can be stored in on-site tanks, so no on-site transportation is needed. [] Solid feedstock material, like manure, spoiled feed or energy crops, maybe delivered by generators or may need to be picked up by the digester operator. [] Loaders, skid steers, tractors, manure spreaders, wagons or trailers maybe needed. [] After transportation and storage on site, solids will need to be moved again from the storage site into the digester.

## Slide 49
Transportation with co-digestion (2)
Co-products:
Liquid effluent volumes are usually increased by co-digestion.
Effluent may, or may not, need to be moved from the digester to a storage pond.
Increased volumes will require more transportation to, and spreading on fields.
  Partner farms may, or may not, pick up and spread their share of effluent. But the AD operator will likely have responsibility for the facility’s overall nutrient management plan and proper use of nutrients.
Separated solid volumes are also increased by co-digestion.
Solids may, or may not, need to be transported to a covered on-site storage bunker or shed.
Partner farms, or farm customers, may or may not pick up solids.
Notes: Liquid effluent volumes are usually increased by co-digestion. [] Effluent may, or may not, need to be moved from the digester to a storage pond. [] Increased volumes will require more transportation to, and spreading on, fields. [] Partner farms may, or may not, pick up and spread their share of affluent. But the AD operator will have responsibility for the facility’s overall nutrient management plan and proper use of nutrients. [] Separated solid volumes are also increased by co-digestion. [] Solids may, or may not, need to be transported to a covered on-site storage bunker or shed. [] Partner farms, or farm customers, may or may not pick up solids.

## Slide 50
Assessment!
Please answer the questions in section 7.7 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.7.

## Slide 51
Module 7: Integration of AD & farming
7.1: On-farm AD vs. partnering with AD
7.2: Manure only or co-digestion?
7.3: Production of AD feedstock
7.4: Clean collection of feedstock
7.5: On-farm use of co-products
7.6: Effects of AD on nutrient management
7.7: Transportation & storage issues
7.8: Opportunities for synergy
This curriculum is adapted from: eXtension Course 3: AD, University of Wisconsin

## Slide 52
Opportunities for synergy

## Slide 53
Requirements for synergy
Synergy (n.) the interaction or cooperation of two or more organizations, substances, or other agents to produce a combined effect greater than the sum of their separate effects.
Can synergy occur between farms and AD?
Farmers need to understand their own farm operations in terms of:
  Economics;
  Logistics;
  Transportation;
  Storage;
  Equipment;
  Nutrient management; and
  Personnel.
Farmers need to understand the implications of installing and operating on-farm AD or of partnering with an AD facility.
Notes: Synergy is the interaction, or cooperation, of two or more organizations, substances or other agents to produce a combined effect greater than the sum of their separate effects. [] Can synergy occur between farms and AD? [] Farmers need to understand their own farm operations in terms of: economics; logistics; transportation; storage; equipment; nutrient management; and personnel. [] Farmers need to understand the implications of installing and operating on-farm AD, or of partnering with an AD facility.

## Slide 54
Models for AD?
Farms can participate in, or use, AD in a number of different models:
Stand-alone on-farm AD
Membership in a cooperative AD
Partnership with an existing on-farm (or biomass) AD plant
These models will be discussed in more detail in the last two modules of this course.
Notes: Farms can participate in or use AD via number of different models. [] First, farms can construct and operate stand-alone on-farm AD. [] Second, farms can become members of an anaerobic digestion cooperative. [] Third, farmers can partner with an existing on-farm or biomass (ie commercial) AD facility. [] These models will be discussed in more detail in the last two modules of this course.

## Slide 55
Assessment!
Please answer the questions in section 7.8 of the Module 7 Assessment.
Notes: [] Please go to the Module 7 assessment and answer questions relating to section 7.7.