## Slide 1
Module 1: Introduction to Bioenergy
1.1: What is bioenergy
1.2: Current & projected energy use
1.3 : Forms of bioenergy
1.4: Bioenergy feedstock materials
1.5: Bioenergy co-products
1.6: Drivers of bioenergy use & development
1.7: The bioenergy debate
1.8: Is bioenergy sustainable?
1.9: Bioenergy vs. food debate
MEC 3040: Bioenergy

## Slide 2
1.4: Bioenergy feedstock materials

## Slide 3
Bioenergy feedstock & supply chain
Bioenergy feedstock: biomass-derived material that can be converted to energy using microbes, heat, chemicals or some combination thereof
Some amount of conversion (aka ‘refining’) is usually required to turn feedstock into use-ready biofuel.
Dahiya (2015)
biomass
biofuel
energy for use
processing
refining
use
(often combustion)
trees
soybean plants
supply chain / value chain
Processing (refining) often involves densification (or aggregation) to make transport of feedstock easier and cheaper.
cordwood, chips, pellets
heat, CHP, electricity
oil, biodiesel
heat, transportation fuel

## Slide 4
Types of bioenergy feedstock materials
Dahiya (2015)
woody
non-woody
lignocellulose
sugar
starch
cellulose/
lignocellulose
fats

## Slide 5
Feedstock sources
Dahiya (2015)
whole-tree chips
forests
agriculture
waste
bole chips
bark chips
short-rotation woody crops
perennial lignocellulosic crops
lignocellulosic residues
sugars / starches
oils
sawmill residues
construction wastes
municipal wastes
oil / fat waste
landfill gas
municipal solid waste

## Slide 6
Biomass feedstock availability
Bioenergy Primer 1; BIOEN1
We’ll discuss each feedstock material in more detail as this course proceeds, but let’s look at some general conclusions about biomass availability here.
The 2005 report, ‘Biomass as Feedstock for a Bioenergy and Bioproducts Industry: the Technical Feasibility of a Billion-Ton Annual Supply’ prepared by DOE & USDA made these conclusions:
We have enough biomass to replace 30% of US petroleum use by 2030.
Biomass harvests could be increased from 2005’s 473 million to 1.1 billion dry tons annually with modest changes to land management practices.
2011 update decreased estimates of forest & crop residue resources, but increased the potential of energy crops.
Because biomass feedstock materials are not energy dense, transportation to processing plants affects the cost of feedstock and profitability of growing bioenergy feedstock.
Willingness to grow bioenergy crops may be limited by distance from processing plants.

## Slide 7
Ethanol feedstock availability
Bioenergy Primer 1; BIOEN1
The 2008 report, ’90-Billion Gallon Biofuel Deployment Study’ prepared by Sandia National Lab and General Motors R&D Center looked at availability of feedstock for ethanol production.
hitectransportation.org/news/2009/Exec_Summary02-2009.pdf
90 billion gallons of biomass ethanol could be produced annually.
15 billion gallons from corn; and
75 billion gallons from cellulosic biomass, mainly perennial energy crops
  Requiring 48 million acres of land now characterized as ‘idle, pasture of non-grazed forest’.
In order for cellulosic ethanol to become commercially viable:
Biomass producers will need consistent & reliable markets;
Production contracts to help ensure supply; &
Supportive policy to encourage development.
While cellulosic biomass doesn’t take food from the hungry, farmers can’t sell cellulosic biomass crops for food if the energy demand / market drops.

## Slide 8
Forest-based feedstock sources
BIOEN1

## Slide 9
Agricultural residue sources
BIOEN1

## Slide 10
Agricultural sources: perennial crops
BIOEN1

## Slide 11
Total biomass sources
BIOEN1

## Slide 12
Biomass yields
BIOEN1
The term yield can mean different things. Average yields are conservative estimates based on averages across producers and years. Attainable yields & potential yields can be obtained if all factors are optimized:
Nutrients (can be controlled to some extent)
Water
Weather
Pests & management

## Slide 13
Biomass profits?
Typically, agricultural profits depend on the price paid for the crop and the combined cost of producing that crop.
BIOEN1
The costs of hauling the crop to the buyer / processor must also be considered as a cost to the producer. So, producers will choose their crops, in part, on their distance from buyers or processing plants.
Biomass is an attractive crop to produce only when processing plants are close enough to limit the costs of hauling and allow profit.

## Slide 14
Biomass supply chain
BIOEN1
forests
power
heat
steam
biofuels
chemicals
source
biomass
processing
use / market
agriculture
waste
densification
tops & branches
small-diameter pulpwood
small understory trees
bark
annual crop residues
perennial energy crops
hybrid willow / poplar
all crop starches / sugar
construction materials
sawmill residue
cardboard & paper
manure
food processing waste
food waste

## Slide 15
Feedstock by conversion process
BIOEN1
lignocellulose
thermal conversion
thermochemical conversion
biochemical conversion
chemical conversion
densification
combustion
power heat
steam
lignocellulose
bio-coal
syngas
charcoal
methanol
syngas
bio-oil
lignocellulose
sugars starches (crops)
organic wastes
trans-esterification
biodiesel
biogas or biomethane
ethanol
fats / oils / grease
gasification
pyrolysis
torrefication
fermentation
anaerobic digestion