## Slide 1
Module 1: Introduction to Bioenergy
1.1: What is bioenergy
1.2: Current & projected energy use
1.3 : Forms of bioenergy
1.4: Bioenergy feedstock materials
1.5: Bioenergy co-products
1.6: Drivers of bioenergy use & development
1.7: The bioenergy debate
1.8: Is bioenergy sustainable?
1.9: Bioenergy vs. food debate
MEC 3040: Bioenergy

## Slide 2
1.5: Bioenergy co- & by-products

## Slide 3
Bioenergy co-products
Co-products: non-energy products of bioenergy processing or use that have economic value
We will discuss more co-products as the course proceeds, but a few of the most valued co-products are listed here.
BIOEN1
Distillers grains: grain after ethanol production
  DDG (dry distillers grains) & WDG (wet distillers grains)
  Produced by 60% of ethanol plants: dry-mill plants
  Animal feed; AD feedstock
Bagasse: the fibrous material remaining when sugarcane is crushed
  Combusted, cellulosic ethanol feedstock; AD feedstock
Glycerol (aka glycerin): high-energy liquid co-product of biodiesel production
  Used by cosmetic & food industries if purified
  Combusted & used for AD feedstock
  950,000 tons produced per year with surplus above market demand
Biochar: co-product of gasification or pyrolysis
  Used as a soil amendment: holds nutrients & sequesters carbon in soil

## Slide 4
Bioenergy by-products
By-products: non-energy products of bioenergy processing or use that do not have significant economic value
A few of significant by-products are listed here.
BIOEN1
Fly ash: fine particulate matter from combustion of solid fuels; silica-rich
  Air pollutant & health hazard regulated by EPA
  Less than half of US fly ash is recycled as amendment to Portand cement
Waste water: water containing biomolecules
  Regulated and cannot be dicharged into waterways without treatment
  Liquid remainder from distillation of grains for ethanol
    4-6 gallons of wastewater are produced per gallon of ethanol
  Water used to ‘wash’ alcohol and glycerol from biodiesel
  Can be treated via anaerobic digestion though it has a low energy content
Carbon dioxide: produced by combustion of biofuels
  Will be regulated by EPA
  We need to make CO2 into a co-product!