## Slide 1
Module 3C: Grass biomass heating
3.16: Grass biomass densification and combustion
3.17: Vermont study of energy grass densification &
combustion
3.18: Conversion of grass to liquid biofuels
3.19: Economic considerations for grass biomass
MEC 3040: Bioenergy

## Slide 2
3.18: Conversion of grass to liquid biofuels

## Slide 3
Liquid fuels
Dahiya (2015)
Grass can be converted into liquid fuels like ethanol, methanol and alkanes.
However, conversion is much more difficult for grasses than for high sugar or starch feedstock materials like sugarcane or grains because of the sugars in grass are bound and cross-linked into complex polymers that are difficult to break down: cellulose, hemicellulose and lignins.
Enzymes from yeast, fungi or bacteria are used to digest the highly fibrous material and break out the sugars for fermentation.

## Slide 4
Liquid conversion steps
Dahiya (2015); DOE (2010)
Feedstock is pre-treated with heat and acid or base to break down fibrous cell walls.
Enzymes or catalysts are used to hydrolyze (or break down) cellulose and hemicellulose into simple sugars like glucose and xylose.
Microbes are added in anaerobic conditions to convert the sugars to alcohols (like ethanol). - Alternatively, chemical catalysts rather than microbes can be used to create other products.
Products are recovered by separation from water, solvents, residual & feedstock materials.
Distribution of product that may, or may not, be blended with other liquid fuels.
The lignin that remains after conversion is burned to create heat & power for the conversion process.

## Slide 5
Scale of conversion plants?
Dahiya (2015); DOE (2010)
The scale of conversion plants varies with the complexity of the process.
There are mobile densifiers that can produce grass briquettes or pellets.
Tractor PTO driven;
Or driven by on-trailer engines
However, cellulosic ethanol plants are complex plants that are built on a large scale to take advantage of economies of scale.
All biomass plants have to cope with the variation inherent in grass biomass feedstock.
Smaller and simpler processors are more likely to adapt…
… than large and complex plants that will have strict standards for feedstock material.