## Slide 1
Module 3A: Cordwood and woodchip heating
3.1: EROEI – energy return on energy investment
3.2: Residential heating: a case for cord wood
3.3: Efficient cord wood heating systems
3.4: Buyer’s guide to wood chip energy
3.5: Wood chip heating systems
3.6: Economic analysis of wood chip systems
3.7: Operating and maintaining a wood chip system
MEC 3040: Bioenergy

## Slide 2
3.7: Operating & maintaining a woodchip system

## Slide 3
Installation & commissioning
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
System manufacturers or installers are responsible for bing sure that it runs properly.
The process of testing the system for performance is called ‘commissioning’.
The performance standards may have been stated in the bid or sales information.
The fuel used in commissioning should be the fuel to be used after commissioning.
Operator training is also critical and should include:
Operating the system;
Maintaining the system; and
Trouble shooting.
The installer should provide an operating manual.

## Slide 4
What about the operator?
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
The biomass system operator is crucial to the success of any biomass energy project.
The operator must be interested and enthusiastic.
The project should involve the operator from the beginning.

## Slide 5
Maintenance
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
The manufacturer’s recommendations should be followed & likely include:
Ash removal from grates;
Ash removal from under grates;
Boiler tube cleaning;
Removal of fly ash;
Cleaning of the fire box & heat exchange surfaces;
Lubrication;
Inspection of drive chains, belts & gearboxes;
Inspection of refractory;
Checking of safety devices; and
Checking and adjusting of fuel feed rates & combustion air.

## Slide 6
Maintenance contracts & records
Wood-chip heating systems: a guide for institutional and commercial biomass installations, BERC (2004)
It may be possible to have maintenance done by the manufacturer, installer or an experienced operator on a contractual basis.
Contract offer the added benefit of periodic oversight by experienced professionals.
The contract may or may not include the cost of maintenance supplies and materials like lubricants and replacement parts.
Performance and maintenance records should be kept to determine, at minimum, how often:
The system fail or needs adjustment; and
Is repaired or routinely maintained.
And total operational hours.
Fuel consumption records allow calculation of fuel costs and needs for the next season.