## Slide 1
SSC 2030: Energy Systems & Sustainability
4. Forms of energy
4.1 Kinetic energy
4.2 Potential energy
4.3 Thermal energy
4.4 Chemical energy
4.5 Energy density
4.6 Electromagnetic radiation
4.7 Nuclear energy
4.8 Power
4.9 Summary of forms of energy

## Slide 2
4. Forms of energy
  4.1 Kinetic energy

## Slide 3
What is kinetic energy?
Kinetic energy: the energy of a moving mass or object
Energy Systems & Sustainability, 2/e, Chapter 4; http://science.jrank.org/
KE = (1/2)(m)(v2)
kinetic energy (J)
mass (kg)
velocity (m/s)
Problem:
If the 130 lb cyclist slows from 20 mph to 10 mph, how much does her kinetic energy change?
KE = (1/2)(59 kg)(9 E-3)2 = 2.4 E-3 J
130 lb 1 kg = 59 kg
2.2 lb
20 miles 1.6093 km 1 E3 m 1 hr = 9 E-3 m/s
1 hr 1 mile 1 km 3600 s
KE = (1/2)(59 kg)(4.5 E-3)2 = 6 E-4 J
ΔKE = 2.4 E-3 J - 6 E-4 J = 1.8 E-3 J

## Slide 4
Kinetic rotational motion
Kinetic rotational energy: a form of kinetic energy used to spin generators to make electricity or flywheels to store energy
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Erot = (1/2)(Ι)(ω2)
kinetic energy (J)
jntertia
(kg m2)
angular velocity (m/s)
This 1802 steam locomotive used a flywheel to even out the power produced by it’s single cylinder engine.
Today, flywheels are being investigated by NASA.

## Slide 5
4. Forms of energy
  4.2 Potential energy

## Slide 6
What is potential energy?
Potential energy: stored energy caused by attractive forces
  gravity (aka position)
  electrostatic attraction
Energy Systems & Sustainability, 2/e, Chapter 4; http://science.jrank.org/
PE = (m)(g)(h)
Potential energy (J)
mass (kg)
gravity
(m/s2)
Problem:
If an elevate water tank holds 100,000 gallons of water at a height of 200 feet, how much potential energy is created?
200 feet 12 inches 2.54 cm 1 m = 61 m
1 foot 1 inch 100 cm
100,000 gallons 3.7854 L 1 m3 1000 kg = 3.7854 E8 kg water
1 gallon 1 L 1 m3
PE = (3.7854 E8 kg)(9.8 m/s2)(61 m) = 2.26 E11 J
height
(m)
work (creates PE)

## Slide 7
Hydropower uses potential energy
Energy Systems & Sustainability, 2/e, Chapter 4; energy.gov

## Slide 8
Pumped storage uses potential energy
Energy Systems & Sustainability, 2/e, Chapter 4; scotsrenewables.com
Scotland’s Cruachan pumped storage hydro facility pumps water to an upper reservoir when surplus electricity is available. When electricity is needed, water is released to generate electricity.
The upper reservoir can store:
7 gigawatt-hours of energy
25 TJ of energy

## Slide 9
4. Forms of energy
  4.3 Thermal energy
  ‘...not that heat generates motion or that motion generates heat (though both are true in certain cases), but that heat itself, its essence and quiddity, is motion and nothing else.’
  - Frances Bacon, 1620

## Slide 10
What is thermal energy?
Thermal energy: an object’s energy measured by temperature (J)
Energy Systems & Sustainability, 2/e, Chapter 4
Q = (m)(C)(ΔT)
heat (J)
mass (kg)
change of temperature
(degrees °)
ΔT = Q .
(m)(C)
Q = (V)(C)(ΔT)
volume (L) or (gallons)
specific heat of water = 4810 J/kg-°
= 8.314 Btu/gal-°
Find specific heat with volumetric units
specific heat capacity
(J/kg-°) or (Btu/lb-°)°
Molecular kinetic theory: the average kinetic motions of atoms depend only on heat. Thus, heat is the kinetic motion of atoms or molecules.

## Slide 11
Thermal energy example
Problem: How much energy does it take to increase the temperature of water in a 400 gallon tank from 50 to 140°F?
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Q = (V)(C)(ΔT)
Q = (400 gallons)(8.314 Btu/gal-°)(140 – 50°F) = 2.99 E5 Btu
Note that since ΔT is the difference in temperature rather than an absolute value, the units can be F, C or K.

## Slide 12
4. Forms of energy
  4.4 Chemical energy

## Slide 13
What is chemical energy?
Chemical energy: the energy stored in inter- & intra-molecular bonds.
  Heat is released by when bonds are made during:
    combustion or…
    reduction-oxidation reactions.
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Compounds / molecules: two or more atoms combined (bonded) at a constant ratio
methane (CH4)
oxygen gas (O2)

## Slide 14
Chemical reactions & chemical energy
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Chemical reactions rearrange atomic connections (bonding) by breaking bonds and create new molecules by forming new atomic bonds.
Reactions obey the law of conservation of mass, but often involved changes in energy depending on the ratio of bonds broken to the bonds made.
methane (CH4)
oxygen gas (O2)
+
+
carbon dioxide
(CO2)
water
(H2O)
combustion
reaction
CH4 + 2O2  CO2 + 2H2O
Combustion reactions: burn carbon- & hydrogen-based fuel in the presence of oxygen gas to produce carbon dioxide, water & energy.

## Slide 15
Exothermic reactions release energy
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Endothermic reactions require energy to occur.
  Heat is a reactant.
  Can be used to store energy rather than make it.
Exothermic reactions release energy as they occur.
  Heat is a product.
  Combustion reactions are exothermic.
C + O2  CO2 ΔH = - 32.8 MJ/kg
C2H6O + 3O2  2CO2 + 3H2O ΔH = - 29.8 MJ/kg
Burning 1 kg of pure carbon (approximating coal) releases 32.8 MJ.
Burning 1 kg of pure ethanol (approximating coal) releases 29.8 MJ.
ΔH is enthalpy or heat energy
Negative ΔH means that heat is released (exothermic).

## Slide 16
Batteries: redox chemistry
Batteries: linked voltaic cells (redox half-cells) that store chemical energy until the half-cells are linked by a conductor
Some have finite power (non-rechargeable).
Others are rechargeable.
Energy Systems & Sustainability, 2/e, Chapter 4
http://www.astragrp.com/bateriku/images/battery_safety_handling.jpg
Discharging:
PbO2 + Pb + 2H2(SO4)  2Pb(SO4) + 2H2O
Example: lead-acid batteries used in cars
Discharge (produce) energy to start the car.
  Pb(SO4) coats the electrodes.
Charged when the car runs.
  Pb(SO4) is redoxed back to plates.
Charging:
2Pb(SO4) + 2H2O  PbO2 + Pb + 2H2(SO4)
anode
cathode
anode & cathode
Builds up on anode & cathode plates.

## Slide 17
Combustion vs. redox reactions
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Redox hydrogen fuel cell
gas combustion
Both type of reactions can use traditional fuels like methanol & methane.
Redox reactions can also use non-traditional fuels like H2 gas.
Redox reactions are more efficient at converting fuel to electricity.
  Internal combustion engine: 30% (so 70% ‘waste’ heat)
  Fuel cells: 70%

## Slide 18
Fuel cells are in commercial use
Energy Systems & Sustainability, 2/e, Chapter 4;
http://www.delawareonline.com/story/news/local/2015/07/22/new-bloom-box/30475483/
http://www.dailytech.com/Microsofts+New+Fuel+Cell+Partner+is+Ready+to+Blow+Away+the+Bloom+Box/article36118.htm
The Bloom box is a fuel cell that passes natural gas (methane) over thin ceramic plates coated with a proprietary redox ‘powder.
As of 2015, installed boxes were producing 160 MW at….
Apple, ebay, Fedex, etc.,.
New design doubles power output.
Revenue, but still little profit.
Source: University Delaware
Redox 25 kW power system
Redox (backed by Microsoft) may be big competition.
Closer to being competitive with combustion.
Technology may provide 100x power for the same cost.

## Slide 19
Bloom box schematic
http://www.dailytech.com/Microsofts+New+Fuel+Cell+Partner+is+Ready+to+Blow+Away+the+Bloom+Box/article36118.htm

## Slide 20
Bloom box schematic
http://www.dailytech.com/Microsofts+New+Fuel+Cell+Partner+is+Ready+to+Blow+Away+the+Bloom+Box/article36118.htm

## Slide 21
4. Forms of energy
  4.5 Energy density / heat content

## Slide 22
Relative energy densities
Energy Systems & Sustainability, 2/e, Chapter 4; http://xkcd.com/1162

## Slide 23
Chemical energy density
Storing energy is ‘expensive’ in terms of quantities of chemical or potential energy needed.
Energy Systems & Sustainability, 2/e, Chapter 4
fuel (=chemical energy) | MJ/kg
hydrogen gas | 130
natural gas | 55
gasoline | 45
oil | 42
coal | 28
ethanol | 27
wood | 15
pounds to store 10 gas gallon equivalents
22
52
68
105
191
6,578
11,440
762,667
lead-acid batteries
water at 80c
pumped storage (h = 370 m)

## Slide 24
HHV vs. LHV heat values?
There are two ‘flavors’ of heat values (or energy densities) for combusted fuels.
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
Fuel | HHV (MJ/kg) | LHV (MJ/kg)
hydrogen | 141.80 | 119.96
methane | 55.50 | 50.00
propane | 50.35 | 46.35
diesel | 44.80 | 43.40
wood | 21.20 | 17.0
HHV (high heat values) used when the steam is condensed after use; condensing steam to water releases additional energy.
Aka HCV or GCV
LHV (low heat values) used when the steam is not condensed after use.
Aka LCV or NCV

## Slide 25
Example: storing energy as H2 (1)
Problem: How much hydrogen gas would be required to store the energy equivalent of 10 gallons of gasoline, and what pressure would be required to store the gas a standard temperature?
Energy Systems & Sustainability, 2/e, Chapter 4
10 gallons gasoline 3.7854 L 1 m3 719.7 kg = 27.2 kg
1 gallon 1000 L m3
Gasoline has a density of 719.7 kg/m3.
27.2 kg 45 MJ = 1224 MJ in 10 gallon of gasoline
1 kg
1224 MJ 1 kg 1 E3 g 1 L 1 m3 = 104.8 m3 H2 gas at STP
130 MJ 1 kg 0.08988 g 1000 L
Ideal gas law: PV = nRT  P = mRT/V
P = mRT = (9.42 kg)(4124.18 Nm/kg-°K)(298 °K) = 1.10 E5 Pa = 16 psi
V 104.8 m3
Problem: this is a massive volume!!!

## Slide 26
Example: storing energy as H2 (2)
Commercial ‘low pressure’ hydrogen storage tanks are rated at 440 psi. How much would this higher pressure storage decrease to volume required to store the hydrogen gas?
Energy Systems & Sustainability, 2/e, Chapter 4
Ideal gas law: PV = mRT  V = mRT/P
V = mRT = (9.42 kg)(4124.18 Nm/kg-°K)(298 °K) = 3.8 m3
P 3.034 E6 Pa (=N/m2)
Pa = N/m2
m3
kg
4124.18 N-m/kg-°K
°K
1 psi = 6894.76 Pa  440 psi 6894.76 Pa = 3.034 E6 Pa
1 psi
What if a commercial compressed gas tank (2000 psi) were used?
2000 psi = 1.38 E8 Pa
V = mRT = (9.42 kg)(4124.18 Nm/kg-°K)(298 °K) = 8.4 E-2 m3
P 1.38 E8 Pa (=N/m2)

## Slide 27
4. Forms of energy
  4.7 Electromagnetic radiation
  & electricity

## Slide 28
Electromagnetic radiation
Electromagnetic radiation: ‘Classically, electromagnetic radiation consists of electromagnetic waves, which are synchronized oscillations of electric and magnetic fields that propagate at the speed of light through a vacuum ‘
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
1820 Oersted: electric current can deflect the needle of a compass
1820 Ampere: two parallel wires carrying electric current generate magnetic force
1821 Faraday: a wire carrying current will spontaneously rotate around a magnet
1832 Faraday: moving a bar magnet in a coil of wire causes current to flow in a coil
1864 Maxwell: EM waves are simply oscillating electric & magnetic fields that can travel through empty space at nearly the speed of light
      The source of all EM radiation are oscillating electric charges
      EM radiation is 'pure energy’
1900 Plank / 1905 Einstein: EM radiation is quantized

## Slide 29
Spectrum of electromagnetic radiation
Energy Systems & Sustainability, 2/e, Chapter 4; wikipedia
EM radiation includes a broad spectrum of types of radiation defined by their wavelengths.
Visible light is a small part of the EM spectrum

## Slide 30
Solar energy (insolation)
The solar energy that reaches the earth represents a small part of the EM spectrum & includes:
UV light (mainly A & B)
visible
Short-wave infrared
Long-wave infrared
Energy Systems & Sustainability, 2/e, Chapter 4; XXXX
Maximum insolation power:
= 1000 W/m2
Power of sunlight hitting the earth’s surface.
Solar energy is responsible for:
Photons (PV power)
Molecular vibration (heat)
Photosynthesis (biomass)

## Slide 31
Electricity: movement of electrons
Electricity: a flow of electrons
Energy Systems & Sustainability, 2/e, Chapter 4
Metals conduct electricity. How?
Electrons flow in response to pressure (an electrical field) or as the result of a chemical reaction; a reduction-oxidation reaction.
Ultimately, it’s all about the law of electrostatic attraction.
Free electrons will move (flow) in response to a stronger attractive force.
Metal atoms are easily oxidized: lose electrons & become + cations.
Free electrons mill about, attracted to the cations.

## Slide 32
Electric power?
Energy Systems & Sustainability, 2/e, Chapter 4; xxx
Electricity power: rate of transfer of electric energy into a circuit
High Pressure, Low Flow Rate
Low Pressure, High Flow Rate
P = (V) (I)
power
(W)
voltage (V)
current
(Amp)
V = (I)(R)
voltage (V)
current (Amp)
resistance
(Ω)
V, I
V, I
Voltage (~pressure): the difference in electrical potential between terminal (source & destination); a measure of energy (V = volt)
Resistance (~friction): material’s ability to slow electron flow (Ω; V/A)
Current (~ flow rate): the flow of electrons (I; units = amperes, A)

## Slide 33
Electric power example
Energy Systems & Sustainability, 2/e, Chapter 4
Problem: A bulb is labelled 1.5 V, 0.3 A. What is the bulb’s resistance and power when it is connected to a 1.5 V battery?
R = V/I = 1.5 V = 5.0 Ω
0.3 A
P = (V) (I) = (1.5 V) (0.3 V) = 0.45 W

## Slide 34
4. Forms of energy
  4.8 Nuclear energy

## Slide 35
Nuclear energy: background
Energy Systems & Sustainability, 2/e, Chapter 4
Quick review of basic atomic structure & chemistry:
Matter is made of atoms.
Atoms have nuclei made of positively charged protons and neutral neutrons & surrounded by negatively charged electrons.
Atomic number is the number of protons in the atoms of an element.
Atomic mass is the mass of the atoms of an element.
Isotopes are atoms with a variant number of neutrons & thus mass that is slightly higher or lower than the average mass of atoms of that element.
What hold nuclei together? After all, since protons are positively charged, the should repel one another when packed together into the nucleus!
  Strong nuclear force (the 3rd force)
  The nuclei of most atoms are stable & do not change.

## Slide 36
Periodic table
Energy Systems & Sustainability, 2/e, Chapter 4; webelements.com
Most actinide isotopes with odd numbers of neutrons are fissile.
Nuclear fuels: U-233, U-235, Pu-239, Pu-241

## Slide 37
Nuclear fission
Energy Systems & Sustainability, 2/e, Chapter 4
Nuclear fission: nuclei of certain elements split into two nearly equal parts
Since the energy of the two fission products is lower than the energy of the atom which is split, energy is released.
1 E8 times as much energy is released from fission of one atom of uranium-235 as from the burning of one carbon atom.
And because the intranuclear forces are very strong, lots of energy is released.

## Slide 38
Special theory of relativity
Energy Systems & Sustainability, 2/e, Chapter 4
Einstein’s special theory of relativity sought to resolve conflicts between Newton’s laws of motion and Maxwell’s laws of electromagnetism.
E = (m)(c2)
energy (J)
mass (kg)
speed of light
(3 E8 m/s2)
The special theory has two big tenets:
1. Mass is not a fixed quantity: the mass of objects in motion is larger
than the mass of objects at rest.
  The increased mass is equal to the object’s kinetic energy.
2. Therefore, mass and energy are the equivalent and mutable.

## Slide 39
Mass is energy is power?
Energy Systems & Sustainability, 2/e, Chapter 4
https://www.brightstorm.com/science/physics/nuclear-physics/mass-energy-equivalence/
So, if mass and energy are equivalent then just convert to harvest energy!
Problem: releasing (converting) nuclear energy is very hard to do because the nuclear force is so darned strong.
Hypothetically, a small, 20 g, marble contains as much energy as a 500-kiloton hydrogen bomb.
So how can we accomplish conversion?
Matter/anti-matter annihilation? Not enough anti-matter …
Nuclear fission?
  Result in a 100,000 greater loss of mass than chemical reactions, thus produce more energy!
Chemical reactions like combustion? Very little mass lost

## Slide 40
Nuclear energy
Energy Systems & Sustainability, 2/e, Chapter 4; www.euronuclear.org
Nuclear energy: is the energy that holds protons and neutrons together in the nucleus
Much greater than the usual chemical energy.
Released during fission or fusion.
The amount of energy released is related to changes in the total mass of the system, per Einstein’s equation:
Eexo = (Δm)(c2)
Problem: When 1 metric tonne of uranium-235 undergoes fission, its mass is decreased by 6.6 g. How much energy is this loss of mass produce?
Eexo = (0.0066 kg)(3 E8 m/s2)2 = 5.94 E14 J = 600 TJ
Mass lost = energy released

## Slide 41
Fusion vs. fission
https://nuclear.duke-energy.com/2013/01/30/fission-vs-fusion-whats-the-difference
Nuclear fusion: the process of fusing two atoms to create a new atom
Enormous amounts of energy is needed to make fusion happen, but more energy is released: net energy yield.
Fusion is safer because no radioactive products are produced.
Not yet practical or applied.
Radioactive U
Radioactive K
Radioactive Ba
H
H
He

## Slide 42
4. Forms of energy
  4.8 Power

## Slide 43
Power
Energy Systems & Sustainability, 2/e, Chapter 4
Power: is the rate of energy flow (energy / time)
Unit = watt (W) = 1 Joule/second = kg-m2/s3
In many cases, power is created when mass flows:
  wind is flow of air;
  hydro is flow of water; &
  combustion depends on the flow rate of fuel to an engine.
When the flow of mass is involved in producing power, the flow rate of mass (Qmass) can be substituted for mass in energy equations, converting energy equations into power equations.
Qmass = mass flow rate (kg/s)
Example:
Kinetic energy (KE) = ½(m)(v2) = kg-m2 = J
s2
Power of KE (PKE) = ½(Qmass)(v2) = kg-m2 = J/s = W
s3

## Slide 44
Power equations
Energy Systems & Sustainability, 2/e, Chapter 4
Kinetic power
Potential power
Chemical power
Electrical power
PKE = (1/2)(Qmass)(v2) = W
PPE = (Qmass)(g)(h) = W
Pfuel = (Qmass)(H) = W
Pelectrical = (V)(I) = W
Qmass flow rate kg/s, gallons/s, etc.
v velocity m/s
g gravitational acceleration m/s2
H heat content J/kg
V voltage V
I current A

## Slide 45
4. Forms of energy
  4.8 Summary of forms of power

## Slide 46
Summary: forms of energy
Energy Systems & Sustainability, 2/e, Chapter 4
Kinetic energy: motion
KE = (1/2)(m)(v2)
Potential energy: gravity (positional energy)
PE = (m)(g)(h)
Thermal energy: heat (Δ temperature)
Q = (m)(c)(ΔT)
Chemical energy: fuels & batteries
Q = (H)(fuel quantity)
Electrical energy: flow of electrons
P = (V)(I)
Nuclear energy: change in mass
E = (m)(c2)