## Slide 1
SSC 2030: Energy Systems & Sustainability
7A. Conventional baseload RE: hydropower
7.1: Hydropower history and global use
7.2: Hydropower technology
7.3: Large and medium dams and barrages
7.4: Small-scale hydropower
7.5: Hydropower without dams
7.6: Tidal power
7.7: Ocean and wave power without barrages
7.8: What about evaporation engines?

## Slide 2
7. Conventional baseload RE
  7.1: Hydropower history and global use

## Slide 3
What is hydropower?
Hydropower is a form of renewable energy that converts the kinetic energy of moving water to mechanical energy and then electricity.
Dams and pumped storage hydropower create elevated reservoirs that store energy as positional potential energy.
  When water is released, potential energy becomes kinetic.
In-flow hydropower (and tidal power) uses the kinetic energy of flowing water to produce electricity without use of dams or reservoirs.
Wave power uses the kinetic energy of constant (not tidal) wave action to produce electricity without use of dams or reservoirs.

## Slide 4
Hydropower: ancient and modern
2,000 B.C.
Greeks use water wheels to grind grains
1929
First major pumped storage on the Hoostatonic River in CT
1933
US establishes the Tennessee Valley Authority
1936
Hoover Dam built
1940
New Deal ramps up hydropower
1975
US begins environmental regulation and protection
2005
US Energy Policy Act provides loan guarantees
2013
US federal boost to small hydro
1960s-1970s
Large dams built across the globe with IMF incentives
2012
Three Gorges Dam becomes operational
(longest)
https://www.energy.gov/eere/water/history-hydropower

## Slide 5
Ancient hydropower
Renewable Energy, 2/e, Chapter 5
http://www.top-alternative-energy-sources.com/water-wheel-design.html
Fig 5.9
The Norse and Greeks used vertical axis mills to grind grains.
Traditional horizontal axis water wheels developed later.

## Slide 6
Hydropower today? Electricity!
https://ensia.com/features/hydropower/
https://www.eia.gov/energyexplained/index.php?page=hydropower_home
Today, the major function of hydropower is the production of renewable electricity.
Hydroelectric power is baseload power as water flows (nearly) constantly.
If dams and pumped storage are used, the amount of power produced can be adjusted very quickly.

## Slide 7
Significant global electricity producer
https://ensia.com/features/hydropower/
https://www.eia.gov/energyexplained/index.php?page=hydropower_home
https://www.hydropower.org/sites/default/files/publications-docs/
2018_hydropower_status_report_infographics_spread_0.pdf
Globally hydropower is:
  16.4% of all electricity
  62% of all renewable electricity
US: 7.5% of all electricity production 44% of utility-scale electric generation

## Slide 8
Largest global hydropower producers
https://www.bp.com/content/dam/bp/en/corporate/pdf/energy-economics/statistical-review/
bp-stats-review-2018-full-report.pdf
China leads by a length.
Country | Consumption (mTOE) | 2017*
China | 261.5 | 28.5%
Canada | 89.8 | 9.8
Brazil | 83.6 | 9.1%
U.S. | 67.1 | 7.3%
Russia | 41.5 | 4.5%
Norway | 32.0 | 3.5%
India | 30.7 | 3.3%
Japan | 17.9 | 2.0%
*Share of global consumption
1 million TOE = 11.63 GWh

## Slide 9
Largest global hydropower producers
https://www.bp.com/content/dam/bp/en/corporate/pdf/energy-economics/statistical-review/
https://www.hydropower.org/sites/default/files/publications-docs/
2018_hydropower_status_report_infographics_spread_0.pdf

## Slide 10
Global hydropower potential?
In 2000, global output was roughly 18% of technical potential.
Region | technical potential*
N. America | 1668
S. America | 2792
Europe | 2706
Oceania | 232
Asia | 5093
Africa | 1888
Global | 14379
*TWh/year
Renewable Energy, 2/e, Chapter 5
This doesn’t consider:
Practical potential;
Economic potential; or
Sustainable potential.

## Slide 11
Hydro plants can be massive
In 2016, nine of ten of the world’s largest electric generating plants were hydropower.
https://www.power-eng.com/articles/2016/10/hydroelectric-plants-include-nine-out-of-the-10-biggest-in-the-world.html

## Slide 12
Growing in most countries
https://www.bp.com/content/dam/bp/en/corporate/pdf/energy-economics/statistical-review/
bp-stats-review-2018-full-report.pdf
Region | Consumption (mTOE) | 2006 – 2016* | 2017*
North America | 164.1 | 0.2% | 6.7%
S/Central America | 162.3 | 0.6% | 4.1%
Europe | 130.4 | 1.6% | - 10.5%
CIS (Central Asia) | 56.7 | 0.4% | 0.9%
Middle East | 4.5 | - 0.6% | - 3.3%
Africa | 29.1 | 2.7% | 7.4%
Asia Pacific | 371.6 | 7.4% | 1.1%
Global total | 918.6 | 0.9% | 2.9%
*Growth rate per annum

## Slide 13
Rate of growth
The global rate of hydropower growth has been remarkably consistent.
Renewable Energy, 2/e, Chapter 5
https://en.wikipedia.org/wiki/Hydroelectricity#/media/File:Top_5_Hydropower-Producing_Countries.png
http://www.earth-policy.org/data_highlights/2012/highlights29

## Slide 14
Damming continues
2014
https://www.vox.com/2014/10/28/7083487/the-world-is-building-thousands-of-new-dams-is-that-really-a-good-idea
Aquatic Sciences (DOI: 10.1007/s00027-014-0377-0)

## Slide 15
7. Conventional baseload RE
  7.2: Hydropower technology

## Slide 16
Quick hydropower math
When dams and reservoirs are involved, potential energy is:
potential energy = MgH
Renewable Energy, 2/e, Chapter 5
mass (kg)
gravity, 9.81 m/s2
height (m)
Power:
P = (1000)(n)(Q)(g)(H)
turbine efficiency (%)
flow (m3/s)
kg/m3
J
J
P = (10)(n)(Q)(H)
kW

## Slide 17
Classifying hydropower
Modern hydropower can be classified using a number of criteria.
Renewable Energy, 2/e, Chapter 5
https://www.usbr.gov/lc/hooverdam/
1. Effective head
2. Capacity: rated power output
3. Type of turbine
4. Type of dam, reservoir, etc.,.
220 m
220 m
2.1 GW
turbo
35 b m3
Hoover dam

## Slide 18
Effective head
Head varies with location and type of hydropower
Renewable Energy, 2/e, Chapter 5
https://www.quora.com/What-is-the-difference-between-a-barrage-and-a-dam
1. Low
2. Medium
3. High
220 m
Barrage (low dam) or run of river
Dam and reservoir
High dam or pumped storage
Low head
Bank-to-bank barrier
Water level depends on height of full—eight gates
Low head
Bank-to-bank barrier
Water level depends on height of gates
High head
Bank-to-bank barrier
Water level depends on:
  Volume diverted to turbines
  Overflow gates at top

## Slide 19
Turbines: Francis
Turbines come in a variety of designs, though the large hydropower plants depend on the Francis turbine.
Has blades and vanes like steam turbines and jet engines.
Works with head from 2 – 300 m.
Renewable Energy, 2/e, Chapter 5
220 m

## Slide 20
Turbines: Pelton wheel
Pelton wheel was developed during the California gold rush.
Jets of water (>1) hit cups and spin the wheel.
Jets can be adjusted to change the speed of spin
Works with higher head (>250 m) or with smaller hydro.
Renewable Energy, 2/e, Chapter 5
https://energyeducation.ca/encyclopedia/Pelton_turbine
220 m

## Slide 21
Choosing a turbine
Turbine choice depends on the site’s combination of head & flow rate.
Renewable Energy, 2/e, Chapter 5
http://rivers.bee.oregonstate.edu/book/export/html/35
Fig 5.23
220 m

## Slide 22
7. Conventional baseload RE
  7.3: Large and medium dams
  and barrages

## Slide 23
Dams and barrages
Building dams and barrages increases the potential energy available for hydropower and make the water supply more consistent.
  A barrage is a low dam used to host hydropower turbines or divert water to a hydro plant.
  Barrages are sometimes said to be ‘run of river’.
Renewable Energy, 2/e, Chapter 5
Other advantages?
  Flood control
  Consistent supply of water for irrigation
  Recreation
  No particulates; relatively low carbon
Disadvantages?
  Displaces human populations
  Floods valuable habitat
  Disrupts aquatic ecosystems
  Reservoirs can create and release significant amounts of methane
  Silting up
  Dam failure
  Geopolitical tension…. or worse
1900s: 200 dam failures o/s China killed 10,000
1975 in China: 250,000 dead
Three Gorges Dam:
1.2 million people
13 cities
140 towns
1,350 villages

## Slide 24
Case study: the Galloway hydros
The Galloway hydros is a system of dams, aqueducts and power plants on the River Dee in southwest Scotland.
Established by an Act of Parliament in 1929; completed 1936.
Renewable Energy, 2/e, Chapter 5
Main long-term seasonal storage of 80 m m3 = 40 m kWh.
Tunnel allows reverse filling during low demand.
Artificial reservoir storing 24 MW for Glenlee.
Series of power plants along the river that allow rapid response to demand:
Kendon
Carsfad
Earlston
Tongland
3
1
2

## Slide 25
Galloway power stations
Vital statistics:
Renewable Energy, 2/e, Chapter 5
Station | head (m) | flow (m3/s) | capacity (kW) | turbine (MW) | turbine type | rotation (rpm)
Drumjohn | 11 | 16 | 2,000 | 2 | prop | 300
Kendoon | 46 | 55 | 24,000 | 12 | Francis | 250
Carsfad | 20 | 73 | 12,000 | 6 | prop | 214
Earlstoun | 20 | 71 | 14,000 | 7 | prop | 214
Glenlee | 116 | 26 | 24,000 | 12 | Francis | 429
Tongland | 32 | 127 | 33,000 | 11 | Francis | 214
Total |  |  | 109,000 | 50 |  | 

## Slide 26
Galloway economics
The Galloway hydro system has been operating for over 70 years.
Renewable Energy, 2/e, Chapter 5
Designed to supply power during peak loads, rather than 24/7.
£60,000 subsidy (~ $1 million) for the first three years.
Property taxed at lower rates than coal-fired power plants paid because the environmental side effects were lower.
Today, only the Glenlee power plant is manned.
Demand and performance have exceeded expectations, except during a few years of drought.
Built at an initial cost of £29/kW, very inexpensive even then.
Generally, capital costs are very high: $2,000-4,000/kW
No fuel costs
85– 95% is engineering, permitting, site work
10% for turbines, generator and control system
Economy of scale is significant.

## Slide 27
Popular today, but…
…when they were constructed, the locals weren’t pleased.
A raider comes today who kills The glories of our glens and hills With unheroic acts and bills and "Private Legislation" The Company promoters pen Will Dam the Deugh and dam the Ken and Dam the Dee - oh Dam the men Who Plan such desecration!
- W.G.M. Dobie

## Slide 28
Galloway environmental concerns
Mainly the salmon. Scotland is famous for its salmon fishery and the dams on the River Dee were between the river’s mouth and its salmon spawning pools. There was concern that dams would block:
  Adult salmon swimming upriver to spawn; and
  Young smelts making their way to the Atlantic.
Renewable Energy, 2/e, Chapter 5
Fish ladders, a series of stepped and rising pools, were installed at 4 dams. Space forced one ladder into a spiral within a tower.
Biologists study the ladders and fish numbers.
Not satisfied.

## Slide 29
Environmental downsides of dams
https://www.hydroreform.org/abouthydro/impacts-on-rivers
Hydropower is a low-carbon technology, however when dams are involved, environmental effects can be very significant.
Extinction, and near-extinction, of species
Loss, or lowering, of biodiversity
Flooding of existing ecosystems
Creation of drought-like conditions below the dam
Changes to fisheries
Economic change and relocation of communities
Altered water quality
Generation and release of methane from reservoirs

## Slide 30
Environmental effects: change in POV
‘The environmental impacts of a hydroelectric project must be thoroughly analyzed since, after it is completed, they are essentially irreversible.’
- Dorf, 1978
Renewable Energy, 2/e, Chapter 5
‘The ecological damage per unit of energy produced is probably greater for hydroelectricity than for any other energy source.’
- Committee on Nuclear and Alternative Energy Systems,1979
‘…carefully planned hydropower development can, and does, make a great contribution to improving electrical system reliability and stability throughout the world. [It] will play an important role in the development of living standards in the developing world, [and] make a substantial contribution to the avoidance of greenhouse gas emissions and the related climate change issues.’
- WEC,2003

## Slide 31
Flooding and silting = methane
When dams create reservoirs, the submerged plant materials decompose. Anaerobic decomposition produces methane that is released from the reservoir.
Regular flooding or silting adds biological ‘fuel’.
Renewable Energy, 2/e, Chapter 5
https://www.scidev.net/global/energy/news/dams-raise-global-warming-gas.html
2011 study at Washington State University:
  Dams emit ~ 1 billion tons of GHG.
  Or about 1.3% of global emissions.
  25% more than previously thought.
  Over a 100-year period, dams emit more methane than:
    rice farming and biomass burning; or
    lakes and wetlands.
  Algae growth increases methane formation.
  Worse in warmer climates than in cooler climates.
Some dams release more GHG than fossil fuel-fired power plants.

## Slide 32
Mitigating damage from dams
https://www.hydroreform.org/abouthydro/impacts-on-rivers
The environmental impacts of existing dams can be minimized by changes in operation that may reduce power output, but increase sustainability.
Time water releases to mimic natural flows, temperatures and oxygen levels
  This also stabilizes water levels
Provide safe passage for fish
Upgrade turbines to avoid loss of power production that might occur with operational changes
Restore or optimize local habitat for fish and wildlife
These operational changes can be thought of as a burden similar to that of installing sophisticated scrubbers at power plants.
These operational changes can be thought of as a burden similar to that of installing sophisticated scrubbers at power plants.
FERC study of 240 dam upgrades since 1986 showed that the loss of energy production was only 1.6%.

## Slide 33
Mitigation case studies
https://www.hydroreform.org/abouthydro/impacts-on-rivers
In northern Michigan, Consumers Power worked with government agencies and citizen groups to restore more natural flows to a local river. Fish populations bounced back quickly, bringing more than $590,000 a year from fisheries into neighboring communities.
These operational changes can be thought of as a burden similar to that of installing sophisticated scrubbers at power plants.
In rural western Massachusetts and southern Vermont, recreational flows at a hydropower dam on the Deerfield River allowed new, multi-million dollar rafting and fishing industries to flourish, creating new jobs while maintaining profitable energy production.
A 2004 agreement on Oregon’s Pelton-Round Butte Project – now jointly owned by Portland General Electric and the Confederated Tribes of the Warm Springs – will result in salmon and steelhead returning to the upper reaches of the Deschutes River for the first time in decades while continuing to supply more than 366 MW of power to customers.

## Slide 34
Fish ladders aren’t effective
A 2012 study of fish ladders at dams on Atlantic rivers in the Northeast showed that fish ladders weren’t effective.
https://e360.yale.edu/features/blocked_migration_fish_ladders_on_us_dams_are_not_effective
https://onlinelibrary.wiley.com/doi/full/10.1111/conl.12000
Only 3% of shad, a migratory fish, made it past all of the dams on the Susquehana, Connecticut and Merrimack rivers and reached their spawning grounds.
Other anadromous fish species had slightly better rates of success.
“While investigating fish passage on the Merrimack River in New Hampshire, our project’s lead researcher, Jed Brown of the U.S. Fish & Wildlife Service, was struck by the long-term lack of recovery of the targeted fish populations — at some fish restoration meetings there were more people in the room than salmon in the river.”
“In the end, the challenges are daunting, and for a simple reason: It’s asking a lot for a finned creature to take an elevator or to climb a ladder.
Biologists, particularly in Europe, are trying the build better passages around dams.

## Slide 35
Geopolitical issues
Gabcikovo-Nagymaros hydroelectric system was a planned series of dams on the Danube river jointly agreed to in 1977 by Czechoslovakia and Hungary, whose border the river forms.
Renewable Energy, 2/e, Chapter 5
The land in this region is rich agricultural land with fragile wetland ecosystems.
After a decade, the Hungarians cancelled the project.
Czechoslovakia split into the Czech Republic and Slovakia.
Slovakia rejected Hungary’s decision, diverted the Danube and kept building.
Environmental impacts were huge despite workarounds.
1993 case went to International Court of Justice.
1995: Slovakia reduced water diversion.
1997: Court ruled both nations were at fault and must negotiate, but the case has never been resolved.

## Slide 36
Geopolitical issues
Renewable Energy, 2/e, Chapter 5
Fig 5.25
Slovakia
Hungary
Austria

## Slide 37
7. Conventional baseload RE
  7.4: Small-scale hydropower

## Slide 38
Small-scale hydro
The scale of small-scale hydro varies:
5 MW in the UK
10 MW in Switzerland
30 MW in the US
Renewable Energy, 2/e, Chapter 5
Smaller? mini-, micro-, pico-
Technology?
Often run-of-river or low-head technology.
Why a smaller scale?
  Large-scale options built or too environmentally costly.
  Local power is needed in rural or undeveloped regions.
Global use?
In 1999, estimates of 18 GW of <10 MW hydro plants in 38 countries.
China?
2002: 26 GW from plants <25 MW
38,700 plants from 100 – 500 kW
4,300 plants 0.5 – 25 MW
Power for 300 million people

## Slide 39
Small-scale hydro: potential
The greatest potential for small-scale hydro is providing ‘water-to-wire’ electricity for remote mountainous regions without electric options.
Renewable Energy, 2/e, Chapter 5
https://blog.nationalgeographic.org/2012/07/20/nepals-mountain-villages-tap-the-power-of-eternal-snows-with-micro-hydro/
Nepal: one person can carry a Peltric turbo-generator set that will produce 1 kW with a head of 50-70 m.
This type of hydropower does not use dams or barrages, and minimizes environmental impact.
A small volume of water is diverted from a stream and then returned after it spins the turbine.

## Slide 40
Power up?
https://www.energy.gov/eere/articles/5-promising-water-power-technologies
Could we add power to existing, non-hydro dams in the US?
Total potential hydropower capacity: 160,000 MW
49% federal
12 GW total

## Slide 41
Elan Valley: small-hydro case study
The Elan Valley reservoirs (Wales) are five lakes created by dams built starting around 1900 in order to supply the city of Birmingham with clean water.
1 E8 m3 of water capacity
Renewable Energy, 2/e, Chapter 5
https://www.elanvalley.org.uk/discover/reservoirs-dams/hydropower

## Slide 42
Adding hydropower
While one of the dams, at Caban Coch, always produced hydropower, it was upgraded, and turbines were added at the other four dams in 1997.
Renewable Energy, 2/e, Chapter 5
https://www.elanvalley.org.uk/discover/reservoirs-dams/hydropower
plants | head (m) | Capacity (kW) | turbine
Craig Goch | 36.5 | 480 | Francis
Pen-y-Garreg | 37.5 | 810 | Francis
Caban Coch | 37.0 | 950 | 2 x Francis
Foel Tower | 13.5 | 300 | Kaplan
Claerwen | 56.0 | 1680 | Francis
total |  | 4.2 MW | 
At Foel Tower, the turbine is inside one of the three 14-m diameter pipes that carries water from the reservoirs to Birmingham.
At Foel Tower, the turbine is inside one of the three 14-m diameter pipes that carries water from the reservoirs to Birmingham.
Because the area is now renowned for its beauty and is a Site of Special Scientific Interest, most of the new buildings were placed underground.

## Slide 43
Boulder, CO: water / electricity supply
Boulder, CO has hydroelectric facilities that also provide water.
Historically: hydro plants  water supply  expanded hydropower
https://bouldercolorado.gov/water/hydroelectricity
At Foel Tower, the turbine is inside one of the three 14-m diameter pipes that carries water from the reservoirs to Birmingham.
8 facilities (5 built in the 1980s)
~ 40 m kWh of electricity (4,741 households; 11% of electricity)
> $ 2 m revenue
20,399 tons of coal avoided
The huge drop from reservoirs to the city required a reduction an pressure, and adding turbines achieved this with power.

## Slide 44
7. Conventional baseload RE
  7.5: Hydropower without dams?

## Slide 45
‘Run of river’?
https://en.wikipedia.org/wiki/Run-of-the-river_hydroelectricity
'Run of river’ is used to describe hydropower that neither uses high dams nor creates significant reservoirs.
But, projects using barrages and creating some impoundments are described using this term.
Less detrimental environmental effects?
‘Softer’ power supply.

## Slide 46
Creating hydropower without dams?
https://en.wikipedia.org/wiki/Run-of-the-river_hydroelectricity
This is a more radical approach that is likely to:
Greatly reduce the environmental and social impacts of hydropower;
But also reduce the scale of hydropower projects and production.
Perhaps this is the approach we should take to new hydropower projects once existing dam sites (damage) are fully powered and exploited?
Most ‘damless’ hydropower projects involve placing some form of turbine in the flow of the river.
Some involve diverting some of the river’s flow for some distance.
Others place turbines in human-created infrastructure.

## Slide 47
In-flow (aka ‘zero head’) turbines
https://www.smart-hydro.de/renewable-energy-systems/hydrokinetic-turbines-river-canal/
Floating or anchoring turbines in the the flow of a river, without creating a dam or diversion, minimizes change to flow of river while creating baseload power.
Smart Turbines is a German company developing in-flow turbines.

## Slide 48
Smart-turbine floating turbine design
https://www.smart-hydro.de/renewable-energy-systems/hydrokinetic-turbines-river-canal/
https://www.youtube.com/watch?v=49DhljMOa7Y

## Slide 49
Smart turbine specifications
https://www.smart-hydro.de/renewable-energy-systems/hydrokinetic-turbines-river-canal/

## Slide 50
Anchored vs. floating
https://www.smart-hydro.de/renewable-energy-systems/hydrokinetic-turbines-river-canal/
This version of the Smart turbine would be anchored on the riverbed and would pose less of a navigational hazard.

## Slide 51
Smart Hydro Power projects
https://www.smart-hydro.de/decentralized-rural-electrification-projects-worldwide/
The sweet spot for this technology is remote, rural electrification, though projects have also been done in developed countries.
https://www.smart-hydro.de/decentralized-rural-electrification-projects-worldwide/

## Slide 52
Turbulent: vortex turbines
https://www.turbulent.be/
Turbulent, a Belgian company has developed a low-velocity, in-low, vortex turbine for:
  15 – 100 kW
  Low flow: > 1.5 m3/s
  Low head: 1.5 – 3 m

## Slide 53
Turbulent: vortex turbines
https://www.turbulent.be/

## Slide 54
Venterra: in-stream turbine ’pod’
A Minneapolis start-up that has developed a low-velocity, in-stream, streambed, modular turbine for:
  50 kW and larger via array (thus scaleable)
  < 2 m depth (direct deployment)
  Self-clearing
  Fish safe
https://www.verterraenergy.com/

## Slide 55
Venterra’s Volturnus
https://www.verterraenergy.com/

## Slide 56
Lucid: in-pipe helical turbines
These helical turbines are designed to both step-down the pressure of municipal water supply pipes and to generate electricity.
  No environmental effects
  Use existing infrastructure
http://lucidenergy.com/how-it-works/
Portland, OR
20-year power purchase agreement
900 MWh / year
Powers 100 homes
Riverside, CA
Powers water plant during the day
Powers streetlights at night

## Slide 57
Lucid: in-pipe helical turbines
Lucid flow requirements, pipe size and power output:
http://lucidenergy.com/how-it-works/

## Slide 58
Micro-hydro at residential scale
HomePower magazine

## Slide 59
7. Conventional baseload RE
  7.6: Tidal power?

## Slide 60
Tides: more complicated
Tides are generally more complicated that dammed hydro sources or run-of-river because:
Head and flow rate vary;
Direction of flow changes;
Salt water is more corrosive; and
Weather is often more significant and disruptive.
Renewable Energy, 2/e, Chapter 6
https://en.wikipedia.org/wiki/Tide
https://www.youtube.com/watch?v=UQb22uvrzxE
But water is 800 times more dense than air and carries more power, and tides are more predictable than wind.
Global average tidal change = 0.6 m

## Slide 61
Example of extreme tidal effects
The River Servern is Britain’s longest river and forms the border between England (south) and Wales (north).
Estuary is tidal.
Funnel shaped
Resonance (constructive addition of waves) causes extremely high tidal ranges of up to 50 feet.
’bore’ or standing wave forms
Renewable Energy, 2/e, Chapter 6
https://en.wikipedia.org/wiki/Severn_Estuary
9 miles
75-100miles

## Slide 62
Tidal barrage
A tidal barrage is a low barrier that captures the potential energy of tidal ranges and allows energy to be harvested by turbines in openings that channel flow.
Energy is generated during both tidal flows: in and out.
Water can be held for the duration of ‘one’ tidal flow.
Renewable Energy, 2/e, Chapter 6
http://www.alternative-energy-tutorials.com/tidal-energy/tidal-barrage.html
Flow rate is lowish, similar to very low-head hydro.
An enormous amount of water flows within 6 hours…
… so many turbines are used to harvest as much energy as possible.

## Slide 63
La Rance, France
500 GWh tidal barrage in the estuary of the La Rance river in Brittany, France.
Construction damaged the estuary ecosystem; some recovery.
Renewable Energy, 2/e, Chapter 6
Google maps
https://www.edf.fr/en/the-edf-group/industrial-provider/renewable-energies/marine-energy/tidal-power
lock
6 gates
6 gates
24-unit power plant
& road crossing
Reversible pump turbines can create pumped hydro storage.
Electricity available 90% of the time.

## Slide 64
Barrage alternatives: tidal fence
A tidal fence across parts of the estuary, interrupted by passages.
  Less power output with less environmental damage.
  Up to 1.3 GW capacity (~ 1 nuclear plant) or ~ 1% of UK power.
Renewable Energy, 2/e, Chapter 6
https://www.theguardian.com/environment/2015/aug/07/revolutionary-tidal-fence-set-to-trap-seas-power
https://www.treehugger.com/renewable-energy/tidal-power-alternative-to-the-severn-barrage-touted.html
6 gates

## Slide 65
Barrage alternatives: tidal reef
The 12-mile tidal reef is lower than a barrage with slower turbines.
  Slightly lower cost than barrage.
  Similar 20,000 GWh capacity
  Holds back some, but not all, of tidal change, so less damage to estuary ecosystems.
  Fish should be able to survive passage through slow turbines.
Renewable Energy, 2/e, Chapter 6
http://news.bbc.co.uk/2/hi/uk_news/wales/south_east/7748431.stm
http://www.i-sis.org.uk/reefReplaceBarrage.php
6 gates

## Slide 66
Barrage alternatives: tidal reef
The tidal reef is a series of semi-floating caissons attached to sea-floor anchors.
Reef rises and falls with the tide.
Maintains a low, but constant, head of 2-m.
Attenuates tidal range without utterly interrupting it.
Less vulnerable to storms because of its low profile?
Renewable Energy, 2/e, Chapter 6
http://www.i-sis.org.uk/reefReplaceBarrage.php
6 gates

## Slide 67
7. Conventional baseload RE
  7.7: Ocean and wave power
  without barrages

## Slide 68
Open Energy’s turbine
The Minas channel of the Bay of Fundy has 50’ tidal range with a speed of ~ 11 mph.
Estimated at 2500 MW potentially extractable power
Renewable Energy, 2/e, Chapter 6
http://www2.philly.com/philly/business/energy/can-this-giant-turbine-turn-the-tide-for-ocean-energy-20170901.html
6 gates
Open Hydro turbine lowered to the ocean floor in a cradle. 190 feet deep.
Open turbine reverses direction with the tide.
2 MW capacity.
Fiberglass blades replaced with stronger material.
The turbine is the generator.
Liquidated by huge new parent company

## Slide 69
Bladed turbines
A number of companies are using bladed tubines on pilings, floating platforms or anchored to the seabed.
Atlantis turbines shown here are 15-20 m in diameter.
Renewable Energy, 2/e, Chapter 6
https://simecatlantis.com/services/turbines/history/
https://www.forbes.com/sites/jamesconca/2017/07/27/tidal-energy-all-renewables-are-not-created-equal/#6e5b69134f4e
6 gates

## Slide 70
RITE project in NYC’s East River
Roosevelt Island Tidal Energy project: Verdant energy installed sea-bed turbines in the East River between Manhattan and ‘mainland’ NY.
Actually the ’East Channel’: a tidal stream.
Six turbines were installed from 2006 – 2009.
Ran for 9,000 hours.
Delivered 70 MWh.
Slow enough to avoid damage to fish.
Renewable Energy, 2/e, Chapter 6
https://www.verdantpower.com/riteproject
https://blog.ansi.org/2016/01/tidal-power-turbines-in-east-river/#gref
6 gates

## Slide 71
Deep Green ocean kite
A Swedish company, Minesto, has just commissioned their Deep Green ocean kite.
Designed for slow tidal or ocean currents.
Motion & speed of the kite amplifies power by a cubic factor.
Renewable Energy, 2/e, Chapter 6
https://minesto.com/our-technology
https://www.power-technology.com/news/minesto-completes-sea-trials-dg500-marine-energy-kite/
6 gates
Next? Testing for power production and power take-off.

## Slide 72
Wave energy
Ocean waves are caused by air currents passing over open water, which are caused by solar energy.
Dense water concentrates solar power.
  Solar power ~ 100 W/m2
  Waves ~ 100 kW/m of crest length
Renewable Energy, 2/e, Chapter 8
6 gates
Wave power does vary with weather conditions: North Atlantic ocean
Condition | Period (s-1) | Amplitude (m) | Power density (kW/m) | Velocity (m/s) | Wavelength (m)
storm | 14 | 14 | 1700 | 23 | 320
average | 9 | 3.5 | 60 | 15 | 150
calm | 5.5 | 0.5 | 1 | 9 | 50
Global potential?
2TW
17,500 TWh annually
Practical? 30 TWh at ~$0.05/kWh
2017: global use 22,000 TWh

## Slide 73
Best wave locations?
Western exposure produces the best potential because of wind direction.
Isolated islands have good potential and little conventional energy.
Renewable Energy, 2/e, Chapter 8
http://www.geni.org/globalenergy/library/renewable-energy-resources/ocean.shtml
6 gates

## Slide 74
Effect of depth and shore
Wave energy causes water particles to move in elliptical paths.
Energy decreases with depth.
Renewable Energy, 2/e, Chapter 8
6 gates
𝝺
𝝺/4
Practically, 95% of wave energy can be harvested between the surface and a depth of ¼ of the average wavelength.
Wave energy decreases closer to shore due to two factors:
Friction with the shallow sea-bed.
(2) When waves break,
energy is lost;
dissipated.

## Slide 75
Closer analysis of UK wave resources
A 2001 analysis looked at technical, practical and economical waver power available to the UK.
Renewable Energy, 2/e, Chapter 8
6 gates
water depth (m) | average (GW) | average (TWh/y) | avg technical (GW) | avg technical (TWh/y) | avg practical (GW) | avg practical (TWh/y)
100 | 80 | 700 | 10 | 87 | 5.7 | 50
40 | 45 | 394 | 10 | 8 | 0.24 | 2.1
20 | 36 | 315 | 7 | 61 |  | 
shore | 30 | 262 | 0.2 | 1.75 | 0.05 | 0.4
Economically: 33 TWh/year
2002 UK electricity demand: 350 TWh

## Slide 76
Types of wave energy devices
Renewable Energy, 2/e, Chapter 8
http://www.emec.org.uk/marine-energy/wave-devices/
6 gates
attenuator
point absorber
oscillating surge converter
pressure differential
rotating mass
Wave power isn’t a new idea and there have been, and are, many different ways to harvest wave energy and convert it to electricity.
We’ll look at a few of the current technologies.

## Slide 77
Attenuator: Pelamis sea snake
The Pelamis sea snake is a floating device that faces into waves and is oscillated by them.
Renewable Energy, 2/e, Chapter 8
http://www.emec.org.uk/about-us/wave-clients/pelamis-wave-power/
6 gates
Joints between segments of the sea snake are flexed by the oscillating motion of the waves passing under them.
Flexion causes hydraulic rams to push high-pressure oil through hydraulic motors, driving electrical generators.
Electricity is transmitted to shore through transmission lines.

## Slide 78
Pelamis performance
Pelamis P1 was the first wave energy device tested at scale that produced power for the national grid (2004– 2009).
  750 kW capacity
Renewable Energy, 2/e, Chapter 8
http://www.emec.org.uk/about-us/wave-clients/pelamis-wave-power/
6 gates
Pelamis P2 was the first wave energy device ordered by a utility company.
  After three years it was placed at a research center.
Pelamis went bankrupt in 2014 due to lack of capital funding.
  IP assets owned by Wave Energy Scotland.

## Slide 79
Point absorber: BOLT lifesaver
The lifesaver is a floating ring tethered to the seafloor by three cables.
A point absorber
Renewable Energy, 2/e, Chapter 8
http://boltseapower.com/
6 gates
As waves life one side of the lifesaver up, cable is pulled off of winch drums, generating power.
As that side of the lifesaver rocks back down, cable winds back onto the winch drums…. Repeat.
Electricity can be used on site or transmitted to shore.
30 kW
56 Tons
$1.6 m

## Slide 80
Point absorber: CETO
CETO is a full submerged buoy that harvests wave energy.
A point absorber
Renewable Energy, 2/e, Chapter 8
https://www.carnegiece.com/wave/what-is-ceto/
6 gates
Protected from storms
Pumps and generator are in the buoy.
Energy cabled to shore
10,000s of hours at sea
steel buoyant actuator
hydualic pump (motion)
tether allows recovery without divers
umbilical & supports
umbilical & supports
240 kW capacity

## Slide 81
Surge conductor: bioWAVE
bioWAVE is mounted on the seafloor and is several stories high.
A ‘pitching point absorber’
Renewable Energy, 2/e, Chapter 8
http://bps.energy/biowave
6 gates
Lays flat in storms.
Hydraulic pumps transfer energy to a generator
Energy cabled to shore
250 kW capacity
Australian trials underway

## Slide 82
Wello Penguin
The Wello Penguin is anchored to the sea floor and captures the rocking motion of the waves at the surface.
A rotating mass converter
Renewable Energy, 2/e, Chapter 8
https://wello.eu/the-penguin/technology/
6 gates
WEC-1 deployed for over 18 months off of the Orkney islands, Scotland.
30-m length x 16-m width
220 tons
600 kW capacity
Supplying power to the national grid.
Low cost (?)
Survived Ophelia with 18-m waves.
WEC-2 now making 15% more power

## Slide 83
Human opinion of wave power
In the UK, and elsewhere, public opinion of wind power is mixed and passions run high.
  How do public opinions of wave power compare?
Renewable Energy, 2/e, Chapter 8
http://ec.europa.eu/environment/integration/research/newsalert/pdf/271na4_en.pdf
6 gates
A study surveyed 352 people in Cornwall near a wave energy study center.
Favor the center?
81.7% for
3.4% against
Economic benefits?
69.6%
More employment?
73.2%
Effect on tourism?
36.1% no neg effect
29.3% positive effect
Effect on surfing?
43.0% no effect
13.4% concerned
Effect on commercial fishing?
12.5% improvement: nurseries
15.2% problematic
GCC?
80.9% beneficial effect
Wildlife?
49.3% concerned
  Most though short-term effect
Negative visual impacts?
30.0%

## Slide 84
Environmental effects of wave power
Wave energy is thought to be quite environmentally benign.
  On-shore facilities will have greater effects than offshore.
Renewable Energy, 2/e, Chapter 8
https://nnmrec.oregonstate.edu/education/effects-environment
6 gates
Near-shore
Changes in water mixing may affect food delivery, reproduction, dispersal of larvae and spores.
Unlikely that movement of sand would be significantly affected.
Estuaries are particularly sensitive.
Offshore: hard surfaces on the bottom and cables will likely be colonized by as faux reefs.
Could introduce a rich new (but native) ecosystem.
Or could introduce non-native species.
Migratory species & marine mammals: effects as yet uncertain
Potential entanglement in cables
Avoidance of energy areas could decrease available habitat and increase difficulty of migration.
Whether noise affects marine mammals is being studied.
Will electromagnetic fields affect marine life?
Lights could affect migratory birds.

## Slide 85
7. Conventional baseload RE
7.8: What about evaporation engines?

## Slide 86
Evaporation
https://pmm.nasa.gov/education/water-cycle
Evaporation is the phase change of water from a liquid to gaseous physical state.
Part of Earth’s natural water cycle
Occurs at the surface: liquid/gas interface
Requires energy input

## Slide 87
The power of evaporation
https://www.technologyreview.com/s/608949/evaporation-engines-could-produce-more-power-than-coal-with-a-huge-caveat/
If evaporation requires input of energy, how could it produce power?
A team of scientists at Columbia University have found a way to use evaporation to produce mechanical work that could be harnessed to produce electricity.
Plastic film is coated with the spores of B. subtilis.
When placed above evaporating water, the strips absorb water and elongate, changing shape and the distribution of weight.
The shift in weight causes the wheel to rotate.
During rotation, the wet strips dry and change shape, increasing spin.
Repeat

## Slide 88
How much power?
https://www.technologyreview.com/s/608949/evaporation-engines-could-produce-more-power-than-coal-with-a-huge-caveat/
Evaporation occurs 24/7, so could produce baseload power.
  GCC will increase rates of evaporation.
  Using the ‘evaporation engine’ increases rate of evaporation.
Power production?
A 64 cm2 surface of water produces 2 µW of power.
“We could match power demand on an hourly basis about 98 percent of the time in warm and dry places, which means you don’t need an external battery to adjust for intermittency.” - Sahin (researcher)
Scaled up potential?
Efficient scale up: 325 GW in the US
  More than currently produced by coal (2017).
This level of power would require covering every body of water greater than 0.1 km2 (except for the Great Lakes).
Might affect climate and weather.
Some fraction of this use and output is more likely.
Evaporation from industrial and human processes have not yet been included in the power model.